Lecture No. 17

Subject:  Distributed Loading

Objectives of Lecture:

- To explain how a load distributed over the surface area of a body (i.e. distributed loading) may be replaced by a resultant force having its magnitude and location on the body

  - Reduction of a Simple Distributed      Loading

- Distributed loading on the surface of a

body having surface area as: L x a

## Fig. 17.1

p = pressure on the surface of the body

(Force/area, i.e. Force/L x a)

- Load intensity along the length (L) of the body

### Fig.17.2

w = load intensity along the length of the body = p a = Force/L

- Magnitude and location of the resultant force (i.e. FR and x)

#### A = Area of the load

intensity diagram

=  FR

#### C = Centroid of the area

#### defined by the load

intensity diagram

=  x

# Fig. 17.3

- Reduced form of the “distributed loading”

##### Fig. 17.4

Numerical Examples

- Try the solved examples from Book

(Examples 4 –20 to 4 –22, page 182 to 184)

- Unsolved Examples

4-139

Replace the distributed loading by an equivalent resultant force and specify its location on the beam, measured from the pin at A (Fig. 4-139)

Fig. 4-139

4-142

Replace the loading by a single resultant force, and specify the location of the force on the beam measured from point O (Fig. 4-142).

Fig. 4-142

4-153

Replace the loading by an equivalent resultant force and couple moment acting at point B (Fig.4-153)

# Fig. 4-153

4-157

Replace the loading by an equivalent force and couple moment acting at point O (Fig. 4-157).

# Fig. 4-57