Lecture No. 18

Subject:  Equilibrium of a Rigid Body

Objectives of Lecture:

- To develop the equations of equilibrium for a rigid body

- To introduce the concept of the free-body diagram for a rigid body

18-1 Conditions for Rigid-Body Equilibrium

## Fig. 18.1(a)

## Fig. 18.1(b)

Considering the equilibrium of the ith particle:

Fi + fi = 0

Considering the equilibrium of all the i particles:

ΣFi + Σfi = 0

But Σfi = 0, therefore, ΣFi = 0

Letting ΣFi = ΣF, we have

[ΣF = 0]--------------------------------Eq. 1

Considering the moments of the forces acting on the body,  about the arbitrary point, O, we have

ΣMO = Σri × Fi

For equilibrium of body

[ΣMO = 0]------------------------------Eq. 2

This way we have two equations of equilibrium for a rigid body:

[ΣF = 0] and [ΣMO = 0]

  - Free-Body Diagrams

- Relevant Information Required for F.B.D.

  - Support reactions

- Roller support

###### Only one reaction

- Pin or Hinge support

###### Two reactions

- Fixed support

Three reactions

- Other common types of supports

  - External and Internal Forces

Only show the external forces, F, on the FBD because the net effect of the internal forces, f, is found to be zero.

  - Weight and the Center of Gravity

    - Apply the weight, W, of a body at its center of gravity, G.

    - For a uniform body, the G is located on its geometric center or centroid.

  - Idealizations

### Apply suitably the models or idealizations, e.g., particle, rigid body, and concentrated force.

- Procedure for Drawing a F.B.D.

- Draw outlined shape

- Show all forces

- Identify each loading and give dimensions

Numerical Examples

- Try the solved examples from Book

(Examples 5-1 to  5 –5, page 202 to 206)

- Unsolved Examples

5-1

Draw the free-body diagram of the 50 Kg paper roll, which has a center of mass at G and rests on the smooth hauler. Explain the significance of each force, acting on the diagram (Fig. 5-1).

Fig. 5-1

5-2

Draw the free-body diagram of member AB, which is supprted by a roller at A and a pin at B. Explain the significance of each force, acting on the diagram (Fig. 5-2).

Fig. 5-2

5-6

Draw the free-body diagram of the crane boom AB which has a weight of 650 lb and center of gravity at G. The boom is supported by a pin at A and cable BC. The load of 1250 lb is suspended from cable attached at B. Explain the significance of each force, acting on the diagram (Fig. 5-6).

# Fig. 5-6

5-7

Draw the free-body diagram of the “spanner wrench” subjected to the 20 lb force. The support at A can be considered a pin, and surface of contact at B is smooth. Explain the significance of each force, acting on the diagram (Fig. 5-7).

# Fig. 5-7