Lecture No. 28, 29, & 30

Subject:  Frames and Machines

Objectives of Lecture:

- To analyze the forces acting on the members of frames and machines composed of pin-connected members

Frames and Machines

- Frames and machines are two common types of structures which are often composed of pin-connected multi-force members

- Frames are generally stationary and are used to support loads

- Machines contain moving parts and are designed to transmit and alter the effect of forces

Procedure for Analysis

I. Free-Body Diagram

- Draw the FBD of either the

- entire structure, or

- a portion of the structure, or

- each of the members of the structure

The choice should be made so that it leads to the most direct solution of the problem

- Forces common to two members which are in     contact act with equal magnitude but opposite sense on the respective FBD of the members

##### II. Equations of Equilibrium

- Apply the equations of equilibrium (i.e. ΣFx  = 0, ΣFY  = 0, ΣMO = 0) to each of the FBDs considered for the analysis of the structure

- There will be one extra equation of equilibrium for each of the hinge joints in the FBD

(i.e. ΣMabout the hinge joint  = 0)

Numerical Examples

- Try the solved examples from Book

(Examples 6–9 to 6 –21, page 288 to 302)

- Unsolved Examples

| 6-67 Determine the force P needed to hold the 20-lb block in equilibrium. |  |
| --- | --- |

| 6-74 The compound beam is supported by a rocker at B and is fixed to the wall at A. If it is hinged (pinned) together at C, determine the reactions at the supports. |  |
| --- | --- |

| 6-75 Determine the horizontal and vertical components force at pins A and C of the two-member frame. |  |
| --- | --- |

| 6-79 Determine the horizontal and vertical components of force that pins A and C exert on the two member arch. |  |
| --- | --- |

| 6-89 The two-member structure is connected at C by a pin, which is fixed to BDE and passes through the smooth slot in member AC. Determine the horizontal and vertical components of reaction at the supports. |  |
| --- | --- |

| 6-103 Two smooth tubes A and B, each having the same weight, W, are suspended from a common point O by means of equal-length cords. A third tube, C, is placed between A and B. Determine the greatest weight of C without upsetting equilibrium. |  |
| --- | --- |

| 6-109 If each of the three uniform links of the mechanism has a length L and weight W, determine the angle θ for equilibrium. The spring which always remains vertical, is unstretched when θ = 0°. |  |
| --- | --- |
| 6-127 The structure is subjected to the loading shown. Member AD is supported by a cable AB and roller at C and fits through a smooth circular hole at D. Member ED is supported by a roller at D and a pole that fits in a smooth snug circular hole at E. Determine the x, y, z components of reaction at E and the tension in cable AB. |  |