بسم الله الرحمن الرحيم

DEPARTMENT OF CIVIL ENGINEERING

ENGINEERING MECHANICS: STATICS

CE 201-012

## Solution of QUIZ NO. 6 – Sections 02 & 03

Analysis of Structural Trussed in 2D             Wednesday, April 24, ‘02

- Explain the two methods used to analyze trusses.

  - The method of joints: draw a FBD for each joint alone and apply two equations of force equilibrium. The equations used are:  Fx = 0; Fy = 0.

  - The method of sections: draw a FBD of a separate substructure of the truss for a selected section. Then apply one or more of the equations of equilibrium to determine a force in a member. The equations used are:  Fx = 0; Fy = 0; Mp = 0.

2.  Analyze the following truss for support reactions, indicate all zero force members, and force in member CD.

Fy = 0: Ay –200 =0

### Ay = 200 kN (upwards).

MA = 0:  Bx(3) – 200 (2)=0

Bx = + 133.333 kN.

Fy = 0: Bx + AX =0

Ax  = - 133.333 kN (       )

Zero force members are shown with a red line crossing each zero force member.

To compute FCD we may use either the method of joints (using section aa) or the method of sections (using section bb and ME = 0).

In this problem the method of joints is much simpler.

Let us however use the method of sections based on the shown FBD.

ME = 0:

133.333(3) –200(2) – FCD cos 36.9o (3) – FCD sin 36.9o (2) = 0

This gives FCD  =0.

# Text boxes

Bx

t

200 kN

a

Ay

Ax

a

D

C

B

A

2 m

2 m

b

3 m

b

#### E

E

FCD

200kN

133.333

200kN

