بسم الله الرحمن الرحيم

DEPARTMENT OF CIVIL ENGINEERING

ENGINEERING MECHANICS: STATICS

CE 201-012

## Solution of QUIZ NO. 08 – Sections 02 & 03

Static Dry Friction                                    Monday, May 20, ‘02

- The man has a weight of 200 lbs, and is walking on an inclined plank that rests on two surfaces with static friction coefficients  =  = 0.3. Determine how far distance d the man can walk up the plank without causing the plank to slip neglecting the weight and thickness of plank.

Note: When the motion is imminent, the friction forces at A and B are both given by  N.  The solution is based on the following FBD.

# Text boxes

0.3 NB

FBD when motion is imminent.

t

n

d

NA

WG

NB

 NA