بسم الله الرحمن الرحيم

King Fahd University of Petroleum & Minerals

### DEPARTMENT OF CIVIL ENGINEERING

Second Semester 2001-2002 (012)

ENGINEERING MECHANICS:  STATICS

## CE 201

##### Solution of Second Major Exam

#### Date: April 15, 2002		         8:00 p.m.	  	       Time allowed: 1 ¾  hours

Name: ……………………………          Number: …………………      e-mail: ...……..…………

Circle the Section: 02; 03.

Summary of Performance

| Problem | Full Mark | Score |
| --- | --- | --- |
| 1 | 30 |  |
| 2 | 20 |  |
| 3 | 20 |  |
| 4 | 30 |  |
| Total | 100 |  |

# Instructor:  Dr. Saeid A. Alghamdi

Remarks: ………………………………………………………………………………………………………………………………………………………………………………………………………………

Problem 1:

Read the following statements carefully then complete sentences by the appropriate phrases and/or words:

  - The tendency of a force to rotate a body about an axis is called the moment   of the force.

  - The cross product of a position vector r with a force F is a measure of the  tendency  of the force to rotate the body about a  point.

  - The mixed triple product uaa .  ( r x F )  gives the moment component of force F about

axis defined by the unit vector uaa.

  - Two forces acting on a body are called a couple if they are equal but opposite. This system of forces is also called a free moment vector as the moment caused depends only on perpendicular distance between the two forces but does not depend on the points of applications of the two forces.

  - The number of unknown support reactions for a given support depends on the number of linear and/or angular movements the support will prevent. For example a fixed support for 2D problems has only three reactions of which two reactions are forces and one reaction is a moment.

  - A general group of forces, moments and couples can be reduced to an equivalent force couple system  ( that is: a single force vector  and single moment vector)  that can be placed at a particular point on a structure. The magnitudes are obtained from sum of forces and moments, and the point of application of the equivalent system is obtained from the principle of moments.

  - For a set of forces F in two dimensions, the expression F) ]p   = [F ] x* is called the principle of equivalency of moments. This principle is used to determine the value of x* as measured from a selected reference point called p.

  - Determine the equivalent resultant force FR and its location measured from the fixed support at A for the following bar that has load distribution w= 2.5 x3.

FR = ∫ dF = ∫ w(x) dx = [2.5/4] x4   = 160 kN (  ).

x*   = ∫ x dF/ 160. =  3.2 ft [measured from A].

Problem 2:

If the 3D pipe shown in Fig. 2 is fixed at support A, determine all the support reactions using the vector method of equilibrium conditions.

Hint: Equilibrium equations are a) F =0; and b) Mp = MA  + [M(F)]A = 0.

Fig. 2:

Calculation of support reactions A and MA:

F1  = 0:    A + F1 + F2 = 0

A = - (F1 + F2) = -200 j + 150 k.  (N).

MA  = 0:    MAri x Fi  = 0

MA = -2 j x (-150 k) – (2.5 i +3 j – 2 k) x (200 j) = 300 i – 500 k – 400 i

=  -100 i – 500 k.  (N.m)

Problem 3:

Knowing that a truss is composed of two force members, study the truss shown in Fig. 3 then:

- Analyze geometry and determine the value of h.

- Determine all zero force members.

- Determine the force FAB in member AB

- Use the method of joints to determine FBE in member BE.

Fig. 3:

- Geometry analysis:

l = 24 sin ft.

h = [ (3)2 – l2  ]1/2 = 9.15 ft.

based on the value of  and other angles around B

- Zero force member: only member BD.

- Member AB is a two force member [ see the direction of the force FAB]:

D/(l+h) = sin 45 o. Then d = (9.231+9.15) (2)1/2/2 = 12.9973 ft.

(CCW) ME = 0: 300(13 +9.15) + 300 (9.15) + A d = 0

Then reaction A = force FAB  =   - 722.5 lbs (T).

FBD at joint B:

FX = 0: FBE  sin  722.5([2]1/2/2) +300 = 0

Then:

FBE = 297.2 (T).

Problem 4:

The beam ADB shown in Fig. 4 is supported by a pin support at A and a cable DCB running over a smooth pulley.  For the load given:

- Draw the separate FBDs of the pulley and the bar ADB.

- Determine the tension in the cable

- Determine the support reactions at A.

Fig. 4:

FBD of ADB:

tan-1 (6/80 = 36.9o .

See the dimensions on the given problem,

MA = 0:  With CCW directions positive

T(4) + T sin 

Thenlbs  (tensile).

From sum of forces along x- and y- directions:

Ax = 214.0 lbs.

Ay = - 128.43 lbs (down)

Problem (  ) - continued:

# Text boxes

x

dF = w(x) dx

cable

MA

A

h

FAB

r1

r2

F2 = 200 j (N)

F2 = -150 k (N)

Cross product

h

l





A = FAB

d



Ey

Ex

+

B

300 lbs

FBC

FBE

FBA

FC

T

T

FBD of pulley:

T

T

300 lb

Ay

Ax