Structural Mechanics I

CE  203-KFUPM-021

Summary of lectures 16-19: Torsion of Circular Shaft & Power Transmission Shafts

Torsion: is an act of twisting of a structural member about its longitudinal axis (as shown in Fig. 1 below) by a torque T= M@ x-axis.

Angular Deformations: The study of kinematics (geometry) of deformations leads to the relationships between angle of twist x) and shear strain (x).

Fig. 1:

on dA

It is readily verified that rr/remaxThen from Hooke’s law G, it is seen that:

rr/remax.

Non-zero stress and strain: Using the cylindrical coordinate (x, r, a circular section under pure torsion it is experimentally verified that all normal strains x, r and the shear strains xr, rare identically zeros. The only non-zero stress and strain are x, xsee Fig.2 below].

Torsion Formula: The relationship between shear stress and internal torque Tint is obtained from statical equivalency where:

### Since  (r) = dF/ dA; ( dF= (r) dA and this causes a torque

### dT = dF . r = (r) dA . r = r2 /remax dA

( Tint = ∫ dT = 1//remax  ∫ r2 dA = J/ [re max] ( max  = Tint re/ J.

Generally:

 (r)  = Tint r/ J,

where: J is the polar moment of inertia for a circular section = D4/32 where D is the diameter of the bar.

Power Transmission Shafts:  The power created by a machine is designated P. It is the time rate (i.e. derivative w.r.t time) of doing work W. The work done by a torque T is an angular work W = T . [ angular displacement x) ] = T x)  ( P = dW/dt = T 

(Tint = P/units of  is; rev/min; 1 rev = 2radians

Units of power: Horse-power  (HP), or Watts units: N.m/sec= 1 Watt. One HP = 550 lb.ft/sec, and One HP = 746 Watts.

The following examples illustrate calculation of Tint, the torsion effects on shafts including transmission of power by a system of gears.

# Text boxes

on dA

Element with shear stress r) on area dA.

A hollow cross section with radii re, and ri

The shaft

x

Fig. 2:

T= M@ x-axis