بسم الله الرحمن الرحيم

DEPARTMENT OF CIVIL ENGINEERING - KFUPM

STRUCTURAL ANALYSIS - I

CE 305-01-'03

# Assignment No.  8

Subjects:

Slope deflections equations and moment distribution for beams

DUE DATE:  Monday, December 15, ‘03

Note: The flexibility is the deformation (linear or angular) caused by a unit force or moment.

- Use the slope-deflection equations and joint equilibrium equations to analyze the beam problem of P10-1 [page 432]. Also compute all reactions and draw the SFD and BMD.

- Use the method of moment distribution to analyze beam problem P11-1 [page 468].  Continue the process of moment distribution till the joint moments are accurate with a two decimal places of accuracy (i.e.: small negligible unbalanced moments).

- Use the method of moment distribution to analyze the frame problem P11-13 [page 469].  Assume that joints A, D, and E are fixed, and note that the frame is without side-sway. Also draw the SFD and BMD for each beam segment.

Note:

This homework is basically: (a) review of applying equations of static equilibrium to compute support reactions; (b) classifying a structure based on its degree of static determinacy and/or stability; and (c) computing internal forces at a specified cross section of a structural member, and drawing of SFD and BMD for beams and frames.