بسم الله الرحمن الرحيم

DEPARTMENT OF CIVIL ENGINEERING - KFUPM

Structural Analysis I

CE 305 – 07-1

# Quiz -1

Saturday, 29 September, 2007

Name: -----------------------------------  				ID. No.: -------------------------------				Score:

Pledge: This is my own and independent work and to this I sign: .................................................

- List two types of Dead Loads that may act on a structure.

- Determine the load for the following block-wall per unit length on the floor assuming the weight density of a block is 110 lb/ft3.

- List at least three types of live loads that may act on a structure.

- Classify the following structures (Frame; Beam; Truss) as determinate, indeterminate, stable and/or unstable. And if indeterminate specify the degree of indeterminacy (internal and external) as appropriate.

A:  Frame (fixed at left support and pinned 	   B: Beam (with roller supports):

at right support:

C:  Truss (assumed to be pinned at both supports at C and at E):

- Draw the SFD and BMD for the following plane frame if it has two pin-supports at A and D and has one frictionless joint at joint B.

Hint: First prove this frame is statically determinate and determine that the reactions are Ax = -2.75 kips; Ay = -2.333 kips kips; Dx = -1.75; Dy = 2.333 kips.

# Text boxes

y

x