بسم الله الرحمن الرحيم

DEPARTMENT OF CIVIL ENGINEERING

ENGINEERING MECHANICS: STATICS

CE 201-023

## QUIZ NO. 4 [Take-home] 01

Force-couple systems; Distributed forces             Saturday, July 26, 2003

1.   Explain why is a couple considered a free vector.

2.  The bar shown is subjected to a couple-force system. If each one of the 20 kN forces is inclined with 600 to the x-axis, determine the equivalent force-couple system at support point O.

3.  The rigid arm shown is subjected to the force linear distribution shown below. The linear load   starts from x= 1 m and ends at x= 6 m. Determine the equivalent force and its location measured from point p.

# Text boxes

30 kN

t

1 m

20 kN/m

20 kN

# O

y

x

p

6 m

20 kN

x-axis

2 m

3 m