## Slide 1: Other Gate Types
COE 202
Digital Logic Design
Dr. Aiman El-Maleh
College of Computer Sciences and Engineering
King Fahd University of Petroleum and Minerals

## Slide 2: Outline
Gate Classifications: Primitive & Complex gates
Buffer, Tri-State Buffer
Nand Gate
Nor Gate
Two-level implementation using Nand gates
Two-level implementation using Nor gates
XOR gate
XNOR gate
Parity Generation and Checking

## Slide 3: Gate classifications
Gate classifications
  Primitive gate - a gate that can be described using a single primitive operation type (AND or OR) plus optional inversion(s), e.g. NAND
  Complex gate - a gate that requires more than one primitive operation to describe it, e.g. XOR
Complex gates can implement Boolean functions with less area and delay than primitive gates.

## Slide 4: Primitive Gates

## Slide 5: Buffer
A buffer is a gate with the function F = X:
In terms of Boolean logic, a buffer is the same as a direct connection!
So why use it?
A buffer is an electronic amplifier that can be used to:
  Improve circuit voltage levels e.g. of a received signal
  Increase current drive capability (i.e. get a larger fan out)
  Introduce desirable circuit delay
X
F

## Slide 6: Tri-State Outputs
Q. Can the outputs of 2 ICs, or 2 gates, be directly connected?
A. Generally, No!!! This is only possible if special types of gates are used.
Q. Why can’t the outputs of 2 normal gates be directly connected?
A. Because this causes a Short Circuit that results in huge current flow with a subsequent potential for damaging the circuit.

## Slide 7: Tri-State Outputs
This is obvious since one output may be at logic 1 (High voltage), while the other output may be at logic 0 (Low voltage).
Furthermore, the common voltage level of the shorted outputs will most likely fall in the invalid range of voltage levels.
Q. What are the types of IC output pins that can be directly connected?
A. These are pins/gates with special output drivers. The two main types are:
  Open-Collector outputs.
  Outputs with Tri-State capability.

## Slide 8: Gates with Tri-State Outputs
These gates can be in one of 2 possible states:
  1. An enabled state where the output may assume one of two possible values:
    Logic 0 value (low voltage)
    Logic 1 value (high voltage)
  2. A disabled state where the gate output is in the Hi-impedance (Hi-Z) state. In this case, the gate output is disconnected (open circuit) from the wire it is driving.
An enable input (E) is used to control the gate into either the enabled or disabled state.
  The enable input (E) may be either active high or active low.
Any gate or IC output may be provided with tri-state capability.

## Slide 9: Condition for Connecting Outputs of Tri-State Gates
Two or more tri-state outputs may be connected provided that at most one of these outputs is enabled while all others are in the Hi-Z state.
This avoids conflict situations where one gate output is high while another is low.
Example: The circuit performs the function

## Slide 10: Example: Tri-State Buffer
F=C’ A + C B

## Slide 11: NAND Gate [NOT (AND)]
The basic NAND gate has the following symbol,
  AND-Invert (NAND)
NAND represents AND NOT, i. e., an AND function followed by an inverter (NOT). The symbol shown is an AND-Invert. The small circle (“bubble”) represents the invert function.

## Slide 12: NAND Gates (continued)
Applying DeMorgan's Law gives Invert-OR (NAND)
This NAND symbol is called Invert-OR, since inputs are inverted and then ORed together
Note the above symbol is still for a NAND
So a NAND gate can be represented in two different but equivalent forms:  AND-then-Invert form
 Invert-then-OR form

## Slide 13: Observations on the NAND Gate
The NAND is not Associative.
NAND usually does not have an operation symbol defined like the “.” for the AND and the “+” for the OR
This is because NAND is not associative and we have difficulty dealing with non-associative arithmetic!:
≠
≠

## Slide 14: Observations on the NAND Gate
i.e. the n-input NAND function can not be derived from a sequence of 2-input NAND operations
But it can be derived as a sequence 2-input AND operation (which is associative) followed by a single final inversion.
The NAND is a Universal Gate.
Universal gate – is a gate that can be used to implement any Boolean function through implementing the 3 basic logic operations: (AND, OR, and NOT)
The NAND gate is the natural implementation for the simplest and fastest electronic circuits.

## Slide 15: Observations on the NAND Gate

## Slide 16: NOR Gate [NOT (OR)]
The basic NOR gate has the following symbol,
  OR-Invert (NOR)
NOR represents OR NOT, i. e., the OR function followed by a NOT. The symbol shown is an OR-Invert. The small circle (“bubble”) represents the invert function.

## Slide 17: NOR Gate (continued)
Applying DeMorgan's Law gives Invert-AND (NOR)
This NOR symbol is called Invert-AND, since inputs are inverted and then ANDed together.
Note the above symbol is still for a NOR.
So a NOR gate can be represented in two different but equivalent forms: OR-then-Invert & Invert-then-AND.
X
Y
Z
Z
Y
X
)
Z
,
Y
,
X
(
F
×
×
=
OR-Invert
Invert-AND

## Slide 18: Observations on the NOR Gate
The NOR gate is not Associative.
NOR usually does not have an operation symbol defined like the “.” for the AND and the “+” for the OR
This is because NOR is not associative and we have difficulty dealing with non-associative arithmetic!:
≠
≠

## Slide 19: Observations on the NOR Gate
i.e. the n-input NOR function can not be derived from a sequence of 2-input NOR operations.
But it can be derived as a sequence 2-input OR operation (which is associative) followed by a single final inversion.
The NOR gate is a universal gate.
The NOR gate is another natural implementation for the simplest and fastest electronic circuits.

## Slide 20: Observations on the NOR Gate

## Slide 21: Equivalent Gates

## Slide 22: Two-Level Implementation using Nand/Nor
We have seen before that Boolean functions in either SOP or POS forms can be implemented using 2-Level implementations.
For SOP forms AND gates will be in the first level and a single OR gate will be in the second level.
For POS forms OR gates will be in the first level and a single AND gate will be in the second level.
Note that using inverters to complement input variables is not counted as a level.
We will show that SOP forms can be implemented using only NAND gates, while POS forms can be implemented using only NOR gates.

## Slide 23: Two-Level Implementation using Nand Gates
Example 1: Implement the following SOP function
F = XZ + Y’Z + X’YZ
Introducing two successive inverters at the inputs of the OR gate results in the shown equivalent implementation.
Two successive inverters on the same line will not have an overall effect on the logic.

## Slide 24: Two-Level Implementation using Nor
Example 2: Implement the following POS function
F = (X+Z) (Y’+Z) (X’+Y+Z)
Introducing two successive inverters at the inputs of the AND gate results in the shown equivalent implementation.
Two successive inverters on the same line will not have an overall effect on the logic.

## Slide 25: Implementation of Multilevel Circuits using NAND/NOR gates
Start from output toward inputs converting gate by gate
Example: Implement the given circuit using only NAND gates

## Slide 26: Implementation of Multilevel Circuits using NAND/NOR gates
Example: Implement the given circuit using only NAND gates

## Slide 27: Complex Gates

## Slide 28: Exclusive OR (XOR) Gate
The exclusive-OR (XOR), operator uses the symbol ⊕, and it performs the following logic operation:
X ⊕ Y = X Y’ + X’ Y
The graphic symbol and truth table of XOR gate is:
The result is 1 only when either X is equal to 1 or Y is equal to 1, but not when both X and Y are equal to 1.

## Slide 29: Exclusive NOR (XNOR) Gate
The exclusive-NOR (XNOR), operator uses the symbol , and it performs the following logic operation
The graphic symbol and truth table of XNOR (Equivalence) gate is shown:
The result is 1 when either both X and Y are 0’s or when both are 1’s. That is why this gate is often referred to as the Equivalence gate.

## Slide 30: 2-input XOR / XNOR Gates
The XOR function means: X OR Y, but NOT BOTH
XNOR is called the equivalence function, operator ().
From the K-maps:
From eqns above, note that
X
Y
X
Å
Y
0
0
0
0
1
1
1
0
1
1
1
0
X
Y
0
0
1
0
1
0
1
0
0
1
1
1
or X
º
Y
(X
Å
Y)
1 for different
inputs
1 for equal
inputs
0
1
2
3
1
1
1
1
Sum
Parity
Y
X
Y
X
Y
X
+
=
Å
Y
X
Y
X
Y
X
+
=
Å

## Slide 31: XOR Implementations
The simple SOP implementation uses the following structure:
A NAND only implementation:
X
Y
X
Y
Y
X
Y
X
Y
X
+
=
Å
Invert-then-AND
= OR-Invert
OR
AND
AND
as above
X
Y
X
Y
AND
AND
OR
Y
X
Y
X

## Slide 32: Properties of XOR/XNOR Operations
Commutativity
Associativity

## Slide 33: Basic Identities of XOR Operation

## Slide 34: Basic Identities of XOR Operation
Proving the above identity is easier done using graphical equivalence between gates

## Slide 35: Basic Identities of XOR Operation
Redraw the given circuit using only 2-input XNOR gates. Minimize the number of 2-input XNOR gates used.

## Slide 36: Basic Identities of XOR Operation
Reimplement the circuit given below using minimum number of 2-input XOR gates.
Z = [(A  B)  B]’  [(A  C)’  B]= = [(A  B)  B]’  [(A  C)  B]’
= [(A  B)  B]  [(A  C)  B]
= [A]  [(A  C)  B] = B  C

## Slide 37: XOR for >2 Variables: The Odd Function
The XOR function can be extended to 3 or more literals. For more than 2 literals, it is called: Odd function, or modulo 2 sum.
=
+
+
+
Å
Å
Z
Y
X
Z
Y
X
Z
Y
X
Z
Y
X
Z
Y
X
The odd function for
3 inputs and 4 inputs
Distance 2
1s in the K-map correspond to minterms with indices having an odd number of 1s in binary, hence the name. Use to generate even parity bit and to check even parity (output = 1 for parity error)

## Slide 38: XNOR for >2 Variables:The Even Function
The XONR function can be extended to 3 or more literals. For more than 2 literals, it is called: Even function.
The odd function for
3 inputs and 4 inputs
=
+
+
+
Å
Å
Z
Y
X
Z
Y
X
Z
Y
X
Z
Y
X
Z
Y
X
Distance 2
1s in the K-map correspond to minterms with indices having an even number of 1s in binary, hence the name. Use to generate odd parity bit and to check odd parity (output = 1 for parity error)

## Slide 39: Parity Generation and Checking
Exclusive-OR functions are very useful in systems using parity bits for error-detection.
A parity bit is used for the purpose of detecting errors during transmission of binary information.
A parity bit is an extra bit included with a binary message to make the total number of 1’s in this message (including the parity bit) either odd or even.
The message, including the parity bit, is transmitted and then checked at the receiving end for errors.
An error is detected if the checked parity does not correspond with the one transmitted.

## Slide 40: Parity Generation and Checking
The circuit that generates the parity bit at the transmitter side is called a parity generator.
The circuit that checks the parity at the receiver side is called a parity checker.

## Slide 41: Parity Generation and Checking
As an example, consider a 3-bit message to be transmitted together with an even parity bit.
The three bits, X, Y, and Z, constitute the message and are the inputs to the even parity generator circuit whose output is the parity bit P.
The 4 bits (X, Y, Z & P) are transmitted to their destination, where they are applied to a parity-checker circuit to check for possible errors in the transmission.

## Slide 42: Parity Generation and Checking
Since the information was transmitted with even parity, the received four bits must have an even number of 1’s.
The parity checker generates an error signal (C = 1), whenever the received four bits have an odd number of 1’s.