## Slide 1: Arithmetic Functions & Circuits
COE 202
Digital Logic Design
Dr. Aiman El-Maleh
College of Computer Sciences and Engineering
King Fahd University of Petroleum and Minerals

## Slide 2: Outline
Hierarchical Design
Iterative Arithmetic Combinational Circuits
Functional Blocks: Half-Adder, Full Adder
4-bit Ripple-Carry Adder (RCA)
Carry Lookahead Adder (CLA)
Iterative Design Examples
Signed Number Representation
Adder/Subtractor for Signed 2’s Complement
BCD Adder
Binary Multiplier

## Slide 3: Hierarchical Design
Let us consider the design of a 4-bit Equal Comparator
Direct implementation
  8 input variables
  Truth table: 256 rows
  8-variable K-map!!
Go hierarchical: Solve a large problem as a set of smaller problems
  4 X 1-bit comparators
  + 1 Final comparator
Advantages:
  Handle simpler problem, Use fewer symbols, Repeated use
4 bits
4 bits
E = 1
If A = B
A
B

## Slide 4: Hierarchical Design

## Slide 5: Advantages of the Hierarchical Approach to Design
Simpler representation of complex systems:
  5 interconnected blocks in the hierarchical design
  Versus 21 interconnected gates in a flat approach
Shielding of complexity: Details of further complexity stop at the symbol of a predefined block (leaf)
Reusability reduces the design effort required (fewer different functional blocks to be designed):
  (Only 1 MX and 1 ME)
Easy to upgrade design later by using improved predefined blocks
Different teams can work simultaneously and independently on different parts Speed up the design

## Slide 6: Iterative (Repetitive) Arithmetic Combinational Circuits
Practical Arithmetic Functions:
  Operate on binary bit vectors (e.g. a 32-bit adder adds two 32-bit numbers and produces a 32-bit number)
  Same basic subfunction is used in each bit position
Designing for the input vectors directly can be very difficult (huge # of inputs & outputs!) (Huge truth tables/Maps!)
Solution: Design functional block for subfunction (e.g. for a bit) and repeat it (iterate it) to obtain a functional block for the overall operation
Cell = subfunction block
Iterative array = An array of interconnected cells

## Slide 7: Iterative (Repetitive) Arithmetic Combinational Circuits
An iterative array can be in a single dimension (1D) or multiple dimensions (spatially)
Iterative array takes advantage of the regularity to make design feasible
Block Diagram of a 1D Iterative Array

## Slide 8: Functional Blocks: Addition
Binary addition is used frequently
“Addition” Development:
  Half-Adder (HA), a 2-input bit-wise addition functional block
  Full-Adder (FA), a 3-input bit-wise addition functional block
  Ripple Carry Adder, an iterative array to perform binary addition
  Carry-Look-Ahead Adder (CLA), Speeds up performance by generating carries from the input numbers directly to avoid carry ripple delay.
A half adder (HA) is an arithmetic circuit that is used to add two bits. The block diagram of HA is shown. It has two inputs and two outputs.

## Slide 9: Functional Block: Half-Adder
A 2-input (no carry input), 1-bit width binary adder that performs the following computations:
A half adder adds two bits to produce two bits: S & C
The output is expressed as a sum bit , S and a carry bit, C
The half adder can be specified as a truth table for S and C
X
0
0
1
1
+ Y
+ 0
+ 1
+ 0
+ 1
C S
0 0
0 1
0 1
1 0

## Slide 10: Logic Simplification: Half-Adder
The K-map for S, C is:
By inspection:
and
These equations lead to several implementations.
Y
X
0
1
3
2
1
1
S
Y
X
0
1
3
2
1
C
)
Y
X
(
)
Y
X
(
S
Y
X
Y
X
Y
X
S
+
+
=
Å
=
+
=
)
(
C
Y
X
C
)
Y
X
(
=
=

## Slide 11: Five Implementations: Half-Adder
We can derive following sets of equivalent equations for the half-adder:
Y
X
C
)
(
S
)
c
(
Y
X
C
)
Y
X
(
)
Y
X
(
S
)
b
(
Y
X
C
Y
X
Y
X
S
)
a
(
Y
X
C
=
=
=
+
+
=
=
+
=
+
Y
X
C
Y
X
S
)
e
(
)
Y
X
(
C
C
)
Y
X
(
S
)
d
(
=
Å
=
+
=
+
=
Most common implementation
For the half-adder

## Slide 12: Implementations: Half-Adder
The most common half adder implementation is:
A NAND only implementation is:
Y
X
C
Y
X
S
=
Å
=
X
Y
C
S

## Slide 13: Functional Block: Full-Adder
A full adder is similar to a half adder, but includes a carry-in bit from lower stages. Like the half-adder, it computes a sum bit, S and a carry bit, C.
  For a carry-in (Z) of 0, it is the same as the half-adder:
  For a carry- in (Z) of 1:
Z
0
0
0
0
X
0
0
1
1
+ Y
+ 0
+ 1
+ 0
+ 1
C S
0
0
0 1
0 1
1 0
Z
1
1
1
1
X
0
0
1
1
+ Y
+ 0
+ 1
+ 0
+ 1
C S
0 1
1 0
1 0
1
1

## Slide 14: Logic Optimization: Full-Adder
X
Y
Z
C
S
0
0
0
0
0
0
0
1
0
1
0
1
0
0
1
0
1
1
1
0
1
0
0
0
1
1
0
1
1
0
1
1
0
1
0
1
1
1
1
1
X
Y
Z
0
1
3
2
4
5
7
6
1
1
1
1
S
X
Y
Z
0
1
3
2
4
5
7
6
1
1
1
1
C
Full Adder Truth Table
Full Adder K-Maps

## Slide 15: Equations: Full-Adder
The Boolean functions for the sum and carry outputs can be manipulated to simplify the circuit, as shown below:
Thus the full adder can be implemented using two half adders and an OR gate as shown below:

## Slide 16: Implementation: 1-bit Full Adder
The term X·Y is “carry generate” at the bit position (i.e. from X and Y)
The term XY is “carry propagate” (i.e. allow Z to be passed as carry out)
The Carry bit C is 1 if both X and Y are 1 (the sum is 2), or if the sum is 1 and a carry-in (Z) occurs.
. Z
)
Y
X
(
Y
X
C
Å
+
=
Ci+1 = Gi + Pi · Ci
Gi = Ai Bi
Pi = Ai  Bi
Here X, Y, and Z, and C are Ai, Bi, Ci and Ci+1, respectively.

## Slide 17: 4-bit Ripple-Carry Adder (RCA)
A 4-bit Ripple-Carry Adder made from four 1-bit Full Adders:
N-bit Ripple-Carry Adder:

## Slide 18: 4-bit RCA: Carry Propagation & Delay
One problem with the addition of binary numbers is the length of time taken to propagate the ripple carry from the least significant bit to the most significant bit.
Gate-level propagation path for the 4-bit
ripple carry adder (XOR = 3 gate delays)
A3
B3
S3
B2
S2
B1
S1
S0
B0
A2
A1
A0
C4
C3
C2
C1
C0
Critical (longest) delay path
(Worst case scenario)
Why not
to C4?
Why not
from C0?
Longest Total Carry Ripple Delay from inputs to S3 = 3 + 3 + 2(n-1) gate delays
where n is the number of stages (= 4 here)  12 gate delays

## Slide 19: Carry Lookahead Adder (CLA)
Defining the equations for the Full Adder in terms of the Pi and Gi:
In the ripple carry adder:
  Gi, Pi, Ci and Si are obtained locally at each bit cell of the adder (i.e. limited to that bit)
In the carry lookahead adder, in order to reduce the length of the ripple carry chain, Ci is changed to a more global function spanning multiple cells
i
i
i
i
i
i
B
A
G
B
A
P
=
Å
=
i
i
i
1
i
i
i
i
C
P
G
C
C
P
S
+
=
Å
=
+

## Slide 20: Carry Lookahead Development
Ci+1 can be removed from the cells and used to derive a set of carry equations spanning multiple cells.
Beginning at the cell 0 with carry in C0:
C1 = G0 + P0 C0
C2 = G1 + P1 C1 = G1 + P1(G0 + P0 C0)
= G1 + P1G0 + P1P0 C0
C3 = G2 + P2 C2 = G2 + P2(G1 + P1G0 + P1P0 C0)
= G2 + P2G1 + P2P1G0 + P2P1P0 C0
C4 = G3 + P3 C3 = G3 + P3G2 + P3P2G1+ P3P2P1G0 +P3P2P1P0 C0
= G0-3 + P0-3 C0 = GG + GP C0
Carry does not ripple anymore!
All 4 carry outputs can be generated in one go from:
The C0 and the two input numbers A,B
2-Level logic
(Only 2 gate delays)
No Rippling

## Slide 21: Carry Lookahead Development
Partial Full adder (PFA), (excludes carry handling stuff) to allow use of ripple or lookahead
4-bit Ripple-Carry adder

## Slide 22: Carry Lookahead Development

## Slide 23: Carry Lookahead Development
The 4-bit carry look-ahead (CLA) adder consists of 3 levels of logic:
  First level: Generates all the P & G signals. Four sets of P & G logic (each consists of an XOR gate and an AND gate).
  Second level: The Carry Look-Ahead (CLA) logic block which consists of four 2-level implementation logic circuits. It generates the carry signals (C1, C2, C3, and C4).
  Third level: Four XOR gates which generate the sum signals (Si) (Si = Pi ⊕ Ci), (S0, S1, S2, and S3).

## Slide 24: Delay for the 4-bit CLA Adder
A3
B3
C3
C4
G3
P3
S3
Delay from {A3,B3, C3} to S3 (sum from last bit) is
3 gate delays (XOR) + max (delay in P3, Delay in C3)
C3 = G2 + P2 C2 = G2 + P2(G1 + P1G0 + P1P0 C0)
= G2 + P2G1 + P2P1G0 + P2P1P0 C0
P’s need 3 gate delays
+ 1 for the AND (Product)
+ 1 for the OR (Sum)
5 Gates
Critical delay path
= 3 + max (3,5) = 3 + 5 = 8 gate delays
Vs 12 gate delays for the carry ripple adder
More significant improvements for wider adders,
e.g. 16-bit, 32-bit, and 64-bit
Lower delay
Last of the 4-bit adder stages
3
3
5

## Slide 25: Hierarchical 16-Bit Carry Lookahead Adder
Designed with Four 4-bit Carry Lookahead Adders (CLA)
A Second-Level Lookahead Carry Unit is required
Uses Group Generate (GG) and Group Propagate (GP) signals

## Slide 26: Iterative Design Examples: Y=3X
Suppose we want to design an iterative circuit to compute the equation Y=3X
First, we need to determine what information we should pass between cells
In this case, we can think of 3X as X+X+X. Thus, we need to pass carry information
We need to determine what is the maximum carry value that we need to pass between cells
We start with the first cell with carry-in=0 and consider when X=1. Then, the result will be 3*1=3 which is in binary is 11. Thus, the output will be 1 and carry-out=1.

## Slide 27: Iterative Design Examples: Y=3X
We continue the process but now having carry-in=1 and X=1. Thus, the result will be 3*1+1=4, which is in binary is 100. The output will be 0 and carry-out=2 (10).
We continue the process but now having carry-in=2 and X=1. Thus, the result will be 3*1+2=5, which is in binary is 101. The output will be 1 and carry-out=2 (10).
Since carry-in=2 produced carry-out=2, this means that the maximum carry-out we will get is 2.
Thus, we need only 2 bits for representing the information that we need to pass among cells.

## Slide 28: Iterative Design Examples: Y=3X
Thus, the single bit cell interface is as shown:
We next create the truth table.
Xi
Yi
Cin1
Cin0
Cout1
Cout0
Y=3X
Cin1 Cin0 Xi | Cout1 Cout0 Yi
0 0 0 | 0 0 0
0 0 1 | 0 1 1
0 1 0 | 0 0 1
0 1 1 | 1 0 0
1 0 0 | 0 1 0
1 0 1 | 1 0 1
1 1 0 | x x x
1 1 1 | x x x
Note that since we not get
Carry=3, the output in this
Case is don’t care.

## Slide 29: Iterative Design Examples: Y=3X
Yi = Cin0  Xi
Cin0 = Cin1’ Cin0’ Xi + Cin1 Xi’
Cin1 = Cin1 Xi + Cin0 Xi = Xi (Cin1 + Cin0)

## Slide 30: Iterative Design Examples: Y=3X

## Slide 31: Iterative Design Examples: Y=3X
3*5=15=0xF
3*1=3=0x3

## Slide 32: Iterative Design Examples: Y=3X
3*6=18=0x12
3*15=45=0x2D

## Slide 33: Iterative Design Examples: Y=3X+C
For implementing the equation Y=3X+C, where C is a constant, this should follow the same principle as the constant C should be connected to the first cell only.
Thus, we repeat the analysis we did but starting with carry-in connected to the first cell to be C instead of 0.
Thus, for implementing Y=3X+1 or 3X+2, the same circuit design used for Y=3X should be used with just connecting the carry-in to 1 and 2 instead of 0.
However, for Y=3X+3 we need to reimplement the equations as we considered carry-in=3 don’t care.
For Y=3X+4 we need 3 bits to represent carry information. So, the whole truth table has to be redone.

## Slide 34: Iterative Design Examples: Y=3X+C
3*3+1=10=0xA
3*3+2=11=0xB

## Slide 35: Iterative Design Examples: Z=X-Y
To implement the equation Z=X-Y, we need to pass here whether a cell borrows from the next cell or not
Thus, the cell interface is as shown:
Truth Table:
Xi
Zi
Bin
Bout
Z=X-Y
Yi
Bin Xi Yi | Bout Zi
0 0 0 | 0 0
0 0 1 | 1
0 1 0 | 0 1
0 1 1 | 0 0
1 0 0 | 1
1 0 1 | 0
1 1 0 | 0 0
1 1 1 | 1 1

## Slide 36: Iterative Design Examples: Z=X-Y
Zi = Bin  Xi  Yi = (Bin  Xi’)  Yi)’
Bout = Bin Xi’ + Bin Yi + Xi’Yi
= Xi’Yi + Bin Xi’Yi’ + Bin Xi Yi
=Xi’Yi + Bin (Xi’Yi’ + Xi Yi) = =Xi’Yi + Bin (Xi’  Yi)
Note that the obtained
Circuit is similar to the
Full Adder

## Slide 37: Iterative Design Examples: Z=X-Y
4-3=1, Bout=0
5-6=7, Bout=1
5+8-6=7

## Slide 38: Iterative Design Examples: Comparator
We would like to design a circuit to compare two numbers whether (X>Y, X=Y, X<Y)
It is sufficient to pass two bits between cells to pass the results of comparison so far as shown in the table below:
Note that for comparators, we can process bits from least significant to most significant or from most significant to least significant.
Gi | Li | Meaning
0 | 0 | X=Y
0 | 1 | X<y
1 | 0 | X>Y
1 | 1 | Unused

## Slide 39: Iterative Design Examples: Comparator
Processing bits from most significant to least significant results in smaller area.
The cell interface is as follows:
Truth Table:
Xi
Gi+1
Z=X-Y
Yi
Li+1
Gi
Li
Gi+1 Li+1 Xi Yi | Gi Li
0 0 0 0 | 0 0
0 0 0 1 | 0 1
0 0 1 0 | 1 0
0 0 1 1 | 0 0
0 1 0 0 | 0 1
0 1 0 1 | 0 1
0 1 1 0 | 0 1
0 1 1 1 | 0 1
Gi+1 Li+1 Xi Yi | Gi Li
1 0 0 0 | 1 0
1 0 0 1 | 0
1 0 1 0 | 0
1 0 1 1 | 1 0
1 1 0 0 | x x
1 1 0 1 | x x
1 1 1 0 | x x
1 1 1 1 | x x

## Slide 40: Iterative Design Examples: Comparator
Gi = Gi+1 + Li+1’ Xi Yi’
Li = Li+1 + Gi+1’ Xi’ Yi

## Slide 41: Iterative Design Examples: Comparator

## Slide 42: Iterative Design Examples: Comparator

## Slide 43: Signed Number Representation
To represent signed numbers, the most significant bit is used to indicate the sign of the number: 0 (+), 1 (-).
There are three representations for signed numbers:
  Sign-Magnitude Representation
  1’s complement Representation
  2’s complement Representation
Sign-Magnitude Representation
  The most significant bit is the sign bit and the remaining bits represent the value in binary format

## Slide 44: Sign-Magnitude Representation
  Leftmost bit is the sign bit: 0 is positive and 1 is negative
  e.g. +9 is represented as 01001, -9 is represented as 11001
  Range: Using n bits, the range of numbers that can be represented is from -(2n-1 - 1) to +2n-1 - 1
  For example, if n = 8 bits then range is -127 to +127
1
0
1
1
0
1
0
0
1
0
1
1
0
1
0
1
Sign-magnitude
8-bit representation of +45
Sign-magnitude
8-bit representation of -45

## Slide 45: Sign-Magnitude Representation
Advantages: Simple (number representation is straight forward).
Disadvantages:
  Has the problem of double representing the 0 (-0 and +0),
  Harder to implement addition/subtraction
    The sign and magnitude parts have to be processed independently.
    Sign bits of the operands have to be examined to determine the actual operation (addition or subtraction).
    Separate circuits are required to perform the addition and subtraction operations.

## Slide 46: Signed-Magnitude Addition/Subtraction
Eight cases for Sign-Magnitude Addition / Subtraction
Operation | ADD Magnitudes | Subtract Magnitudes | 
 |  | A >= B | A < B
(+A) + (+B) | +(A+B) |  | 
(+A) + (-B) |  | +(A–B) | -(B–A)
(-A) + (+B) |  | -(A–B) | +(B–A)
(-A) + (-B) | -(A+B) |  | 
(+A) – (+B) |  | +(A–B) | -(B–A)
(+A) – (-B) | +(A+B) |  | 
(-A) – (+B) | -(A+B) |  | 
(-A) – (-B) |  | -(A–B) | +(B–A)

## Slide 47: One’s Complement Representation
Positive numbers are represented using normal binary equivalent .
Negative numbers are represented by the 1's complement (complement) of the normal binary representation of the magnitude.
Example:
  +9 is represented as 01001
  -9 is represented as 10110 (obtained by complementing the binary representation of 9).

## Slide 48: Why is it called “one’s complement?”
Complementing a single bit is equivalent to subtracting it from 1.
0’ = 1, and 1 - 0 = 1 1’ = 0, and 1 - 1 = 0
Similarly, complementing each bit of an n-bit number is equivalent to subtracting that number from 2n-1.
For example, we can negate the 5-bit number 01101.
  Here n=5, and 2n-1 = 3110 = 111112.
  Subtracting 01101 from 11111 yields 10010:
1 1 1 1 1
- 0 1 1 0 1
1 0 0 1 0

## Slide 49: One’s Complement Representation
Range: Using n bits, the range of numbers that can be represented is from -(2n-1 - 1) to +2n-1 - 1 .
Advantages:
  Still relatively simple to represent the numbers,
  Simpler Add/Subtract circuit design (subtracting a number from another involves complementing the subtracted and then adding it to the other number). A-B=A+B’
Disadvantages:
  Has the problem of double representing the 0 (-0 and +0),
  It may require two addition operations as if there is a carry out it has to be added to get the correct result
Overflow: occurs when the result is out of range

## Slide 50: One’s Complement Addition
Example 1: Adding 0111 (+7) + 0111 (+7)
  The result is 1110 and the carry out is 0, hence an overflow has occurred (adding two positive numbers resulted in a negative number, -1 in this case).
Example 2: Subtracting 0001 (+1) – 0111 (+7)
  0001 (+1) + 1000 (-7) = 1001 (-6)
  The result is 1001 with no end carry. The result represents -6 (the correct result) and no further addition is required.
Example 3: Subtracting 0111 (+7) - 0001 (+1)
  0111 (+7) + 1110 (-1) = 0101 (+5) with carry out=1
  The result is 0101 with an end carry of 1. This carry has to be added to the previous result and yields 0110 (+6), the correct answer).

## Slide 51: Two’s Complement Representation
Positive numbers are represented using normal binary equivalent.
Negative numbers are represented by the 2's complement of the normal binary representation of the magnitude.
The 2's complement of a binary number equals its 1's complement + 1.
Another easy way to obtain the 2's complement of a binary number:
  start at the LSB, leaving all the 0s unchanged, look for the first occurrence of a 1. Leave this 1 unchanged and complement all the bits after it.

## Slide 52: Computing the 2's Complement
Another way to obtain the 2's complement:
Start at the least significant 1
Leave all the 0s to its right unchanged
Complement all the bits to its left
starting value | 001001002 = +36
step1: Invert the bits (1's complement) | 110110112
step 2: Add 1 to the value from step 1 | + 12
sum = 2's complement representation | 110111002 = -36
Binary Value
= 00100 1 00
2's Complement
= 11011 1 00
least
significant 1
2’s complement of 110111002 (-36) = 001000112 + 1 = 001001002 = +36
The 2’s complement of A is the negative of A

## Slide 53: Two’s Complement Representation
Example:
  +9 is represented as 01001
  To represent -9, first obtain the binary equivalent of +9: 01001. Now leave the LSB 1 unchanged and complement all the remaining bits to get 10111, which represents -9 in 2's complement.
Range:
  Using n bits, the range of numbers that can be represented is from -2n-1 to +2n-1 - 1.
  The -2n-1 is represented by the 1000..000 code, which has no 2's complement, hence the unsymmetrical range. E.g. if 8 bits are used, the range of numbers that can be represented is from -128 to +127.

## Slide 54: Two’s Complement Representation
To find the value of a number represented in two’s complement, check the sign bit
  If the sign bit is 0, the number is positive and find its value using weighted method
  If the sign is 1, the number is negative and you can find value in two ways
    Take the 2’s complement, you will get the corresponding positive value, then add a minus sign to it
    Use the weighted method using a negative weight for the sign bit
Example: Find the value of the 4-bit number 1011
  Take the 2’s complement-> 0101 = +5; thus 1011 represents -5
  Using the weighted method-> -8+2+1=-5

## Slide 55: Two’s Complement Representation
Advantages:
  No double representation of 0 (the 2's complement of 0 is still 0),
  Simplest Add/Subtract circuit design (subtracting a number from another involves 2's complementing the subtracted and then adding it to the other number),
  Add/Subtract operations is done in one-step
  The end result is already represented in 2's complement (only if there is no overflow).
That is why this is the most preferred method for signed-number representations in computers.

## Slide 56: Two’s Complement Representation
Disadvantages:
  The unsymmetrical range, which is not a serious problem,
  It is slightly more complex to obtain the 2's complement (it involves complementing and adding 1). However this can be accomplished very easily during the Add/Subtract operations (by making the first carry in 1 and complementing the subtrahend).
Overflow: occurs if the result is out of range
  Adding two positive numbers and getting a negative number
  Adding two negative numbers and getting a positive number
  If the last two carries are not equal

## Slide 57: Two’s Complement Addition
Example 1: Adding 0111 (+7) + 0111 (+7)
  The result is 1110 (-2), hence an overflow has occurred (adding two positive numbers resulted in a negative number).
Example 2: Subtracting 0001 (+1) - 0111 (+7)
  0001 (+1) - 0111 (+7) = 0001 (+1) + 1001 (-7) = 1010 (-6)
  The result represents -6 in 2's complement (the correct result) and no further operation is required.
Example 3: Subtracting 0111 (+7) – 0001 (+1)
  0111 (+7) – 0001 (+1) = 0111 (+7) + 1111 (-1) = 0110
  The result is 0110 (+6, the correct result). Since the last two carries being 1 no overflow has occurred and no further operations are required.

## Slide 58: Signed Number Representation (n=4)

## Slide 59: Adder/Subtractor for Signed 2’s Complement
One circuit computes A + B or A – B:
Subtraction is done by the addition of the 2's Complement
For S = 0 (add):
B is passed through to the adder unchanged
For S = 1 (subtract):  2’s complement of B is obtained using XORs to form the 1’s comp + 1 applied to C0 of
1st stage 2’s comp. added to A
Subtract/
Add
No correction
Needed

## Slide 60: Carry and Overflow
Carry is important when …
  Adding or subtracting unsigned integers
  Indicates that the unsigned sum is out of range
Overflow is important when …
  Adding or subtracting signed integers
  Indicates that the signed sum is out of range
Overflow occurs when
  Adding two positive numbers and the sum is negative
  Adding two negative numbers and the sum is positive
Simplest way to detect Overflow: V = Cn–1  Cn
  Cn-1 and Cn are the carry-in and carry-out of most-significant bit

## Slide 61: Carry and Overflow Examples
0
1
0
0
0
0
0
0
0
1
0
0
1
1
1
1
+
1
0
0
0
1
1
1
1
79
64
143
(-113)
Carry = 0 Overflow = 1
1
1
0
0
1
1
1
0
1
1
1
0
1
1
0
1
0
+
0
1
1
1
0
1
1
1
218 (-38)
157 (-99)
119
Carry = 1 Overflow = 1
1
1
1
We can have carry without overflow and vice-versa
Four cases are possible (Examples are 8-bit numbers)
1
1
1
1
1
0
0
0
0
0
0
0
1
1
1
1
+
0
0
0
0
0
1
1
1
15
248 (-8)
7
Carry = 1 Overflow = 0
1
1
1
1
1
0
0
0
0
1
0
0
0
0
0
0
0
1
1
1
1
+
0
0
0
1
0
1
1
1
15
8
23
Carry = 0 Overflow = 0
1

## Slide 62: Range, Carry, Borrow, and Overflow
Unsigned Integers: n-bit representation
Signed Integers: n-bit 2's complement representation
max = 2n–1
min = 0
Carry = 1
Addition
Numbers > max
Borrow = 1
Subtraction
Numbers < min
Positive
Overflow
Numbers > max
Negative
Overflow
Numbers < min
max = 2n-1–1
Finite Set of Signed Integers
0
min = -2n-1
Finite Set of Unsigned Integers

## Slide 63: Design by Contraction
Contraction is a technique for simplifying the logic
Applying 0s and 1s to some inputs and propagating values and simplifying equations
Converting a function block to a more simplified function
Examples of Design by Contraction
  Incrementing a number by a fixed constant
  Comparing a number to a fixed constant

## Slide 64: Designing an Incrementer
1
1

## Slide 65: Designing an Incrementer
An incrementer is a special case of an adder
Sum = A + 1 (B = 0, C0 = 1)
An n-bit Adder can be simplified into an n-bit Incrementer
1
0
0
0
0
0
0
0
0

## Slide 66: Simplifying the Incrementer Circuit
Many gates were eliminated
No longer needed when an input is a constant
Last cell can be replicated to implemented an n-bit incrementer
Incrementer
4
4
a [3:0]
s [3:0]
c4

## Slide 67: Iterative Design: Y=X-1
To design an iterative design to implement a decrementer, Y=X-1, we can convert this into Y=X+2’s complement of 1, i.e. Y=X+11…111
Thus, we need to add 1 to every cell
The cell interface is as follows:
Truth Table:
Xi
Yi
Cin
Cout
Y=X-1
Cin Xi | Cout Yi
0 0 | 0 1
0 1 | 0
1 0 | 1 0
1 1 | 1 1

## Slide 68: Iterative Design: Y=X-1
0-1=-1=111
7-1=6=110
-1-1=-2=110

## Slide 69: Design by Contraction: Y=X-1

## Slide 70: Design by Contraction: Y=X-1
Note that X1 + X1’ X0 can be simplified to X1 + X0. Thus, the AND gate can be eliminated in stage 2. Similarly, it can be eliminated in stage 3.
Also note that X1’  X0 = (X1  X0)’
Doing these optimizations we reach to the same solution obtained using iterative design.

## Slide 71: Zero versus Sign Extension
Unsigned Integers are Zero-Extended
Signed Integers are Sign-Extended
Given that X is a 4-bit number
  If X is a 4-bit unsigned integer  Range = 0 to 15
  If X is a 4-bit signed integer  Range = -8 to +7
  If unsigned X = 4’b1101 (binary), then X = 13 (decimal)
  If signed X = 4’b1101 (binary), then X = -3 (decimal)
  If X is zero-extended from 4 to 6 bits then X = 6’b001101 = 13
  If X is sign-extended from 4 to 6 bits then X = 6’b111101 = -3

## Slide 72: Unsigned Addition S = X + Y
Design a circuit that computes: S = X + Y (unsigned X and Y)
X[3:0] and Y[3:0] are 4-bit unsigned integers  Range = 0 to 15
Solution:
Maximum S = 15 + 15 = 30  unsigned S must be 5 bits
FA
X0
Y0
S0
0
FA
X1
Y1
S1
FA
X2
Y2
S2
FA
X3
S3
S4
Y3
c1
c2
c3
c4
c0
Most-significant sum bit S4 is the carry bit c4

## Slide 73: Signed Addition S = X + Y
Design a circuit that computes: S = X + Y (signed X and Y)
X[3:0] and Y[3:0] are 4-bit signed integers  Range = -8 to +7
Solution:
Minimum S = (-8) + (-8) = -16, Maximum S = (+7) + (+7) = + 14
Therefore, signed range of S = -16 to +14  S must be 5 bits
X and Y are sign-extended
X3 and Y3 are replicated to produce S4
FA
X0
Y0
S0
0
FA
X1
Y1
S1
FA
X2
Y2
S2
FA
X3
S3
Y3
c1
c2
c3
c0
FA
S4
c4

## Slide 74: S = 2*X + Y (Unsigned X and Y)
Design a circuit that computes S = 2*X + Y (unsigned X and Y)
X[3:0] and Y[3:0] are 4-bit unsigned integers  range = 0 to 15
Solution:
2*X + Y = X << 1 + Y (Shift-Left X by 1 bit)
Maximum value of S = 2*15 + 15 = 45  S is 6 bits = S[5:0]
FA
X0
Y1
S1
c1
c2
c3
c4
c5
S0
Y0
0
FA
X1
Y2
S2
FA
X2
Y3
S3
FA
X3
0
S4
S5

## Slide 75: S = 2*X + Y (Signed X and Y)
Design a circuit that computes S = 2*X + Y using Full Adders
X[3:0] and Y[3:0] are 4-bit signed integers  range = -8 to +7
Solution:
Range of X and Y is -8 to +7  Minimum S = 2*(-8) + (-8) = -24
Maximum S = 2*(+7) + 7 = +21  S is 6 bits = S[5:0]
FA
X0
Y1
S1
S0
Y0
0
FA
X1
Y2
S2
FA
X2
Y3
S3
FA
X3
S4
FA
S5
c1
c2
c3
c4
c5
X and Y are
sign-extended.
Sign bits X3 and Y3 are replicated.

## Slide 76: Unsigned Less Than: LT = X < Y
Design a circuit that computes unsigned LT (unsigned X and Y)
Solution:
If (X < Y) then (X – Y) < 0, If (X == Y) then (X – Y == 0)
Do unsigned subtraction, LT = S4 = sign-bit of the result
FA
X0
Y0
S0
1
FA
X1
Y1
S1
FA
X2
Y2
S2
FA
X3
S3
LT = S4
Y3
c1
c2
c3
c4
c0
GE = c4
EQ
Equality
(X – Y == 0)

## Slide 77: Signed Less Than: LT = X < Y
Design a circuit that computes signed LT (Signed X and Y)
Solution:
If (X < Y) then (X – Y) < 0, If (X == Y) then (X – Y == 0)
Do signed subtraction, LT = S4 = sign-bit of the result
S0
S1
S2
S3
LT = S4
EQ
Equality
(X – Y == 0)
FA
X0
Y0
1
FA
X1
Y1
FA
X2
Y2
FA
X3
FA
Y3
c1
c2
c3
c4
c0
Sign Extension

## Slide 78: BCD Adder
If two BCD digits are added then their sum result will not always be in BCD.
Consider the two given examples:
Whenever the sum result is > 9, it will not be in BCD and will require correction to get a valid BCD result.
Correction is done through the addition of 6 to the result to skip the six invalid values.

## Slide 79: BCD Adder
Consider the given examples of non-BCD sum result and its correction:

## Slide 80: BCD Adder
The maximum sum result of a BCD input adder can be 19. As maximum number in BCD is 9 and may be there will be a carry from previous stage also, so 9 + 9 + 1 = 19 .
The logic circuit that checks the necessary BCD correction can be derived by detecting the condition where the resulting binary sum is 01010 through 10011 (decimal 10 through 19).

## Slide 81: BCD Adder
F is true when CO is true OR when (Z3 Z2 + Z3 Z1) is true.
Thus, the correction step (adding 0110) is performed if the following function equals 1:

## Slide 82: Multiple Digit BCD Addition
Add: 2905 + 1897 in BCD
Showing carries and digit corrections
+1
0101
0111
1100
0110
0010
0000
1001
1010
0110
0000
+1
1001
1000
10010
0110
1000
+1
0010
0001
0100
0100
+
carry
digit correction
Final answer: 2905 + 1897 = 4802

## Slide 83: Ripple-Carry BCD Adder
Inputs are BCD digits: 0 to 9
Sum are BCD digits: ones, tens, hundreds, thousands, etc.
Can be extended to any number of BCD digits
BCD adders are larger in size than binary adders
BCD
Adder
c3
S [15:12]
B [15:12]
4
4
4
A [15:12]
c4
BCD
Adder
c2
S [11:8]
B [11:8]
4
4
4
A [11:8]
BCD
Adder
c1
S [7:4]
B [7:4]
4
4
4
A [7:4]
Tens
BCD
Adder
c0
S [3:0]
B [3:0]
4
4
4
A [3:0]
Ones
Hundreds
Thousands

## Slide 84: Binary Multiplier
Multiplication of binary numbers is performed in the same way as with decimal numbers.
The multiplicand is multiplied by each bit of the multiplier, starting from the least significant bit.
The result of each such multiplication forms a partial product. Successive partial products are shifted one bit to the left.
The product is obtained by adding these shifted partial products.

## Slide 85: Binary Multiplier
Example 1: Consider an example of multiplication of two numbers, say A and B (2 bits each), C = A x B.
The first partial product is formed by multiplying the B1B0 by A0. The multiplication of two bits such as A0 and B0 produces a 1 if both bits are 1; otherwise it produces a 0 like an AND operation. So the partial products can be implemented with AND gates.
The second partial product is formed by multiplying the B1B0 by A1 and is shifted one position to the left.

## Slide 86: Binary Multiplier
Example 2: Consider the example of multiplying two numbers, say A (3-bit number) and B (4-bit number).
Since J = 3 and K = 4, 12 (J x K) AND gates and two 4-bit ((J - 1) K-bit) adders are needed to produce a product of seven (J + K) bits.

## Slide 87: 4-bit × 4-bit Binary Multiplier
Suppose we want to multiply two numbers A and B
  Example on 4-bit numbers: A = a3 a2 a1 a0 and B = b3 b2 b1 b0
Step 1: AND (multiply) each bit of A with each bit of B
  Requires n2 AND gates and produces n2 product bits
  Position of aibj = (i+j). For example, Position of a2b3 = 2+3 = 5
a0b0
a1b0
a2b0
a3b0
a0b1
a1b1
a2b1
a3b1
a0b2
a1b2
a2b2
a3b2
a0b3
a1b3
a2b3
a3b3
A × B

## Slide 88: Adding the Bits Vertically
ADD the product bits vertically using Carry-Save adders
  Full Adder adds three vertical bits
  Half Adder adds two vertical bits
  Each adder produces a partial sum and a carry
Use Carry-propagate adder for final addition

## Slide 89: Carry Save Adder
A n-bit carry-save adder produces two n-bit outputs
  n-bit partial sum bits and n-bit carry bits
All the n bits of a carry-save adder work in parallel
  The carry does not propagate as in a carry-propagate adder
  This is why a carry-save is faster than a carry-propagate adder
Useful when adding multiple numbers (as in a multiplier)
Carry-Propagate Adder
+
a0
b0
s0
+
a1
b1
s1
+
a31
b31
s31
. . .
cout
cin
Carry-Save Adder
. . .
+
a31
b31
s'31
c'31
c31
+
a1
b1
s'1
c'1
c1
+
a0
b0
s'0
c'0
c0

## Slide 90: Carry-Save Adders in a Multiplier
Step 1: Use carry save adders to add the partial products
  Reduce the partial products to just two numbers
Step 2: Use carry-propagate adder to add last two numbers
P0
FA
a2b0 a1b1
HA
FA
FA
a3b0 a2b1
a0b0
HA
a1b0 a0b1
HA
HA
FA
FA
FA
FA
a3b1 a2b2
FA
a3b2
a2b3
a3b3
a1b3
a0b3
a1b2
a0b2
P1
P2
P3
P4
P5
P6
P7
Carry Save Adder
Carry Propagate Adder
Carry Save