## Slide 1: Sequential Circuit Analysis & Design
COE 202
Digital Logic Design
Dr. Aiman El-Maleh
College of Computer Sciences and Engineering
King Fahd University of Petroleum and Minerals

## Slide 2: Outline
Sequential Circuit Model
Synchronous vs. Asynchronous Sequential Circuits
Latches and Flip Flops
Sequential Circuit Timing Constraints
Sequential Circuit Analysis
Mealy vs. Moore Sequential Circuit Models
Sequential Circuit Design Procedure
Sequential Circuit Design Examples

## Slide 3: Combinational vs. Sequential Circuits
Combinational Circuit
  Outputs are a function of inputs only
  NO internal memory
Sequential Circuit
  Outputs are a function of Inputs and internal Memory
  Internal Memory stores information based on previous inputs
  The content of the internal Memory is called State

## Slide 4: Sequential Circuit Model
A Sequential circuit consists of:
1. Memory elements:
  Latches or Flip-Flops
  Store the Present State
2. Combinational Logic
  Computes the Outputs of the circuit
  Outputs depend on Inputs and Present State
  Computes the Next State of the circuit
  Next State also depends on the Inputs and the Present State

## Slide 5: Synchronous vs. Asynchronous Sequential Circuits
Synchronous Sequential Circuit
  Uses a clock signal to control changes in the memory elements
  Changes happen at discrete instances of time
Asynchronous Sequential Circuit
  Changes in the memory elements can happen at any instance of time
Our focus will be on Synchronous Sequential Circuits
  Easier to design and analyze than asynchronous sequential circuits

## Slide 6: Synchronous Sequential Circuits
Synchronous sequential circuits use a clock signal
The clock signal is an input to the memory elements
The clock determines when memory should be updated
The present state = output value of memory (stored)
The next state = input value to memory (not stored yet)

## Slide 7: The Clock
Time
Clock Cycle
Clock Cycle
Positive
Pulse
Negative
Pulse
Clock is a periodic signal = Train of pulses (1's and 0's)
The same Clock Cycle repeats indefinitely over time
Positive Pulse: when the level of the clock is 1
Negative Pulse: when the level of the clock is 0
Rising (Positive) Edge: when clock goes from 0 to 1
Falling (Negative) Edge: when clock goes from 1 down to 0

## Slide 8: Clock Cycle versus Clock Frequency
Time
Clock Cycle
Clock Cycle
Clock Cycle
Clock Cycle (or period) is a time duration
  Measured in seconds, milli-, micro-, nano-, or pico-seconds
  1 ms = 10-3 sec, 1 µs = 10-6 sec, 1 ns = 10-9 sec, 1 ps = 10-12 sec
Clock Frequency = number of cycles per second (Hertz)
  1 Hz=1 cycle/sec, 1 KHz=103 Hz, 1 MHz=106 Hz, 1 GHz=109 Hz
Clock Frequency = 1 / Clock Cycle
  Example: Given the clock cycle=0.5 ns=0.5 ×10-9 sec
  Then, the clock frequency=1/(0.5×10-9)=2×109 Hz=2 GHz

## Slide 9: Memory Elements
A memory element may be constructed using cascaded inverters
  Q will maintain the stored data
  However, there is no input to change
  the stored data.
  If we replace the inverters by two 2-input NOR gates we get a memory element where we can store a 1 (S=1, R=0) or 0 (S=0, R=1). Note that when (S=0, R=0), the stored value is preserved.
  This is called Set-Reset Latch (SR-Latch)

## Slide 10: Memory Elements
  If we replace the inverters by two 2-input NAND gates we get a memory element where we can store a 1 (S=1, R=0) or 0 (S=0, R=1). Note that when (S=0, R=0), the stored value is preserved.
  Thus, an SR-Latch can be built using either two cascaded 2-input NOR gates or NAND gates.

## Slide 11: SR Latch Operation
If and then Set ()
If and then Reset ()
When , and are unchanged
The latch stores its outputs and as long as
When , and are undefined (should never be used)

## Slide 12: SR Latch Operation
If the forbidden input values are applied followed by this will make the SR latch oscillate!!

## Slide 13: SR Latch with NAND Gates
If and then Set ()
If and then Reset ()
When , and are unchanged (remain the same)
The latch stores its outputs and as long as
When , and are undefined (should never be used)
Known as
the Latch

## Slide 14: SR Latch with a Clock Input
An additional Clock input signal C is used
Clock controls when the state of the latch can be changed
When C=0, the S and R inputs have no effect on the latch
The latch will remain in the same state, regardless of S and R
When C=1, then normal SR latch operation
C | S | R | Next State of Q
0 | X | X | No Change
1 | 0 | 0 | No Change
1 | 0 | 1 | Q=0; Reset State
1 | 1 | 0 | Q=1; Set State
1 | 1 | 1 | Undefined

## Slide 15: SR Latch with a Clock Input
An additional Clock input signal C is used
Clock controls when the state of the latch can be changed
When C=0, the S and R inputs have no effect on the latch
The latch will remain in the same state, regardless of S and R
When C=1, then normal SR latch operation
S
R

## Slide 16: D-Latch with a Clock Input
Only one data input
An inverter is added: and
and can never be 11 simultaneously  No undefined state
When , remains the same (No change in state)
When , and
Transparent

## Slide 17: Graphic Symbols for Latches
A bubble appears at the complemented output
Indicates that is the complement of
A bubble also appears at the inputs of an latch
Indicates that logic-0 is used (not logic-1) to set (or reset) the latch (as in the NAND latch implementation)

## Slide 18: Problem with Latches
A latch is level-sensitive (sensitive to the level of the clock)
As long as the clock signal is high, any change in the value of input appears in the output
  Output keeps changing its value during a clock cycle
  Final value of output is uncertain
Desired behavior: output changes only once per clock pulse
Due to this uncertainty, latches are NOT used as memory elements in synchronous circuits

## Slide 19: Flip-Flops
Latches can not be used as
Memory Elements in synchronous
sequential circuits as they are Level
Sensitive.
Flip Flops are Edge Sensitive; they
change their value on the edge of the clock (Edge-Triggered)
Flip Flops change their value once every clock cycle at either the rising edge or falling edge of the clock

## Slide 20: Master Slave Rising (Positive) Edge-Trigerred D Flip Flop
Built using two latches in a master-slave configuration
When CLK=0, the master is activated and the value on D is copied to Qm. The slave is unactivated and keeps its previous value.
When CLK=1, the master is unactivated and it holds the last value stored at Qm while the slave is activated and copies the value of Qm.

## Slide 21: Master Slave Rising (Positive) Edge-Trigerred D Flip Flop
The Flip Flop output q changes only once every clock cycle when the Clock changes from 0 to 1
The last value in the D input just before the edge of the clock is copied to the Q.

## Slide 22: Master Slave Falling (Negative) Edge-Trigerred D Flip Flop
Similar to rising (positive) edge-triggered flip-flop
Only one latch is enabled at any given time
  When C=1, the master is enabled and the D input is latched (slave disabled)
  When C=0, the slave is enabled to generate the outputs (master is disabled)
Master
Slave
Output changes when C changes from 1 to 0

## Slide 23: Graphic Symbols for Flip-Flops
D Flip
Flop
D Flip
Flop
A Flip-Flop has a similar symbol to a Latch
The difference is the arrowhead at the clock input C
The arrowhead indicates sensitivity to the edge of the clock
A bubble at the C input indicates falling (negative) edge-triggered FF

## Slide 24: D Flip-Flop with Asynchronous Set/Reset
When Flip-Flops are powered, their initial state is unknown
Some flip-flops have Asynchronous Set/Reset
Sets/Resets state (to logic value 1/0), independent of clock
If S/R input is inverted (bubble), S/R = 0 sets/resets flip-flop
Inputs |  |  |  | Outputs | 
S |  |  |  |  | 
1 | 0 | X | X | 0 | 1
0 | 1 | X | X | 1 | 0
1 | 1 | 0 | ↑ | 0 | 1
1 | 1 | 1 | ↑ | 1 | 0
Inputs |  |  |  | Outputs | 
S |  |  |  |  | 
1 | 0 | X | X | 0 | 1
0 | 1 | X | X | 1 | 0
1 | 1 | 0 | ↑ | 0 | 1
1 | 1 | 1 | ↑ | 1 | 0

## Slide 25: Synchronous vs. Asynchronous Set/Reset
When we start circuit operation
we must initialize the machine
to an initial state
This will initialize the flip-flops
to any desired values
Reset can be done either synchronously or asynchronously
Asynchronous set/reset initializes flip flops to 1/0 independent of the clock
Synchronous set/reset initializes flip flops to 1/0 synchronized with the edge of the clock

## Slide 26: Synchronous vs. Asynchronous Set/Reset
Asynchronous set/reset is provided built in with flip-flops
However, synchronous set/reset has to be provided explicitly through added logic gates
Synchronous Reset
Synchronous Set
1
1
1
0
0

## Slide 27: Sequential Circuit Timing Constraints
Setup Time (Ts): Time duration for which the data input must be valid and stable before the arrival of the clock edge.
Hold Time (Th): Time duration for which the data input must not be changed after the clock transition occurs.
Ts and Th must be ensured for proper operation of flip-flops
Valid data-in
Data Can be Modified after Th
Clock
Rising
Edge
Th
Ts

## Slide 28: Sequential Circuit Timing Constraints
Tclkq = Clock to q delay – Time between clock edge and data appearing at the output of the FF
TC = worst case delay through combinational logic
Based on the FF & combinational logic timing parameters, the following timing constraints are required for correct operation of the circuit: Tclk ≥ Tclkq + TC + Ts

## Slide 29: Sequential Circuit Analysis
Given a sequential circuit, the objective is to derive outputs & state behavior (outputs and next state) from (present states and inputs)
To analyze the behavior of a sequential circuit, the following procedure should be applied:
  1. Initialize the sequential circuit to an initial state (Reset=1)
  2. Apply Inputs
  3. Observe Outputs
  4. Pulse the Clock
  (Copy Next State to Present State)
  Repeat steps 2-4 for each input

## Slide 30: Sequential Circuit Analysis
Two equivalent approaches to represent sequential circuit behavior:
  State Table: A truth table-like approach
  State Diagram: A graphical, more intuitive way of representing the state table and expressing the sequential circuit operation
State table: a truth table describing behavior of comb. logic
  Combination Logic Inputs:
    Present State: values of state variables for each state (FF outputs)
    External Inputs
  Combination Logic Outputs:
    Next-state –value of the state (FF outputs) at time (t+1) based on present state and inputs. (Determined by FF inputs)
    Outputs –value of the outputs as a function of the present state and (sometimes) the inputs.

## Slide 31: Sequential Circuit Analysis
State Diagram: describes behavior of comb. Logic by
  representing each state in a circle and
  drawing arrows that show the transition from each present state to next states for each input and the corresponding output
Sequential Circuit Analysis Procedure:
  Obtain the equations at the inputs of the Flip-Flops
  Obtain the output equations
  Fill the state table for all possible input and state values
  Draw the state diagram

## Slide 32: Moore and Mealy Sequential Circuit Models
There are two sequential circuit models:
  Mealy Model: Outputs depend on present state and inputs
  Moore Model: Outputs depend on present state only

## Slide 33: Sequential Circuit Analysis Example
What are the equations on the inputs of the flip-flops?
and are the current state
and are the next state
The values ofand
and at the next clock edge
What is the output equation?

## Slide 34: Sequential Circuit Analysis Example

## Slide 35: Sequential Circuit Analysis Example

## Slide 36: Sequential Circuit Analysis Example

## Slide 37: Moore Sequential Circuit Analysis Example
Flip-Flop Input Equation:
⨁ ⨁
Output Equation:
Z =
Output does not depend on input: Moore Model

## Slide 38: Mealy Machine
The outputs are a function of the present state and Inputs
The outputs are NOT synchronized with the clock
The outputs may change if inputs change during the clock cycle
The outputs may have momentary false values (called glitches)
The correct outputs are present just before the edge of the clock

## Slide 39: Mealy State Diagram
An example of a Mealy state diagram is shown on the right
Each arc is labeled with:
Input / Output
The output is shown on the arcs of the state diagram
The output depends on the current state and input
Notice that State 11 cannot be reached from the other states

## Slide 40: Tracing a Mealy State Diagram
Cycle | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Input x | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0
Present State A B | ? | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1
 | ? | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0
Output z | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0
When the circuit is powered, the initial state (AB) is unknown
Even though the initial state is unknown, the input x = 0 forces a transition to state AB = 00, regardless of the present state
Sometimes, a reset input is used to initialize the state to 00

## Slide 41: Tracing a Mealy State Diagram
Cycle | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Input x | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0
Present State A B | ? | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1
 | ? | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0
Output z | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0
A
B
Negative edge-triggered

## Slide 42: Moore Machine
The outputs are a function of the Flip-Flop outputs only
The outputs depend on the current state only
The outputs are synchronized with the clock
Glitches cannot appear in the outputs (even if inputs change)
A given design might mix between Mealy and Moore

## Slide 43: Moore State Diagram
An example of a Moore state diagram is shown on the right
Arcs are labeled with input only
The output is shown inside the state: (State / Output)
The output depends on the current state only
00
0
01
0
10
0
11
1
1
1
1
0
0
0
1
0

## Slide 44: Tracing a Moore State Diagram
When the circuit is powered, the initial state (AB) and output are unknown
Input x = 0 resets the state AB to 00. Can also be done with a reset signal.
Cycle | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Input x | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0
Present State A B | ? | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1
 | ? | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1
Output z | ? | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
00
0
01
0
10
0
11
1
1
1
1
0
0
0
1
0

## Slide 45: Tracing a Moore State Diagram
Cycle | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Input x | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0
Present State A B | ? | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1
 | ? | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1
Output z | ? | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
Negative edge-triggered
A
B
The output is synchronized with the clock. No false output (or glitch) can appear.

## Slide 46: Sequential Circuit Analysis Example
Is the circuit type Mealy or Moore? Why?
Derive expressions for the D0 and D1 flip flop inputs and the external output Z.
What is the circuit initial state?
Derive the state transition table of the circuit.

## Slide 47: Sequential Circuit Analysis Example
Is the circuit type Mealy or Moore? Why?
  Mealy since Z depends on the input x.
Derive expressions for D0 and D1 flip flop inputs and output Z.
What is the circuit initial state? Initial state
Derive the state transition table of the circuit.

## Slide 48: Sequential Circuit Design Procedure
1. Specification – e.g. Verbal description
2. Formulation – Interpret the specification to obtain a state diagram and a state table
3. State Assignment - Assign binary codes to symbolic states
4. Flip-Flop Input Equation Determination - Select flip-flop types and derive flip-flop input equations from next state entries in the state table
5. Output Equation Determination - Derive output equations from output entries in the state table
6. Verification - Verify correctness of final design

## Slide 49: The State Diagram
A state is an abstraction of memory
Each state should store unique information that distinguishes it from other states
Examples:
  State represents the fact that the last input is a 0 or 1
  State represents the fact that the last two-input sequence is "11“
  State represents that carry = 1
Obtaining the state diagram is the most important step in the design process

## Slide 50: Example: Sequence Detector
A sequence detector is a sequential circuit that detects a specific sequence of bits in the input
The input is a serial bit stream: One input bit is fed to the sequence detector each cycle
The output is also a bit stream: One output bit each cycle that indicates whether a given sequence is detected or not
Sequence Detector

## Slide 51: Example: Sequence Detector
1. Specifications: Detect the occurrence of bit sequence 1101 whenever it occurs on input X and indicate this detection by raising an output Z high assuming overlapping of detected sequences
2. Formulation: State Diagram
Reset

## Slide 52: Example: Sequence Detector
From the State Diagram, we can fill in the 2-D State Table
There are 4 states, one input, and one output.
Two dimensional table with four rows, one for each current state.
State Diagram
State Table
Reset

## Slide 53: Example: Sequence Detector
3. State Assignment: From abstract symbols to binary bit representation of states
Each of the m symbolic states must be assigned a unique binary code
Minimum number of state bits (state variables) (FFs) required is nb, such that 2nb ≥ ns
If 2nb > ns, this leaves (2nb – ns) unused states
Utilize them as don’t care conditions to simplify CL design
But may need caution: e.g. what if the circuit enters an unused state by mistake
nb= log2 ns

## Slide 54: Example: Sequence Detector
Also which code is given to which state?  different CL implementations  may influence optimization, e.g. (with 2 FFs) State A is assigned 00 or 01 or 10 or 11?
There are possible encodings = 24
Let A = 00 (to suit being a Reset state), B = 01, C = 11, D = 10

## Slide 55: Example: Sequence Detector
For optimization of FF input equations we express A(t+1), B(t+1), Z(t) in terms of A(t), B(t) and X(t) (using one dimensional state table)

## Slide 56: Example: Sequence Detector

## Slide 57: Example: Sequence Detector (Moore Model)
With the Moore model, output is associated with only a state not a state and an input as in Mealy model
This means that we need to add a fifth state (remembers the target sequence 1101) and produces the required Z=1 output

## Slide 58: Example: Sequence Detector (Mealy Model)
Design Mealy type "111" sequence detector with sequence overlapping
State Diagram:
State Assignment:
  Assign: S0 = 00, S1 = 01, and S2 = 10 (State 11 is Unused)
0 / 0
0 / 0
S0
0 / 0
1 / 0
S1
1 / 0
S2
1 / 1
Reset

## Slide 59: Example: Sequence Detector (Mealy Model)
State Table:
Present State | Next State |  | Output | 
 | = 0 | = 1 | = 0 | = 1
S0 | S0 | S1 | 0 | 0
S1 | S0 | S2 | 0 | 0
S2 | S0 | S2 | 0 | 1
Present State | Next State |  |  | 
S0 | S0 | S1 | 0 | 0
S1 | S0 | S2 | 0 | 0
S2 | S0 | S2 | 0 | 1
Present State | Next State |  | Output | 
 | = 0 | = 1 | = 0 | = 1
0 0 | 0 0 | 0 1 | 0 | 0
0 1 | 0 0 | 1 0 | 0 | 0
1 0 | 0 0 | 1 0 | 0 | 1
Present State | Next State |  |  | 
0 0 | 0 0 | 0 1 | 0 | 0
0 1 | 0 0 | 1 0 | 0 | 0
1 0 | 0 0 | 1 0 | 0 | 1

## Slide 60: Example: Sequence Detector (Mealy Model)
Present State = Flip-Flop Outputs and (state 11 is unused)
Next State = Flip-Flop Inputs and
Flip-Flop Input equations: and
Output equation:
Present State | Next State |  | Output | 
 | = 0 | = 1 | = 0 | = 1
0 0 | 0 0 | 0 1 | 0 | 0
0 1 | 0 0 | 1 0 | 0 | 0
1 0 | 0 0 | 1 0 | 0 | 1
1 1 | X X | X X | X | X
Present State | Next State |  |  | 
0 0 | 0 0 | 0 1 | 0 | 0
0 1 | 0 0 | 1 0 | 0 | 0
1 0 | 0 0 | 1 0 | 0 | 1
1 1 | X X | X X | X | X

## Slide 61: Example: Sequence Detector (Mealy Model)

## Slide 62: Example: Sequence Detector (Moore Model)
Dear Mealy type "111" sequence detector with sequence overlapping
State Diagram:
State Assignment:
  S0 = 00, S1 = 01, S2 = 10 and S3 = 11

## Slide 63: Example: Sequence Detector (Moore Model)
Present State | Next State |  | Output
 | = 0 | = 1 | 
S0 | S0 | S1 | 0
S1 | S0 | S2 | 0
S2 | S0 | S3 | 0
S3 | S0 | S3 | 1
Present State | Next State |  | 
S0 | S0 | S1 | 0
S1 | S0 | S2 | 0
S2 | S0 | S3 | 0
S3 | S0 | S3 | 1
Present State | Next State |  | Output
 | = 0 | = 1 | 
0 0 | 0 0 | 0 1 | 0
0 1 | 0 0 | 1 0 | 0
1 0 | 0 0 | 1 1 | 0
1 1 | 0 0 | 1 1 | 1
Present State | Next State |  | 
0 0 | 0 0 | 0 1 | 0
0 1 | 0 0 | 1 0 | 0
1 0 | 0 0 | 1 1 | 0
1 1 | 0 0 | 1 1 | 1
State Assignment
S0 = 00, S1 = 01
S2 = 10, S3 = 11

## Slide 64: Example: Sequence Detector (Moore Model)
Two D-type Flips-Flops
Present State = Flip-Flop Outputs and
Next State = Flip-Flop Inputs and
Next State equations: and
Output equation: (from the state diagram)
Present State | Next State |  | Output
 | = 0 | = 1 | 
0 0 | 0 0 | 0 1 | 0
0 1 | 0 0 | 1 0 | 0
1 0 | 0 0 | 1 1 | 0
1 1 | 0 0 | 1 1 | 1
Present State | Next State |  | 
0 0 | 0 0 | 0 1 | 0
0 1 | 0 0 | 1 0 | 0
1 0 | 0 0 | 1 1 | 0
1 1 | 0 0 | 1 1 | 1
0
1
00
01
11
10
0
0
0
1
0
1
0
1
0
1
00
01
11
10
0
1
0
0
0
1
0
1

## Slide 65: Example: Sequence Detector (Moore Model)
,

## Slide 66: Mealy versus Moore Sequence Detector
In general, Moore state diagrams have more states than corresponding Mealy.
The drawback of Mealy is that glitches can appear in the output if the input is not synchronized with the clock.
Mealy Sequence Detector
Moore Sequence Detector

## Slide 67: Sequential Circuit Verification
Sequential circuits should be verified by showing that the circuit produces the original state diagram
Verification can be done manually, or with the help of a simulation program
All possible input combinations are applied at each state and the state variables and outputs are observed
A reset input is used to reset the circuit to its initial state
Apply a sequence of inputs to test all the state-input combinations, i.e., all transitions in the state diagram
Observe the output and the next state that appears after each clock edge in the timing diagram

## Slide 68: Verification Input Test Sequence
Required to verify the correct operation of a sequential circuit
It should test each state transition of the state diagram
Test sequences can be produced from the state diagram
Consider the Mealy sequence detector, starting at S0 (reset), we can use an input test sequence to verify all state transitions:
Input test sequence: reset then x = 0, 1, 0, 1, 1, 0, 1, 1, 1, 1
Reset input forces initial state to be S0

## Slide 69: Verifying the Mealy Sequence Detector

## Slide 70: Sequential Comparator
Design a sequential circuit that compares two numbers A and B
Two Inputs: A and B
A consists of n bits
B consists of n bits
Bit streaming starting at bit 0
Compare A0 with B0, A1 with B1, etc. (Bit 0 is least significant bit)
Two outputs: GT (Greater Than) and LT (Less Than)
Sequential
Comparator

## Slide 71: Designing the State Diagram
01
10
00, 11, 10
00, 11, 01
GT
10
10
01
LT
01
Reset: start initially in state EQ
EQ indicates Equality (output is 00)
Stay in EQ as long as AiBi = 00 or 11
Go to LT if Ai < Bi (AiBi = 01)
LT indicates Less Than (output is 01)
Go to GT if Ai > Bi (AiBi = 10)
GT is Greater Than (output is 10)
Complete the state diagram
LT  GT and GT  LT
LT  LT and GT  GT
EQ
00
Reset
00, 11
Moore State Diagram

## Slide 72: State Assignment and State Table
Three States  Two Flip-Flops
D-type Flip-Flops will be used
State Assignment: EQ = 00, LT = 01, GT = 10
Output = Present State (Q1 and Q0)
01
10
00, 11, 10
00, 11, 01
GT
10
10
01
LT
01
EQ
00
Reset
00, 11
Present State Q1 Q0 | Next State (D1 D0) |  |  | 
 | A B 0 0 | A B 0 1 | A B 1 0 | A B 1 1
0 0 | 0 0 | 0 1 | 1 0 | 0 0
0 1 | 0 1 | 0 1 | 1 0 | 0 1
1 0 | 1 0 | 0 1 | 1 0 | 1 0
1 1 | X X | X X | X X | X X

## Slide 73: Deriving the Next State Equations
State 11 is unused
When present state is 11, don't cares are used to fill the next state.
Output = Present state
00
01
11
10
00
01
11
10
1
X
0
0
0
X
0
0
1
X
0
0
1
X
1
1
00
01
11
10
00
01
11
10
0
X
0
1
1
X
1
1
0
X
0
1
0
X
0
0
Present State Q1 Q0 | Next State (D1 D0) |  |  | 
 | A B 0 0 | A B 0 1 | A B 1 0 | A B 1 1
0 0 | 0 0 | 0 1 | 1 0 | 0 0
0 1 | 0 1 | 0 1 | 1 0 | 0 1
1 0 | 1 0 | 0 1 | 1 0 | 1 0
1 1 | X X | X X | X X | X X

## Slide 74: Sequential Comparator Circuit Diagram

## Slide 75: Sequential Circuit Code Detector
It is required to design a sequential circuit that detects the 3-bit codes 010 or 110
Note that code detector is different from sequence detector
Code detector checks the code every 3 bits in this example
S0
S1
S2
S3
X/0
1/0
1/0
0/1
0/0
X/0
Reset

## Slide 76: Sequential Circuit Design: Y = 3*X + 1
single input X and a single output Y.
The circuit receives an unsigned number serially through the input X from the least significant bit (LSB) to the most significant bit (MSB), and computes the equation Y=3*X+1 and generates the output serially from the least significant bit to the most significant bit.

## Slide 77: Sequential Circuit Design: Y = 3*X + 1
Present State | Next State |  | Output | 
 | = 0 | = 1 | = 0 | = 1
0 0 | 0 1 | 1 0 | 1 | 0
0 1 | 0 1 | 0 0 | 0 | 1
1 0 | 0 0 | 1 0 | 0 | 1
1 1 | X X | X X | X | X
Present State | Next State |  |  | 
0 0 | 0 1 | 1 0 | 1 | 0
0 1 | 0 1 | 0 0 | 0 | 1
1 0 | 0 0 | 1 0 | 0 | 1
1 1 | X X | X X | X | X
State Assignment
S0 = 00, S1 = 01, S2 = 10
Present State | Next State |  | Output | 
 | = 0 | = 1 | = 0 | = 1
S0 | S1 | S2 | 1 | 0
S1 | S1 | S0 | 0 | 1
S2 | S0 | S2 | 0 | 1
Present State | Next State |  |  | 
S0 | S1 | S2 | 1 | 0
S1 | S1 | S0 | 0 | 1
S2 | S0 | S2 | 0 | 1
S0 (C=1), S1 (C=0), S2 (C=2)

## Slide 78: Sequential Circuit Design: Y = 3*X + 1
D1 = F0’ X
D0 = F1’ X’
Z = F1’ F0’ X’ + F1 X + F0 X
= F1’ F0’ X’ + X (F1 + F0)
= (X  (F1+F0))’

## Slide 79: Sequential Circuit Design: Y = X - 1
Design a sequential circuit to compute the equation Y=X-1 serially.
Note that -1=11..111. Thus, we will add 1 with every bit.
Present State | Next State |  | Output | 
 | = 0 | = 1 | = 0 | = 1
S0 | S0 | S1 | 1 | 0
S1 | S1 | S1 | 0 | 1
Present State | Next State |  |  | 
S0 | S0 | S1 | 1 | 0
S1 | S1 | S1 | 0 | 1
S0 (C=0), S1 (C=1))
State | S0 | S0 | S0 | S0 | S1
Input (X) | 0 | 0 | 0 | 1 | 0
Output (Y) | 1 | 1 | 1 | 0 | 0
Input: X=8
Output: Y=7

## Slide 80: BCD to Excess-3 Serial Code Converter
It is required to design a serial BCD to Excess-3 converter.
Assume that once the machine is reset, a continues stream of BCD digits will be transmitted serially and converted to Excess-3 digits.

## Slide 81: BCD to Excess-3 Serial Code Converter
State Diagram
State Table

## Slide 82: BCD to Excess-3 Serial Code Converter

## Slide 83: BCD to Excess-3 Serial Code Converter
Karnaugh maps for the encoded state bits and output bit (Bout)

## Slide 84: BCD to Excess-3 Serial Code Converter