## Slide 1: Introduction to Assembly Language Programming
COE 301 Computer Organization
Prof. Aiman El-Maleh
College of Computer Sciences and Engineering
King Fahd University of Petroleum and Minerals
[Adapted from slides of Dr. M. Mudawar, COE 301, KFUPM]

## Slide 2: Outline
The MIPS Instruction Set Architecture
Introduction to Assembly Language
Defining Data
Memory Alignment and Byte Ordering
System Calls

## Slide 3: Instruction Set Architecture (ISA)
Critical interface between hardware and software
An ISA includes the following …
  Instructions and Instruction Formats
    Data Types, Encodings, and Representations
    Addressing Modes: to address Instructions and Data
    Handling Exceptional Conditions (like division by zero)
  Programmable Storage: Registers and Memory
Examples (Versions) First Introduced in
  Intel (8086, 80386, Pentium, ...) 1978
  MIPS (MIPS I, II, III, IV, V) 1986
  PowerPC (601, 604, …) 1993

## Slide 4: Instructions
Instructions are the language of the machine
We will study the MIPS instruction set architecture
  Known as Reduced Instruction Set Computer (RISC)
  Elegant and relatively simple design
  Similar to RISC architectures developed in mid-1980’s and 90’s
  Very popular, used in many products
    Silicon Graphics, ATI, Cisco, Sony, etc.
  Comes next in sales after Intel IA-32 processors
    Almost 100 million MIPS processors sold in 2002 (and increasing)
Alternative design: Intel IA-32
  Known as Complex Instruction Set Computer (CISC)

## Slide 5: Overview of the MIPS Processor
Memory
Up to 232 bytes = 230 words
4 bytes per word
$0
$1
$2
$31
Hi
Lo
ALU
F0
F1
F2
F31
FP
Arith
EPC
Cause
BadVaddr
Status
EIU
FPU
TMU
Execution &
Integer Unit
(Main proc)
Floating
Point Unit
(Coproc 1)
Trap &
Memory Unit
(Coproc 0)
. . .
. . .
Integer
mul/div
Arithmetic &
Logic Unit
32 General
Purpose
Registers
Integer Multiplier/Divider
32 Floating-Point
Registers
Floating-Point
Arithmetic Unit

## Slide 6: MIPS General-Purpose Registers
32 General Purpose Registers (GPRs)
  Assembler uses the dollar notation to name registers
    $0 is register 0, $1 is register 1, …, and $31 is register 31
  All registers are 32-bit wide in MIPS32
  Register $0 is always zero
    Any value written to $0 is discarded
Software conventions
  Software defines names to all registers
    To standardize their use in programs
  Example: $8 - $15 are called $t0 - $t7
    Used for temporary values
$0 = $zero
$1 = $at
$2 = $v0
$3 = $v1
$4 = $a0
$5 = $a1
$6 = $a2
$7 = $a3
$8 = $t0
$9 = $t1
$10 = $t2
$11 = $t3
$12 = $t4
$13 = $t5
$14 = $t6
$15 = $t7
$16 = $s0
$17 = $s1
$18 = $s2
$19 = $s3
$20 = $s4
$21 = $s5
$22 = $s6
$23 = $s7
$24 = $t8
$25 = $t9
$26 = $k0
$27 = $k1
$28 = $gp
$29 = $sp
$30 = $fp
$31 = $ra

## Slide 7: MIPS Register Conventions
Name | Register | Usage
$zero | $0 | Always 0 (forced by hardware)
$at | $1 | Reserved for assembler use
$v0 – $v1 | $2 – $3 | Result values of a function
$a0 – $a3 | $4 – $7 | Arguments of a function
$t0 – $t7 | $8 – $15 | Temporary Values
$s0 – $s7 | $16 – $23 | Saved registers (preserved across call)
$t8 – $t9 | $24 – $25 | More temporaries
$k0 – $k1 | $26 – $27 | Reserved for OS kernel
$gp | $28 | Global pointer (points to global data)
$sp | $29 | Stack pointer (points to top of stack)
$fp | $30 | Frame pointer (points to stack frame)
$ra | $31 | Return address (used by jal for function call)
Assembler can refer to registers by name or by number
  It is easier for you to remember registers by name
  Assembler converts register name to its corresponding number

## Slide 8: Instruction Formats
All instructions are 32-bit wide. Three instruction formats:
Register (R-Type)
  Register-to-register instructions
  Op: operation code specifies the format of the instruction
Immediate (I-Type)
  16-bit immediate constant is part in the instruction
Jump (J-Type)
  Used by jump instructions
Op6
Rs5
Rt5
Rd5
funct6
sa5
Op6
Rs5
Rt5
immediate16
Op6
immediate26

## Slide 9: Next . . .
The MIPS Instruction Set Architecture
Introduction to Assembly Language
Defining Data
Memory Alignment and Byte Ordering
System Calls

## Slide 10: Assembly Language Statements
Three types of statements in assembly language
  Typically, one statement should appear on a line
Executable Instructions
  Generate machine code for the processor to execute at runtime
  Instructions tell the processor what to do
Pseudo-Instructions and Macros
  Translated by the assembler into real instructions
  Simplify the programmer task
Assembler Directives
  Provide information to the assembler while translating a program
  Used to define segments, allocate memory variables, etc.
  Non-executable: directives are not part of the instruction set

## Slide 11: Instructions
Assembly language instructions have the format:
[label:] mnemonic [operands] [#comment]
Label: (optional)
  Marks the address of a memory location, must have a colon
  Typically appear in data and text segments
Mnemonic
  Identifies the operation (e.g. add, sub, etc.)
Operands
  Specify the data required by the operation
  Operands can be registers, memory variables, or constants
  Most instructions have three operands
L1: addiu $t0, $t0, 1 #increment $t0

## Slide 12: Comments
Comments are very important!
  Explain the program's purpose
  When it was written, revised, and by whom
  Explain data used in the program, input, and output
  Explain instruction sequences and algorithms used
  Comments are also required at the beginning of every procedure
    Indicate input parameters and results of a procedure
    Describe what the procedure does
Single-line comment
  Begins with a hash symbol # and terminates at end of line

## Slide 13: Program Template
# Title: Filename:
# Author: Date:
# Description:
# Input:
# Output:
################# Data segment #####################
.data
. . .
################# Code segment #####################
.text
.globl main
main: # main program entry
. . .
li $v0, 10 # Exit program
syscall

## Slide 14: .DATA, .TEXT, & .GLOBL Directives
.DATA directive
  Defines the data segment of a program containing data
  The program's variables should be defined under this directive
  Assembler will allocate and initialize the storage of variables
.TEXT directive
  Defines the code segment of a program containing instructions
.GLOBL directive
  Declares a symbol as global
  Global symbols can be referenced from other files
  We use this directive to declare main procedure of a program

## Slide 15: Layout of a Program in Memory
Stack Segment
0x7FFFFFFF
Dynamic Area
Static Area
Text Segment
Reserved
0x04000000
0x10000000
0
Data Segment
Memory
Addresses
in Hex
Stack Grows
Downwards

## Slide 16: Next . . .
The MIPS Instruction Set Architecture
Introduction to Assembly Language
Defining Data
Memory Alignment and Byte Ordering
System Calls

## Slide 17: Data Definition Statement
Sets aside storage in memory for a variable
May optionally assign a name (label) to the data
Syntax:
[name:] directive initializer [, initializer] . . .
  var1: .WORD 10
All initializers become binary data in memory

## Slide 18: Data Directives
.BYTE Directive
  Stores the list of values as 8-bit bytes
.HALF Directive
  Stores the list as 16-bit values aligned on half-word boundary
.WORD Directive
  Stores the list as 32-bit values aligned on a word boundary
.WORD w:n Directive
  Stores the 32-bit value w into n consecutive words aligned on a word boundary.

## Slide 19: Data Directives
.HALF w:n Directive
  Stores the 16-bit value w into n consecutive half-words aligned on a half-word boundary .
.BYTE w:n Directive
  Stores the 8-bit value w into n consecutive bytes.
.FLOAT Directive
  Stores the listed values as single-precision floating point
.DOUBLE Directive
  Stores the listed values as double-precision floating point

## Slide 20: String Directives
.ASCII Directive
  Allocates a sequence of bytes for an ASCII string
.ASCIIZ Directive
  Same as .ASCII directive, but adds a NULL char at end of string
  Strings are null-terminated, as in the C programming language
.SPACE n Directive
  Allocates space of n uninitialized bytes in the data segment
Special characters in strings follow C convention
  Newline: \n Tab:\t Quote: \”

## Slide 21: Examples of Data Definitions
.DATA
var1: .BYTE 'A', 'E', 127, -1, '\n'
var2: .HALF -10, 0xffff
var3: .WORD 0x12345678
Var4: .WORD 0:10
var5: .FLOAT 12.3, -0.1
var6: .DOUBLE 1.5e-10
str1: .ASCII "A String\n"
str2: .ASCIIZ "NULL Terminated String"
array: .SPACE 100

## Slide 22: Next . . .
The MIPS Instruction Set Architecture
Introduction to Assembly Language
Defining Data
Memory Alignment and Byte Ordering
System Calls

## Slide 23: Memory Alignment
Memory is viewed as an array of bytes with addresses
  Byte Addressing: address points to a byte in memory
Words occupy 4 consecutive bytes in memory
  MIPS instructions and integers occupy 4 bytes
Alignment: address is a multiple of size
  Word address should be a multiple of 4
    Least significant 2 bits of address should be 00
  Halfword address should be a multiple of 2
.ALIGN n directive
  Aligns the next data definition on a 2n byte boundary
0
4
8
12
address
not aligned
. . .
aligned word
not aligned
Memory

## Slide 24: Symbol Table
Assembler builds a symbol table for labels (variables)
  Assembler computes the address of each label in data segment
Example Symbol Table
.DATA
var1: .BYTE 1, 2,'Z'
str1: .ASCIIZ "My String\n"
var2: .WORD 0x12345678
.ALIGN 3
var3: .HALF 1000
Label
var1
str1
var2
var3
Address
0x10010000
0x10010003
0x10010010
0x10010018
0
0
0
0
0
0
var1
1
2
'Z'
0x10010000
str1
'M'
'y'
' '
'S'
't'
'r'
'i'
'n'
'g'
'\n'
0
0x12345678
0x10010010
var2 (aligned)
1000
var3 (address is multiple of 8)
0
0
Unused
0
0
0
0
Unused

## Slide 25: Byte Ordering and Endianness
Processors can order bytes within a word in two ways
Little Endian Byte Ordering
  Memory address = Address of least significant byte
  Example: Intel IA-32, Alpha
Big Endian Byte Ordering
  Memory address = Address of most significant byte
  Example: SPARC, PA-RISC
MIPS can operate with both byte orderings
Byte 0
Byte 1
Byte 2
Byte 3
32-bit Register
MSB
LSB
. . .
. . .
Byte 0
Byte 1
Byte 2
Byte 3
a
a+3
a+2
a+1
Memory
address
Byte 3
Byte 0
Byte 1
Byte 2
Byte 3
32-bit Register
MSB
LSB
. . .
. . .
Byte 0
Byte 1
Byte 2
a
a+3
a+2
a+1
Memory
address

## Slide 26: Next . . .
The MIPS Instruction Set Architecture
Introduction to Assembly Language
Defining Data
Memory Alignment and Byte Ordering
System Calls

## Slide 27: System Calls
Programs do input/output through system calls
MIPS provides a special syscall instruction
  To obtain services from the operating system
  Many services are provided in the SPIM and MARS simulators
Using the syscall system services
  Load the service number in register $v0
  Load argument values, if any, in registers $a0, $a1, etc.
  Issue the syscall instruction
  Retrieve return values, if any, from result registers

## Slide 28: Syscall Services
Service | $v0 | Arguments / Result
Print Integer | 1 | $a0 = integer value to print
Print Float | 2 | $f12 = float value to print
Print Double | 3 | $f12 = double value to print
Print String | 4 | $a0 = address of null-terminated string
Read Integer | 5 | Return integer value in $v0
Read Float | 6 | Return float value in $f0
Read Double | 7 | Return double value in $f0
Read String | 8 | $a0 = address of input buffer $a1 = maximum number of characters to read
Allocate Heap memory | 9 | $a0 = number of bytes to allocate Return address of allocated memory in $v0
Exit Program | 10 | 

## Slide 29: Syscall Services – Cont’d
Print Char | 11 | $a0 = character to print
Read Char | 12 | Return character read in $v0
Open File | 13 | $a0 = address of null-terminated filename string $a1 = flags (0=read, 1=write, 9=append) $a2 = mode (ignored) Return file descriptor in $v0 (negative if error)
Read from File | 14 | $a0 = File descriptor $a1 = address of input buffer $a2 = maximum number of characters to read Return number of characters read in $v0
Write to File | 15 | $a0 = File descriptor $a1 = address of buffer $a2 = number of characters to write Return number of characters written in $v0
Close File | 16 | $a0 = File descriptor

## Slide 30: Reading and Printing an Integer
################# Code segment #####################
.text
.globl main
main: # main program entry
li $v0, 5 # Read integer
syscall # $v0 = value read
move $a0, $v0 # $a0 = value to print
li $v0, 1 # Print integer
syscall
li $v0, 10 # Exit program
syscall

## Slide 31: Reading and Printing a String
################# Data segment #####################
.data
str: .space 10 # array of 10 bytes
################# Code segment #####################
.text
.globl main
main: # main program entry
la $a0, str # $a0 = address of str
li $a1, 10 # $a1 = max string length
li $v0, 8 # read string
syscall
li $v0, 4 # Print string str
syscall
li $v0, 10 # Exit program
syscall

## Slide 32: Program 1: Sum of Three Integers
# Sum of three integers
#
# Objective: Computes the sum of three integers.
# Input: Requests three numbers.
# Output: Outputs the sum.
################### Data segment ###################
.data
prompt: .asciiz "Please enter three numbers: \n"
sum_msg: .asciiz "The sum is: "
################### Code segment ###################
.text
.globl main
main:
la $a0,prompt # display prompt string
li $v0,4
syscall
li $v0,5 # read 1st integer into $t0
syscall
move $t0,$v0

## Slide 33: Sum of Three Integers – Slide 2 of 2
li $v0,5 # read 2nd integer into $t1
syscall
move $t1,$v0
li $v0,5 # read 3rd integer into $t2
syscall
move $t2,$v0
addu $t0,$t0,$t1 # accumulate the sum
addu $t0,$t0,$t2
la $a0,sum_msg # write sum message
li $v0,4
syscall
move $a0,$t0 # output sum
li $v0,1
syscall
li $v0,10 # exit
syscall

## Slide 34: Program 2: Case Conversion
# Objective: Convert lowercase letters to uppercase
# Input: Requests a character string from the user.
# Output: Prints the input string in uppercase.
################### Data segment #####################
.data
name_prompt: .asciiz "Please type your name: "
out_msg: .asciiz "Your name in capitals is: "
in_name: .space 31 # space for input string
################### Code segment #####################
.text
.globl main
main:
la $a0,name_prompt # print prompt string
li $v0,4
syscall
la $a0,in_name # read the input string
li $a1,31 # at most 30 chars + 1 null char
li $v0,8
syscall

## Slide 35: Case Conversion – Slide 2 of 2
la $a0,out_msg # write output message
li $v0,4
syscall
la $t0,in_name
loop:
lb $t1,($t0)
beqz $t1,exit_loop # if NULL, we are done
blt $t1,'a',no_change
bgt $t1,'z',no_change
addiu $t1,$t1,-32 # convert to uppercase: 'A'-'a'=-32
sb $t1,($t0)
no_change:
addiu $t0,$t0,1 # increment pointer
j loop
exit_loop:
la $a0,in_name # output converted string
li $v0,4
syscall
li $v0,10 # exit
syscall