## Slide 1: Instruction Set Architecture
ICS 233
Computer Architecture and Assembly Language
Dr. Aiman El-Maleh
College of Computer Sciences and Engineering
King Fahd University of Petroleum and Minerals
[Adapted from slides of Dr. M. Mudawar, ICS 233, KFUPM]

## Slide 2: Outline
Instruction Set Architecture
Overview of the MIPS Processor
R-Type Arithmetic, Logical, and Shift Instructions
I-Type Format and Immediate Constants
Jump and Branch Instructions
Translating If Statements and Boolean Expressions
Load and Store Instructions
Translating Loops and Traversing Arrays
Addressing Modes

## Slide 3: Instruction Set Architecture (ISA)
Critical interface between hardware and software
An ISA includes the following …
  Instructions and Instruction Formats
    Data Types, Encodings, and Representations
    Addressing Modes: to address Instructions and Data
    Handling Exceptional Conditions (like division by zero)
  Programmable Storage: Registers and Memory
Examples (Versions) First Introduced in
  Intel (8086, 80386, Pentium, ...) 1978
  MIPS (MIPS I, II, III, IV, V) 1986
  PowerPC (601, 604, …) 1993

## Slide 4: Instructions
Instructions are the language of the machine
We will study the MIPS instruction set architecture
  Known as Reduced Instruction Set Computer (RISC)
  Elegant and relatively simple design
  Similar to RISC architectures developed in mid-1980’s and 90’s
  Very popular, used in many products
    Silicon Graphics, ATI, Cisco, Sony, etc.
  Comes next in sales after Intel IA-32 processors
    Almost 100 million MIPS processors sold in 2002 (and increasing)
Alternative design: Intel IA-32
  Known as Complex Instruction Set Computer (CISC)

## Slide 5: Next . . .
Instruction Set Architecture
Overview of the MIPS Processor
R-Type Arithmetic, Logical, and Shift Instructions
I-Type Format and Immediate Constants
Jump and Branch Instructions
Translating If Statements and Boolean Expressions
Load and Store Instructions
Translating Loops and Traversing Arrays
Addressing Modes

## Slide 6: Overview of the MIPS Processor
Memory
Up to 232 bytes = 230 words
4 bytes per word
$0
$1
$2
$31
Hi
Lo
ALU
F0
F1
F2
F31
FP
Arith
EPC
Cause
BadVaddr
Status
EIU
FPU
TMU
Execution &
Integer Unit
(Main proc)
Floating
Point Unit
(Coproc 1)
Trap &
Memory Unit
(Coproc 0)
. . .
. . .
Integer
mul/div
Arithmetic &
Logic Unit
32 General
Purpose
Registers
Integer Multiplier/Divider
32 Floating-Point
Registers
Floating-Point
Arithmetic Unit

## Slide 7: MIPS General-Purpose Registers
32 General Purpose Registers (GPRs)
  Assembler uses the dollar notation to name registers
    $0 is register 0, $1 is register 1, …, and $31 is register 31
  All registers are 32-bit wide in MIPS32
  Register $0 is always zero
    Any value written to $0 is discarded
Software conventions
  Software defines names to all registers
    To standardize their use in programs
  Example: $8 - $15 are called $t0 - $t7
    Used for temporary values
$0 = $zero
$1 = $at
$2 = $v0
$3 = $v1
$4 = $a0
$5 = $a1
$6 = $a2
$7 = $a3
$8 = $t0
$9 = $t1
$10 = $t2
$11 = $t3
$12 = $t4
$13 = $t5
$14 = $t6
$15 = $t7
$16 = $s0
$17 = $s1
$18 = $s2
$19 = $s3
$20 = $s4
$21 = $s5
$22 = $s6
$23 = $s7
$24 = $t8
$25 = $t9
$26 = $k0
$27 = $k1
$28 = $gp
$29 = $sp
$30 = $fp
$31 = $ra

## Slide 8: MIPS Register Conventions
Name | Register | Usage
$zero | $0 | Always 0 (forced by hardware)
$at | $1 | Reserved for assembler use
$v0 – $v1 | $2 – $3 | Result values of a function
$a0 – $a3 | $4 – $7 | Arguments of a function
$t0 – $t7 | $8 – $15 | Temporary Values
$s0 – $s7 | $16 – $23 | Saved registers (preserved across call)
$t8 – $t9 | $24 – $25 | More temporaries
$k0 – $k1 | $26 – $27 | Reserved for OS kernel
$gp | $28 | Global pointer (points to global data)
$sp | $29 | Stack pointer (points to top of stack)
$fp | $30 | Frame pointer (points to stack frame)
$ra | $31 | Return address (used by jal for function call)
Assembler can refer to registers by name or by number
  It is easier for you to remember registers by name
  Assembler converts register name to its corresponding number

## Slide 9: Instruction Formats
All instructions are 32-bit wide. Three instruction formats:
Register (R-Type)
  Register-to-register instructions
  Op: operation code specifies the format of the instruction
Immediate (I-Type)
  16-bit immediate constant is part in the instruction
Jump (J-Type)
  Used by jump instructions
Op6
Rs5
Rt5
Rd5
funct6
sa5
Op6
Rs5
Rt5
immediate16
Op6
immediate26

## Slide 10: Instruction Categories
Integer Arithmetic
  Arithmetic, logical, and shift instructions
Data Transfer
  Load and store instructions that access memory
  Data movement and conversions
Jump and Branch
  Flow-control instructions that alter the sequential sequence
Floating Point Arithmetic
  Instructions that operate on floating-point registers
Miscellaneous
  Instructions that transfer control to/from exception handlers
  Memory management instructions

## Slide 11: Next . . .
Instruction Set Architecture
Overview of the MIPS Processor
R-Type Arithmetic, Logical, and Shift Instructions
I-Type Format and Immediate Constants
Jump and Branch Instructions
Translating If Statements and Boolean Expressions
Load and Store Instructions
Translating Loops and Traversing Arrays
Addressing Modes

## Slide 12: R-Type Format
Op: operation code (opcode)
  Specifies the operation of the instruction
  Also specifies the format of the instruction
funct: function code – extends the opcode
  Up to 26 = 64 functions can be defined for the same opcode
  MIPS uses opcode 0 to define R-type instructions
Three Register Operands (common to many instructions)
  Rs, Rt: first and second source operands
  Rd: destination operand
  sa: the shift amount used by shift instructions
Op6
Rs5
Rt5
Rd5
funct6
sa5

## Slide 13: Integer Add /Subtract Instructions
Instruction | Meaning | R-Type Format |  |  |  |  | 
add $s1, $s2, $s3 | $s1 = $s2 + $s3 | op = 0 | rs = $s2 | rt = $s3 | rd = $s1 | sa = 0 | f = 0x20
addu $s1, $s2, $s3 | $s1 = $s2 + $s3 | op = 0 | rs = $s2 | rt = $s3 | rd = $s1 | sa = 0 | f = 0x21
sub $s1, $s2, $s3 | $s1 = $s2 – $s3 | op = 0 | rs = $s2 | rt = $s3 | rd = $s1 | sa = 0 | f = 0x22
subu $s1, $s2, $s3 | $s1 = $s2 – $s3 | op = 0 | rs = $s2 | rt = $s3 | rd = $s1 | sa = 0 | f = 0x23
add & sub: overflow causes an arithmetic exception
  In case of overflow, result is not written to destination register
addu & subu: same operation as add & sub
  However, no arithmetic exception can occur
  Overflow is ignored
Many programming languages ignore overflow
  The + operator is translated into addu
  The – operator is translated into subu

## Slide 14: Addition/Subtraction Example
Consider the translation of: f = (g+h) – (i+j)
Compiler allocates registers to variables
  Assume that f, g, h, i, and j are allocated registers $s0 thru $s4
  Called the saved registers: $s0 = $16, $s1 = $17, …, $s7 = $23
Translation of: f = (g+h) – (i+j)
addu $t0, $s1, $s2 # $t0 = g + h
addu $t1, $s3, $s4 # $t1 = i + j
subu $s0, $t0, $t1 # f = (g+h)–(i+j)
  Temporary results are stored in $t0 = $8 and $t1 = $9
Translate: addu $t0,$s1,$s2 to binary code
Solution:
000000
op
10001
rs = $s1
10010
rt = $s2
01000
rd = $t0
00000
sa
100001
func

## Slide 15: Logical Bitwise Operations
Logical bitwise operations: and, or, xor, nor
AND instruction is used to clear bits: x and 0 = 0
OR instruction is used to set bits: x or 1 = 1
XOR instruction is used to toggle bits: x xor 1 = not x
NOR instruction can be used as a NOT, how?
  nor $s1,$s2,$s2 is equivalent to not $s1,$s2
x
0
0
1
1
y
0
1
0
1
x and y
0
0
0
1
x
0
0
1
1
y
0
1
0
1
x or y
0
1
1
1
x
0
0
1
1
y
0
1
0
1
x xor y
0
1
1
0
x
0
0
1
1
y
0
1
0
1
x nor y
1
0
0
0

## Slide 16: Logical Bitwise Instructions
Instruction | Meaning | R-Type Format |  |  |  |  | 
and $s1, $s2, $s3 | $s1 = $s2 & $s3 | op = 0 | rs = $s2 | rt = $s3 | rd = $s1 | sa = 0 | f = 0x24
or $s1, $s2, $s3 | $s1 = $s2 ¦ $s3 | op = 0 | rs = $s2 | rt = $s3 | rd = $s1 | sa = 0 | f = 0x25
xor $s1, $s2, $s3 | $s1 = $s2 ^ $s3 | op = 0 | rs = $s2 | rt = $s3 | rd = $s1 | sa = 0 | f = 0x26
nor $s1, $s2, $s3 | $s1 = ~($s2¦$s3) | op = 0 | rs = $s2 | rt = $s3 | rd = $s1 | sa = 0 | f = 0x27
Examples:
Assume $s1 = 0xabcd1234 and $s2 = 0xffff0000
and $s0,$s1,$s2
# $s0 = 0xabcd0000
or $s0,$s1,$s2
# $s0 = 0xffff1234
xor $s0,$s1,$s2
# $s0 = 0x54321234
nor $s0,$s1,$s2
# $s0 = 0x0000edcb

## Slide 17: Shift Operations
Shifting is to move all the bits in a register left or right
Shifts by a constant amount: sll, srl, sra
  sll/srl mean shift left/right logical by a constant amount
  The 5-bit shift amount field is used by these instructions
  sra means shift right arithmetic by a constant amount
  The sign-bit (rather than 0) is shifted from the left
shift-in 0
. . .
shift-out MSB
sll
32-bit register
. . .
shift-in 0
shift-out LSB
srl
. . .
shift-in sign-bit
shift-out LSB
sra

## Slide 18: Shift Instructions
$s1 = 0x0000abcd
$s1 = 0xcd123400
Instruction | Meaning | R-Type Format |  |  |  |  | 
sll $s1,$s2,10 | $s1 = $s2 << 10 | op = 0 | rs = 0 | rt = $s2 | rd = $s1 | sa = 10 | f = 0
srl $s1,$s2,10 | $s1 = $s2>>>10 | op = 0 | rs = 0 | rt = $s2 | rd = $s1 | sa = 10 | f = 2
sra $s1, $s2, 10 | $s1 = $s2 >> 10 | op = 0 | rs = 0 | rt = $s2 | rd = $s1 | sa = 10 | f = 3
sllv $s1,$s2,$s3 | $s1 = $s2 << $s3 | op = 0 | rs = $s3 | rt = $s2 | rd = $s1 | sa = 0 | f = 4
srlv $s1,$s2,$s3 | $s1 = $s2>>>$s3 | op = 0 | rs = $s3 | rt = $s2 | rd = $s1 | sa = 0 | f = 6
srav $s1,$s2,$s3 | $s1 = $s2 >> $s3 | op = 0 | rs = $s3 | rt = $s2 | rd = $s1 | sa = 0 | f = 7
Shifts by a variable amount: sllv, srlv, srav
  Same as sll, srl, sra, but a register is used for shift amount
Examples: assume that $s2 = 0xabcd1234, $s3 = 16
sll $s1,$s2,8
sra $s1,$s2,4
$s1 = 0xfabcd123
srlv $s1,$s2,$s3
rt=$s2=10010
op=000000
rs=$s3=10011
rd=$s1=10001
sa=00000
f=000110
$s1 = $s2<<8
$s1 = $s2>>4
$s1 = $s2>>>$s3

## Slide 19: Binary Multiplication
Shift-left (sll) instruction can perform multiplication
  When the multiplier is a power of 2
You can factor any binary number into powers of 2
  Example: multiply $s1 by 36
    Factor 36 into (4 + 32) and use distributive property of multiplication
  $s2 = $s1*36 = $s1*(4 + 32) = $s1*4 + $s1*32
sll $t0, $s1, 2 ; $t0 = $s1 * 4
sll $t1, $s1, 5 ; $t1 = $s1 * 32
addu $s2, $t0, $t1 ; $s2 = $s1 * 36

## Slide 20: Your Turn . . .
sll $t0, $s1, 1 ; $t0 = $s1 * 2
sll $t1, $s1, 3 ; $t1 = $s1 * 8
addu $s2, $t0, $t1 ; $s2 = $s1 * 10
sll $t0, $s1, 4 ; $t0 = $s1 * 16
addu $s2, $s2, $t0 ; $s2 = $s1 * 26
Multiply $s1 by 26, using shift and add instructions
Hint: 26 = 2 + 8 + 16
Multiply $s1 by 31, Hint: 31 = 32 – 1
sll $s2, $s1, 5 ; $s2 = $s1 * 32
subu $s2, $s2, $s1 ; $s2 = $s1 * 31

## Slide 21: Next . . .
Instruction Set Architecture
Overview of the MIPS Processor
R-Type Arithmetic, Logical, and Shift Instructions
I-Type Format and Immediate Constants
Jump and Branch Instructions
Translating If Statements and Boolean Expressions
Load and Store Instructions
Translating Loops and Traversing Arrays
Addressing Modes

## Slide 22: I-Type Format
Constants are used quite frequently in programs
  The R-type shift instructions have a 5-bit shift amount constant
  What about other instructions that need a constant?
I-Type: Instructions with Immediate Operands
16-bit immediate constant is stored inside the instruction
  Rs is the source register number
  Rt is now the destination register number (for R-type it was Rd)
Examples of I-Type ALU Instructions:
  Add immediate: addi $s1, $s2, 5 # $s1 = $s2 + 5
  OR immediate: ori $s1, $s2, 5 # $s1 = $s2 | 5
Op6
Rs5
Rt5
immediate16

## Slide 23: I-Type ALU Instructions
Instruction | Meaning | I-Type Format |  |  | 
addi $s1, $s2, 10 | $s1 = $s2 + 10 | op = 0x8 | rs = $s2 | rt = $s1 | imm16 = 10
addiu $s1, $s2, 10 | $s1 = $s2 + 10 | op = 0x9 | rs = $s2 | rt = $s1 | imm16 = 10
andi $s1, $s2, 10 | $s1 = $s2 & 10 | op = 0xc | rs = $s2 | rt = $s1 | imm16 = 10
ori $s1, $s2, 10 | $s1 = $s2 ¦ 10 | op = 0xd | rs = $s2 | rt = $s1 | imm16 = 10
xori $s1, $s2, 10 | $s1 = $s2 ^ 10 | op = 0xe | rs = $s2 | rt = $s1 | imm16 = 10
lui $s1, 10 | $s1 = 10 << 16 | op = 0xf | 0 | rt = $s1 | imm16 = 10
addi: overflow causes an arithmetic exception
  In case of overflow, result is not written to destination register
addiu: same operation as addi but overflow is ignored
Immediate constant for addi and addiu is signed
  No need for subi or subiu instructions
Immediate constant for andi, ori, xori is unsigned

## Slide 24: Examples: I-Type ALU Instructions
Examples: assume A, B, C are allocated $s0, $s1, $s2
No need for subi, because addi has signed immediate
Register 0 ($zero) has always the value 0
A = B+5; translated as
C = B–1; translated as
addiu $s0,$s1,5
addiu $s2,$s1,-1
A = B&0xf; translated as
C = B|0xf; translated as
andi $s0,$s1,0xf
ori $s2,$s1,0xf
C = 5; translated as
A = B; translated as
ori $s2,$zero,5
ori $s0,$s1,0
rt=$s2=10010
op=001001
rs=$s1=10001
imm = -1 = 1111111111111111

## Slide 25: 32-bit Constants
I-Type instructions can have only 16-bit constants
What if we want to load a 32-bit constant into a register?
Can’t have a 32-bit constant in I-Type instructions 
  We have already fixed the sizes of all instructions to 32 bits
Solution: use two instructions instead of one 
  Suppose we want: $s1=0xAC5165D9 (32-bit constant)
  lui: load upper immediate
Op6
Rs5
Rt5
immediate16
lui $s1,0xAC51
ori $s1,$s1,0x65D9
0xAC51
0x65D9
$s1=$17
0xAC51
0x0000
$s1=$17
clear lower
16 bits
load upper
16 bits

## Slide 26: Next . . .
Instruction Set Architecture
Overview of the MIPS Processor
R-Type Arithmetic, Logical, and Shift Instructions
I-Type Format and Immediate Constants
Jump and Branch Instructions
Translating If Statements and Boolean Expressions
Load and Store Instructions
Translating Loops and Traversing Arrays
Addressing Modes

## Slide 27: J-Type Format
J-type format is used for unconditional jump instruction:
j label # jump to label
. . .
label:
26-bit immediate value is stored in the instruction
  Immediate constant specifies address of target instruction
Program Counter (PC) is modified as follows:
  Next PC =
  Upper 4 most significant bits of PC are unchanged
Op6
immediate26
immediate26
PC4
00
least-significant 2 bits are 00

## Slide 28: Conditional Branch Instructions
MIPS compare and branch instructions:
beq Rs,Rt,label branch to label if (Rs == Rt)
bne Rs,Rt,label branch to label if (Rs != Rt)
MIPS compare to zero & branch instructions
Compare to zero is used frequently and implemented efficiently
bltz Rs,label branch to label if (Rs < 0)
bgtz Rs,label branch to label if (Rs > 0)
blez Rs,label branch to label if (Rs <= 0)
bgez Rs,label branch to label if (Rs >= 0)
No need for beqz and bnez instructions. Why?

## Slide 29: Set on Less Than Instructions
MIPS also provides set on less than instructions
slt rd,rs,rt if (rs < rt) rd = 1 else rd = 0
sltu rd,rs,rt unsigned <
slti rt,rs,im16 if (rs < im16) rt = 1 else rt = 0
sltiu rt,rs,im16 unsigned <
Signed / Unsigned Comparisons
Can produce different results
Assume $s0 = 1 and $s1 = -1 = 0xffffffff
slt $t0,$s0,$s1 results in $t0 = 0
sltu $t0,$s0,$s1 results in $t0 = 1

## Slide 30: More on Branch Instructions
MIPS hardware does NOT provide instructions for …
blt, bltu branch if less than (signed/unsigned)
ble, bleu branch if less or equal (signed/unsigned)
bgt, bgtu branch if greater than (signed/unsigned)
bge, bgeu branch if greater or equal (signed/unsigned)
Can be achieved with a sequence of 2 instructions
How to implement: blt $s0,$s1,label
Solution: slt $at,$s0,$s1
bne $at,$zero,label
How to implement: ble $s2,$s3,label
Solution: slt $at,$s3,$s2
beq $at,$zero,label

## Slide 31: Pseudo-Instructions
Introduced by assembler as if they were real instructions
  To facilitate assembly language programming
Assembler reserves $at = $1 for its own use
  $at is called the assembler temporary register
ori $s1, $zero, 0xabcd
li $s1, 0xabcd
slt $s1, $s3, $s2
sgt $s1, $s2, $s3
nor $s1, $s2, $zero
not $s1, $s2
slt $at, $s1, $s2
bne $at, $zero, label
blt $s1, $s2, label
lui $at, 0xabcd
ori $s1, $at, 0x1234
li $s1, 0xabcd1234
addu $s1, $zero, $s2
move $s1, $s2
Conversion to Real Instructions
Pseudo-Instructions

## Slide 32: Jump, Branch, and SLT Instructions
Instruction | Meaning | Format |  |  | 
j label | jump to label | op6 = 2 | imm26 |  | 
beq rs, rt, label | branch if (rs == rt) | op6 = 4 | rs5 | rt5 | imm16
bne rs, rt, label | branch if (rs != rt) | op6 = 5 | rs5 | rt5 | imm16
blez rs, label | branch if (rs<=0) | op6 = 6 | rs5 | 0 | imm16
bgtz rs, label | branch if (rs > 0) | op6 = 7 | rs5 | 0 | imm16
bltz rs, label | branch if (rs < 0) | op6 = 1 | rs5 | 0 | imm16
bgez rs, label | branch if (rs>=0) | op6 = 1 | rs5 | 1 | imm16
Instruction | Meaning | Format |  |  |  |  | 
slt rd, rs, rt | rd=(rs<rt?1:0) | op6 = 0 | rs5 | rt5 | rd5 | 0 | 0x2a
sltu rd, rs, rt | rd=(rs<rt?1:0) | op6 = 0 | rs5 | rt5 | rd5 | 0 | 0x2b
slti rt, rs, imm16 | rt=(rs<imm?1:0) | 0xa | rs5 | rt5 | imm16 |  | 
sltiu rt, rs, imm16 | rt=(rs<imm?1:0) | 0xb | rs5 | rt5 | imm16 |  | 

## Slide 33: Next . . .
Instruction Set Architecture
Overview of the MIPS Processor
R-Type Arithmetic, Logical, and Shift Instructions
I-Type Format and Immediate Constants
Jump and Branch Instructions
Translating If Statements and Boolean Expressions
Load and Store Instructions
Translating Loops and Traversing Arrays
Addressing Modes

## Slide 34: Translating an IF Statement
Consider the following IF statement:
if (a == b) c = d + e; else c = d – e;
Assume that a, b, c, d, e are in $s0, …, $s4 respectively
How to translate the above IF statement?
bne $s0, $s1, else
addu $s2, $s3, $s4
j exit
else: subu $s2, $s3, $s4
exit: . . .

## Slide 35: Compound Expression with AND
Programming languages use short-circuit evaluation
If first expression is false, second expression is skipped
if (($s1 > 0) && ($s2 < 0)) {$s3++;}
# One Possible Implementation ...
bgtz $s1, L1 # first expression
j next # skip if false
L1: bltz $s2, L2 # second expression
j next # skip if false
L2: addiu $s3,$s3,1 # both are true
next:

## Slide 36: Better Implementation for AND
The following implementation uses less code
Reverse the relational operator
Allow the program to fall through to the second expression
Number of instructions is reduced from 5 to 3
if (($s1 > 0) && ($s2 < 0)) {$s3++;}
# Better Implementation ...
blez $s1, next # skip if false
bgez $s2, next # skip if false
addiu $s3,$s3,1 # both are true
next:

## Slide 37: Compound Expression with OR
Short-circuit evaluation for logical OR
If first expression is true, second expression is skipped
Use fall-through to keep the code as short as possible
bgt, ble, and li are pseudo-instructions
  Translated by the assembler to real instructions
if (($sl > $s2) || ($s2 > $s3)) {$s4 = 1;}
bgt $s1, $s2, L1 # yes, execute if part
ble $s2, $s3, next # no: skip if part
L1: li $s4, 1 # set $s4 to 1
next:

## Slide 38: Your Turn . . .
Translate the IF statement to assembly language
$s1 and $s2 values are unsigned
$s3, $s4, and $s5 values are signed
  bgtu $s1, $s2, next
  move $s3, $s4
next:
if( $s1 <= $s2 ) {
$s3 = $s4
}
if (($s3 <= $s4) &&
($s4 > $s5)) {
$s3 = $s4 + $s5
}
  bgt $s3, $s4, next
  ble $s4, $s5, next
  addu $s3, $s4, $s5
next:

## Slide 39: Next . . .
Instruction Set Architecture
Overview of the MIPS Processor
R-Type Arithmetic, Logical, and Shift Instructions
I-Type Format and Immediate Constants
Jump and Branch Instructions
Translating If Statements and Boolean Expressions
Load and Store Instructions
Translating Loops and Traversing Arrays
Addressing Modes

## Slide 40: Load and Store Instructions
Instructions that transfer data between memory & registers
Programs include variables such as arrays and objects
Such variables are stored in memory
Load Instruction:
  Transfers data from memory to a register
Store Instruction:
  Transfers data from a register to memory
Memory address must be specified by load and store
Memory
Registers
load
store

## Slide 41: Load and Store Word
Load Word Instruction (Word = 4 bytes in MIPS)
lw Rt, imm16(Rs) # Rt = MEMORY[Rs+imm16]
Store Word Instruction
sw Rt, imm16(Rs) # MEMORY[Rs+imm16] = Rt
Base or Displacement addressing is used
  Memory Address = Rs (base) + Immediate16 (displacement)
  Immediate16 is sign-extended to have a signed displacement
Op6
Rs5
Rt5
immediate16
Base or Displacement Addressing
Memory Word
Base address
+

## Slide 42: Example on Load & Store
Translate A[1] = A[2] + 5 (A is an array of words)
  Assume that address of array A is stored in register $s0
  lw $s1, 8($s0) # $s1 = A[2]
  addiu $s2, $s1, 5 # $s2 = A[2] + 5
  sw $s2, 4($s0) # A[1] = $s2
Index of A[2] and A[1] should be multiplied by 4. Why?
sw
Memory
A[1]
A[0]
A[2]
A[3]
. . .
. . .
A+12
A+8
A+4
A
Registers
address of A
$s0 = $16
value of A[2]
$s1 = $17
A[2] + 5
$s2 = $18
. . .
. . .
lw

## Slide 43: Load and Store Byte and Halfword
0
0
s
s
s
s
s
0
0
s
bu
b
h
hu
sign – extend
zero – extend
sign – extend
zero – extend
32-bit Register
The MIPS processor supports the following data formats:
  Byte = 8 bits, Halfword = 16 bits, Word = 32 bits
Load & store instructions for bytes and halfwords
  lb = load byte, lbu = load byte unsigned, sb = store byte
  lh = load half, lhu = load half unsigned, sh = store halfword
Load expands a memory data to fit into a 32-bit register
Store reduces a 32-bit register to fit in memory

## Slide 44: Load and Store Instructions
Instruction | Meaning | I-Type Format |  |  | 
lb rt, imm16(rs) | rt = MEM[rs+imm16] | 0x20 | rs5 | rt5 | imm16
lh rt, imm16(rs) | rt = MEM[rs+imm16] | 0x21 | rs5 | rt5 | imm16
lw rt, imm16(rs) | rt = MEM[rs+imm16] | 0x23 | rs5 | rt5 | imm16
lbu rt, imm16(rs) | rt = MEM[rs+imm16] | 0x24 | rs5 | rt5 | imm16
lhu rt, imm16(rs) | rt = MEM[rs+imm16] | 0x25 | rs5 | rt5 | imm16
sb rt, imm16(rs) | MEM[rs+imm16] = rt | 0x28 | rs5 | rt5 | imm16
sh rt, imm16(rs) | MEM[rs+imm16] = rt | 0x29 | rs5 | rt5 | imm16
sw rt, imm16(rs) | MEM[rs+imm16] = rt | 0x2b | rs5 | rt5 | imm16
Base or Displacement Addressing is used
  Memory Address = Rs (base) + Immediate16 (displacement)
Two variations on base addressing
  If Rs = $zero = 0 then Address = Immediate16 (absolute)
  If Immediate16 = 0 then Address = Rs (register indirect)

## Slide 45: Next . . .
Instruction Set Architecture
Overview of the MIPS Processor
R-Type Arithmetic, Logical, and Shift Instructions
I-Type Format and Immediate Constants
Jump and Branch Instructions
Translating If Statements and Boolean Expressions
Load and Store Instructions
Translating Loops and Traversing Arrays
Addressing Modes

## Slide 46: Translating a WHILE Loop
Consider the following WHILE statement:
i = 0; while (A[i] != k) i = i+1;
Where A is an array of integers (4 bytes per element)
Assume address A, i, k in $s0, $s1, $s2, respectively
How to translate above WHILE statement?
xor $s1, $s1, $s1 # i = 0
move $t0, $s0 # $t0 = address A
loop: lw $t1, 0($t0) # $t1 = A[i]
beq $t1, $s2, exit # exit if (A[i]== k)
addiu $s1, $s1, 1 # i = i+1
sll $t0, $s1, 2 # $t0 = 4*i
addu $t0, $s0, $t0 # $t0 = address A[i]
j loop
exit: . . .
Memory
A[2]
A[i]
A[1]
A[0]
. . .
. . .
A
A+4
A+8
A+4×i
. . .

## Slide 47: Using Pointers to Traverse Arrays
Consider the same WHILE loop:
i = 0; while (A[i] != k) i = i+1;
Where address of A, i, k are in $s0, $s1, $s2, respectively
We can use a pointer to traverse array A
Pointer is incremented by 4 (faster than indexing)
xor $s1, $s1, $s1 # i = 0
move $t0, $s0 # $t0 = $s0 = addr A
j cond # test condition
loop: addiu $s1, $s1, 1 # i = i+1
addiu $t0, $t0, 4 # point to next
cond: lw $t1, 0($t0) # $t1 = A[i]
bne $t1, $s2, loop # loop if A[i]!= k
Only 4 instructions (rather than 6) in loop body

## Slide 48: Copying a String
move $t0, $s0 # $t0 = pointer to source
move $t1, $s1 # $t1 = pointer to target
L1: lb $t2, 0($t0) # load byte into $t2
sb $t2, 0($t1) # store byte into target
addiu $t0, $t0, 1 # increment source pointer
addiu $t1, $t1, 1 # increment target pointer
bne $t2, $zero, L1 # loop until NULL char
The following code copies source string to target string
Address of source in $s0 and address of target in $s1
Strings are terminated with a null character (C strings)
i = 0;
do {t=source[i]; target[i]=t; i++;} while (t!=0);

## Slide 49: Summing an Integer Array
  move $t0, $s0 # $t0 = address A[i]
  xor $t1, $t1, $t1 # $t1 = i = 0
  xor $s2, $s2, $s2 # $s2 = sum = 0
L1: lw $t2, 0($t0) # $t2 = A[i]
  addu $s2, $s2, $t2 # sum = sum + A[i]
  addiu $t0, $t0, 4 # point to next A[i]
  addiu $t1, $t1, 1 # i++
bne $t1, $s1, L1 # loop if (i != n)
Assume $s0 = array address, $s1 = array length = n
sum = 0;
for (i=0; i<n; i++) sum = sum + A[i];

## Slide 50: Next . . .
Instruction Set Architecture
Overview of the MIPS Processor
R-Type Arithmetic, Logical, and Shift Instructions
I-Type Format and Immediate Constants
Jump and Branch Instructions
Translating If Statements and Boolean Expressions
Load and Store Instructions
Translating Loops and Traversing Arrays
Addressing Modes

## Slide 51: Addressing Modes
Op6
Rs5
Rt5
immediate16
Base or Displacement Addressing
Word
Operand is in memory (load/store)
Register = Base address
+
Halfword
Byte
Op6
Rs5
Rt5
immediate16
Immediate Addressing
Operand is a constant
Op6
Rs5
Rt5
Rd5
funct6
sa5
Register Addressing
Register
Operand is in a register
Where are the operands?
How memory addresses are computed?

## Slide 52: Branch / Jump Addressing Modes
Used for branching (beq, bne, …)
Word = Target Instruction
Op6
Rs5
Rt5
immediate16
PC-Relative Addressing
PC30
00
+1
Target Instruction Address
PC = PC + 4 × (1 + immediate16)
PC30 + immediate16 + 1
00
immediate26
PC4
00
Target Instruction Address
Word = Target Instruction
immediate26
Op6
Pseudo-direct Addressing
PC26
:
00
Used by jump instruction
PC4

## Slide 53: Jump and Branch Limits
Jump Address Boundary = 226 instructions = 256 MB
  Text segment cannot exceed 226 instructions or 256 MB
  Upper 4 bits of PC are unchanged
Branch Address Boundary
  Branch instructions use I-Type format (16-bit immediate constant)
  PC-relative addressing:
    Target instruction address = PC + 4×(1 + immediate16)
    During assembly: immediate=(Target address – (PC+4))/4, where PC contains address of current instruction
immediate26
PC4
00
Target Instruction Address
PC30 + immediate16 + 1
00

## Slide 54: Jump and Branch Limits
    During execution, PC contains the address of current instruction (thus we add 1 to immediate16).
    Maximum branch limit is -215 to +215-1 instructions.
    If immediate is positive => Forward Jump
    If immediate is negative => Backward Jump
Example
0
Again:4
8 beq $s1,$s2,Next
12
16 bne $s1,$zero,Again
Next: 20
Forward Jump
During assembly:
Immediate=(Next-(PC+4))/4=(20-12)/4=2
During execution:
PC=PC+4*(immediate+1)=8+4*(3)=20
Backward Jump
During assembly:
Immediate=(Again-(PC+4))/4=(4-20)/4=-4
During execution:
PC=PC+4*(immediate+1)=16+4*(-3)=4

## Slide 55: Summary of RISC Design
All instructions are typically of one size
Few instruction formats
All operations on data are register to register
  Operands are read from registers
  Result is stored in a register
General purpose integer and floating point registers
  Typically, 32 integer and 32 floating-point registers
Memory access only via load and store instructions
  Load and store: bytes, half words, words, and double words
Few simple addressing modes

## Slide 56: Four Design Principles
Simplicity favors regularity
  Fix the size of instructions (simplifies fetching & decoding)
  Fix the number of operands per instruction
    Three operands is the natural number for a typical instruction
Smaller is faster
  Limit the number of registers for faster access (typically 32)
Make the common case fast
  Include constants inside instructions (faster than loading them)
  Design most instructions to be register-to-register
Good design demands good compromises
  Fixed-size instructions compromise the size of constants