## Slide 1: Integer Multiplication and Division
ICS 233
Computer Architecture and Assembly Language
Dr. Aiman El-Maleh
College of Computer Sciences and Engineering
King Fahd University of Petroleum and Minerals
[Adapted from slides of Dr. M. Mudawar, ICS 233, KFUPM]

## Slide 2: Presentation Outline
Unsigned Integer Multiplication
Signed Integer Multiplication
Faster Integer Multiplication
Integer Division
Integer Multiplication and Division in MIPS

## Slide 3: Unsigned Multiplication
Paper and Pencil Example:
Multiplicand 11002 = 12
Multiplier × 11012 = 13
1100
0000
1100
1100
Product 100111002 = 156
m-bit multiplicand × n-bit multiplier = (m+n)-bit product
Accomplished via shifting and addition
Binary multiplication is easy
0 × multiplicand = 0
1 × multiplicand = multiplicand

## Slide 4: Multiply Hardware
Instead of shifting multiplicand to left, shift the product to the right
Initialize LO = Multiplier, HI=0
Product = HI and LO registers
= 0
Start
LO[0]?
HI = HI + Multiplicand
32nd Repetition?
Done
= 1
No
Yes
LO=Multiplier, HI=0
Shift Product = (HI,LO) Right 1 bit
32-bit ALU
Control
64 bits
32 bits
write
add
LO[0]
Multiplicand
shift right
32 bits
HI
LO
32 bits
carry

## Slide 5: Multiply Example
Consider: 11002 × 11012, Product = 100111002 (156)
4-bit multiplicand and multiplier are used in this example
4-bit adder produces a 5-bit sum (with carry)
1 1 0 0
Shift Right Product = (HI, LO)
0 1 1 1 1 0 0 1
LO[0] = 0 => Do Nothing
1 1 0 0
Shift Right Product = (HI, LO)
0 0 1 1 0 0 1 1
1 1 0 0
Shift Right Product = (HI, LO)
0 1 1 0 0 1 1 0
1 1 0 0
Shift Right Product = (HI, LO)
1 0 0 1 1 1 0 0
2
1 1 0 0
0 0 0 0 1 1 0 1
Initialize (LO = Multiplier, HI=0)
0
1
3
4
Multiplicand
Product = HI, LO
Carry
Iteration
0
1 1 0 0 1 1 0 1
LO[0] = 1 => ADD
+
0
1 1 1 1 0 0 1 1
LO[0] = 1 => ADD
+
1
0 0 1 1 1 0 0 1
LO[0] = 1 => ADD
+

## Slide 6: Next . . .
Unsigned Integer Multiplication
Signed Integer Multiplication
Faster Integer Multiplication
Integer Division
Integer Multiplication and Division in MIPS

## Slide 7: Signed Multiplication
So far, we have dealt with unsigned integer multiplication
Version 1 of Signed Multiplication
  Convert multiplier and multiplicand into positive numbers
    If negative then obtain the 2's complement and remember the sign
  Perform unsigned multiplication
  Compute the sign of the product
  If product sign < 0 then obtain the 2's complement of the product
Refined Version:
  Use the unsigned multiplication hardware
  When shifting right, extend the sign of the product
  If multiplier is negative, the last step should be a subtract

## Slide 8: Signed Multiplication (Pencil & Paper)
Case 1: Positive Multiplier
Multiplicand 11002 = -4
Multiplier × 01012 = +5
11111100
111100
Product 111011002 = -20
Case 2: Negative Multiplier
Multiplicand 11002 = -4
Multiplier × 11012 = -3
11111100
111100
00100 (2's complement of 1100)
Product 000011002 = +12
Sign-extension
Sign-extension

## Slide 9: Sequential Signed Multiplier
ALU produces 32-bit result + Sign bit
Sign bit set as follows:
  No overflow  Extend sign-bit of result
  Overflow  Invert sign-bit of result
= 0
Start
LO[0]?
First 31 iterations: HI = HI + Multiplicand
Last iteration: HI = HI – Multiplicand
32nd Repetition?
Done
= 1
No
Yes
HI = 0, LO = Multiplier
Shift Right (Sign, HI, LO) 1 bit
32-bit ALU
Control
64 bits
32 bits
write
add, sub
LO[0]
Multiplicand
shift right
32 bits
HI
LO
32 bits
Sign

## Slide 10: Signed Multiplication Example
Consider: 11002 (-4) × 11012 (-3), Product = 000011002
Check for overflow: No overflow  Extend sign bit
Last iteration: add 2's complement of Multiplicand
1 1 0 0
Shift (Sign, HI, LO) right 1 bit
1 1 0 1 1 0 0 1
LO[0] = 0 => Do Nothing
1 1 0 0
Shift (Sign, HI, LO) right 1 bit
1 1 1 1 0 0 1 1
1 1 0 0
Shift (Sign, HI, LO) right 1 bit
1 1 1 0 0 1 1 0
Shift (Sign, HI, LO) right 1 bit
0 0 0 0 1 1 0 0
2
1 1 0 0
0 0 0 0 1 1 0 1
Initialize (HI = 0, LO = Multiplier)
0
1
3
4
Multiplicand
Product = HI, LO
Sign
Iteration
1
1 1 0 0 1 1 0 1
LO[0] = 1 => ADD
+
1
1 0 1 1 0 0 1 1
LO[0] = 1 => ADD
+
0 1 0 0
0
0 0 0 1 1 0 0 1
LO[0] = 1 => SUB (ADD 2's compl)
+

## Slide 11: Signed Multiplication Example
Consider: 10102 (-6) × 11112 (-1),
Product = 000001102 (+6)
1 0 1 0
Shift (Sign, HI, LO) right 1 bit
1 0 1 0 1 1 0 1
LO[0] = 1 => ADD
1 0 1 0
Shift (Sign, HI, LO) right 1 bit
1 0 1 1 1 0 1 1
1 0 1 0
Shift (Sign, HI, LO) right 1 bit
1 1 0 1 0 1 1 1
Shift (Sign, HI, LO) right 1 bit
0 0 0 0 0 1 1 0
2
1 0 1 0
0 0 0 0 1 1 1 1
Initialize (HI = 0, LO = Multiplier)
0
1
3
4
Multiplicand
Product = HI, LO
Sign
Iteration
1
1 0 1 0 1 1 1 1
LO[0] = 1 => ADD
+
1
0 1 0 1 1 0 1 1
LO[0] = 1 => ADD
+
0 1 1 0
0
0 0 0 0 1 1 0 1
LO[0] = 1 => SUB (ADD 2's compl)
+
+
0 1 1 1 0 1 1 1
1

## Slide 12: Next . . .
Unsigned Multiplication
Signed Multiplication
Faster Multiplication
Unsigned Division
Signed Division
Multiplication and Division in MIPS

## Slide 13: Multiplication using Multiple Adders
32-bit adder for each bit of the multiplier
  31 adders are needed for a 32-bit multiplier
  AND multiplicand with each bit of multiplier
  Product = accumulated shifted sum
Each adder produces a 33-bit output
  Most significant bit is a carry bit
  Least significant bit is a product bit
  Upper 32 bits go to next adder
Array multiplier can be optimized
  Carry save adders reduce delays
32-bit
A
B1
32 bits
A
B0
32-bit
A
B2
32 bits
32 bits
1
33 bits
32 bits
1
33 bits
32-bit
A
B3
32 bits
32 bits
1
33 bits
32-bit
A
B31
32 bits
32 bits
1 bit
33 bits
P1
P2
P3
P31
P63..32
. .
32 bits
. . .
P0
1

## Slide 14: Multiplication Example
  Example on 4-bit numbers:
  A = a3 a2 a1 a0 and B = b3 b2 b1 b0
AND (multiply) each bit of A with each bit of B
  Requires n2 AND gates and produces n2 product bits
1001 (9) × 0101 (5)
= 0 0 1 0 1 1 0 1 (45)
4-bit
0
0000
1
4-bit
1
1001
0010
1
0100
0101
1
1011
4-bit
0
0010
1
0101
1001
0
1
1
1
1
1001
1001
1001
0100
0000
1
0
0
0
1001

## Slide 15: Carry Save Adders
Used when adding multiple numbers (as in multipliers)
All the bits of a carry-save adder work in parallel
  The carry does not propagate as in a carry-propagate adder
  This is why a carry-save is faster than a carry-propagate adder
A carry-save adder has 3 inputs and produces two outputs
  It adds 3 numbers and produces partial sum and carry bits
Carry-Propagate Adder
+
a0
b0
s0
+
a1
b1
s1
+
a31
b31
s31
. . .
cout
cin
Carry-Save Adder
. . .
+
a31
b31
s'31
c'31
c31
+
a1
b1
s'1
c'1
c1
+
a0
b0
s'0
c'0
c0

## Slide 16: Tree Multiplier
Use carry save adders to add the partial products
  Reduce the partial products to just two numbers
Add last two numbers using a carry-propagate adder
P0
+
a2b0 a1b1
+
+
+
a3b0 a2b1
a0b0
+
a1b0 a0b1
+
+
+
+
+
+
a3b1 a2b2
+
a3b2
a2b3
a3b3
a1b3
a0b3
a1b2
a0b2
P1
P2
P3
P4
P5
P6
P7
Carry Save Adder
Carry Propagate Adder

## Slide 17: Next . . .
Unsigned Integer Multiplication
Signed Integer Multiplication
Faster Integer Multiplication
Integer Division
Integer Multiplication and Division in MIPS

## Slide 18: Unsigned Division (Paper & Pencil)
Try to see how big a number can be subtracted, creating a digit of the quotient on each attempt
= 19 Quotient
Divisor 10112 110110012 = 217 Dividend
-1011
10
101
1010
10100
-1011
1001
10011
-1011
10002 = 8 Remainder
Binary division is accomplished via shifting and subtraction
Dividend =
Quotient × Divisor
+ Remainder
217 = 19 × 11 + 8
1
0
0
1
12

## Slide 19: Sequential Division
Uses two registers: HI and LO
Initialize: HI = Remainder = 0 and LO = Dividend
Shift (HI, LO) LEFT by 1 bit (also Shift Quotient LEFT)
  Shift the remainder and dividend registers together LEFT
Compute: Difference = Remainder – Divisor
If (Difference ≥ 0) then
  Remainder = Difference
  Set Least significant Bit of Quotient
Observation to Reduce Hardware:
  LO register can be also used to store the computed Quotient

## Slide 20: Sequential Division Hardware
Initialize:
  HI = 0, LO = Dividend
Results:
  HI = Remainder
  LO = Quotient
Start
Difference?
2. HI = Remainder = Difference
Set least significant bit of LO
32nd Repetition?
Done
< 0
≥ 0
No
Yes
Shift (HI, LO) Left
Difference = HI – Divisor
shift left
Divisor
32-bit ALU
LO
32 bits
write
sub
32 bits
Difference
sign
set lsb
HI
32 bits
Control

## Slide 21: Unsigned Integer Division Example
2: Diff < 0 => Do Nothing
Example: 11102 / 00112 (4-bit dividend & divisor)
Result Quotient = 01002 and Remainder = 00102
4-bit registers for Remainder and Divisor (4-bit ALU)
2: Rem = Diff, set lsb of LO
1 0 0 1
0 0 0 0
2: Diff < 0 => Do Nothing
2: Diff < 0 => Do Nothing
2
0 0 0 0
1 1 1 0
Initialize
0
1
3
4
HI
Difference
LO
Iteration
0 0 1 1
Divisor
1 1 1 0
1: Shift Left, Diff = HI - Divisor
0 0 0 1
1 1 0 0
0 0 1 1
0 0 0 0
1: Shift Left, Diff = HI - Divisor
0 0 1 1
1 0 0 0
0 0 1 1
1 1 1 0
1: Shift Left, Diff = HI - Divisor
0 0 0 1
0 0 1 0
0 0 1 1
1 1 1 1
1: Shift Left, Diff = HI - Divisor
0 0 1 0
0 1 0 0
0 0 1 1

## Slide 22: Signed Integer Division
Simplest way is to remember the signs
Convert the dividend and divisor to positive
  Obtain the 2's complement if they are negative
Do the unsigned division
Compute the signs of the quotient and remainder
  Quotient sign = Dividend sign XOR Divisor sign
  Remainder sign = Dividend sign
Negate the quotient and remainder if their sign is negative
  Obtain the 2's complement to convert them to negative

## Slide 23: Signed Integer Division Examples
Positive Dividend and Positive Divisor
  Example: +17 / +3 Quotient = +5 Remainder = +2
Positive Dividend and Negative Divisor
  Example: +17 / –3 Quotient = –5 Remainder = +2
Negative Dividend and Positive Divisor
  Example: –17 / +3 Quotient = –5 Remainder = –2
Negative Dividend and Negative Divisor
  Example: –17 / –3 Quotient = +5 Remainder = –2
The following equation must always hold:
Dividend = Quotient × Divisor + Remainder

## Slide 24: Next . . .
Unsigned Integer Multiplication
Signed Integer Multiplication
Faster Multiplication
Integer Division
Integer Multiplication and Division in MIPS

## Slide 25: Integer Multiplication in MIPS
Multiply instructions
  mult $s1,$s2 Signed multiplication
  multu $s1,$s2 Unsigned multiplication
32-bit multiplication produces a 64-bit Product
Separate pair of 32-bit registers
  HI = high-order 32-bit of product
  LO = low-order 32-bit of product
MIPS also has a special mul instruction
  mul $s0,$s1,$s2 $s0 = $s1 × $s2
  Put low-order 32 bits into destination register
  HI & LO are undefined
Multiply
Divide
$0
HI
LO
$1
.
.
$31

## Slide 26: Integer Division in MIPS
Divide instructions
  div $s1,$s2 Signed division
  divu $s1,$s2 Unsigned division
Division produces quotient and remainder
Separate pair of 32-bit registers
  HI = 32-bit remainder
  LO = 32-bit quotient
  If divisor is 0 then result is unpredictable
Moving data from HI/LO to MIPS registers
  mfhi Rd (move from HI to Rd)
  mflo Rd (move from LO to Rd)
Multiply
Divide
$0
HI
LO
$1
.
.
$31

## Slide 27: Integer Multiply/Divide Instructions
Instruction | Meaning | Format |  |  |  |  | 
mult Rs, Rt | Hi, Lo = Rs × Rt | op6 = 0 | Rs5 | Rt5 | 0 | 0 | 0x18
multu Rs, Rt | Hi, Lo = Rs × Rt | op6 = 0 | Rs5 | Rt5 | 0 | 0 | 0x19
mul Rd, Rs, Rt | Rd = Rs × Rt | 0x1c | Rs5 | Rt5 | Rd5 | 0 | 0x02
div Rs, Rt | Hi, Lo = Rs / Rt | op6 = 0 | Rs5 | Rt5 | 0 | 0 | 0x1a
divu Rs, Rt | Hi, Lo = Rs / Rt | op6 = 0 | Rs5 | Rt5 | 0 | 0 | 0x1b
mfhi Rd | Rd = Hi | op6 = 0 | 0 | 0 | Rd5 | 0 | 0x10
mflo Rd | Rd = Lo | op6 = 0 | 0 | 0 | Rd5 | 0 | 0x12
Signed arithmetic: mult, div (Rs and Rt are signed)
  LO = 32-bit low-order and HI = 32-bit high-order of multiplication
  LO = 32-bit quotient and HI = 32-bit remainder of division
Unsigned arithmetic: multu, divu (Rs and Rt are unsigned)
NO arithmetic exception can occur

## Slide 28: Integer to String Conversion
Objective: convert an unsigned 32-bit integer to a string
How to obtain the decimal digits of the number?
  Divide the number by 10, Remainder = decimal digit (0 to 9)
  Convert decimal digit into its ASCII representation ('0' to '9')
  Repeat the division until the quotient becomes zero
  Digits are computed backwards from least to most significant
Example: convert 2037 to a string
  Divide 2037/10 quotient = 203 remainder = 7 char = '7'
  Divide 203/10 quotient = 20 remainder = 3 char = '3'
  Divide 20/10 quotient = 2 remainder = 0 char = '0'
  Divide 2/10 quotient = 0 remainder = 2 char = '2'

## Slide 29: Integer to String Procedure
#--------------------------------------------------------------
# int2str: Converts an unsigned integer into a string
# Input: $a0 = unsigned integer
# In/Out: $a1 = address of string buffer (12 bytes)
#--------------------------------------------------------------
int2str:
move $t0, $a0 # $t0 = dividend = unsigned integer
li $t1, 10 # $t1 = divisor = 10
addiu $a1, $a1, 11 # start at end of string buffer
sb $zero, 0($a1) # store a NULL byte
convert:
divu $t0, $t1 # LO = quotient, HI = remainder
mflo $t0 # $t0 = quotient
mfhi $t2 # $t2 = remainder
addiu $t2, $t2, 0x30 # convert digit to a character
addiu $a1, $a1, -1 # point to previous byte
sb $t2, 0($a1) # store digit character
bnez $t0, convert # loop if quotient is not 0
jr $ra # return to caller