COE 301/ICS 233, Term 172

Computer Architecture & Assembly Language

HW# 3 Solution

# Write a MIPS assembly program that does the following:

## Ask the user to enter the number of rows R and read it.

## Ask the user to enter the number of columns C and read it.

## Ask the user to enter a two-dimensional array of RxC characters. Elements of a single row should be separated by a single space and each row is read in a new line.

## Print the entered array in a new line printing also its entered dimensions.

## Ask the user to enter two row numbers

## Exchange the two entered rows and print the array after the exchange.

A sample execution of the program is shown below:

Enter number of rows in the array: 3

Enter number of columns in the array: 5

Enter an array of 3x5 characters:

0 1 2 3 4

5 6 7 8 9

a b c d e

The entered 3x5 array is:

0 1 2 3 4

5 6 7 8 9

a b c d e

Enter a row number: 0

Enter another row number: 2

The array after exchanging Row 0 and Row 2 is:

a b c d e

5 6 7 8 9

0 1 2 3 4

################# Data segment #####################

.data

msg1: .asciiz "Enter number of rows in the array:"

msg2: .asciiz "Enter number of columns in the array:"

msg3: .asciiz "Enter an array of "

msg4: .asciiz " characters:\n"

msg5: .asciiz "The entered "

msg6: .asciiz " array is:\n"

msg7: .asciiz "Enter a row number:"

msg8: .asciiz "Enter another row number:"

msg9: .asciiz "The array after exchanging Row "

msg10: .asciiz " and Row "

msg11: .asciiz " is:\n"

Array: .space 400	# it is assumed that we have a max. array size of 20x20

Buffer: .space 40

################# Code segment #####################

.text

.globl main

main:	# main program entry

# Read number of rows and columns

la $a0, msg1

li $v0, 4

syscall

li $v0, 5

syscall

move $s0, $v0	# Number of rows

la $a0, msg2

li $v0, 4

syscall

li $v0, 5

syscall

move $s1, $v0	# Number of columns

# Printing messgae for reading the array

la $a0, msg3

li $v0, 4

syscall

move $a0, $s0

li $v0, 1

syscall

li $a0,'x'

li $v0, 11

syscall

move $a0, $s1

li $v0, 1

syscall

la $a0, msg4

li $v0, 4

syscall

# Reading the array and storing it

la $s2, Array

move $t0, $s0

NextR:

la $a0, Buffer

move $a1, $s1

sll $a1, $a1, 1

addi $a1, $a1, 1

li $v0, 8

syscall

move $t1, $s1

NextC:

lb $t2, ($a0)

sb $t2, ($s2)

addi $a0, $a0, 2

addi $s2, $s2, 1

addi $t1, $t1, -1

bnez $t1, NextC

addi $t0, $t0, -1

bnez $t0, NextR

# Displaying the entered array

la $a0, msg5

li $v0, 4

syscall

move $a0, $s0

li $v0, 1

syscall

li $a0,'x'

li $v0, 11

syscall

move $a0, $s1

li $v0, 1

syscall

la $a0, msg6

li $v0, 4

syscall

la $a0, Array

move $a1, $s0

move $a2, $s1

jal DispArray

# Getting First Row

la $a0, msg7

li $v0, 4

syscall

li $v0, 5

syscall

move $s3, $v0	# First row to be exchanged

# Getting Second Row

la $a0, msg8

li $v0, 4

syscall

li $v0, 5

syscall

move $s4, $v0	# Second row to be exchanged

# Exchanging the two rows

la $a0, Array

move $a1, $s1

move $a2, $s3

move $a3, $s4

jal ExchgRows

# Displaying the array after the exchange

la $a0, msg9

li $v0, 4

syscall

move $a0, $s3

li $v0, 1

syscall

la $a0, msg10

li $v0, 4

syscall

move $a0, $s4

li $v0, 1

syscall

la $a0, msg11

li $v0, 4

syscall

la $a0, Array

move $a1, $s0

move $a2, $s1

jal DispArray

li $v0, 10	# Exit program

syscall

# A procedure that receives in $a0 the address of an array,

# in $a1 the number of rows, and in $a2 the number of columns

# and displays the array.

DispArray:

move $t0, $a0

NR:

move $t1, $a2

NC:

lb $a0, ($t0)

li $v0, 11

syscall

li $a0, ' '

syscall

addi $t0, $t0, 1

addi $t1, $t1, -1

bnez $t1, NC

li $a0, 10

syscall

addi $a1, $a1, -1

bnez $a1, NR

jr $ra

# A procedure that receives in $a0 the address of an array,

# in $a1 the number of columns, and in $a2 & $a3 the two

# rows to be exchanged.

ExchgRows:

# Compute starting address of first row

mul $t0, $a1, $a2

add $t0, $t0, $a0

# Compute starting address of second row

mul $t1, $a1, $a3

add $t1, $t1, $a0

# Performing the exchange

Next:

lb $t3, ($t0)

lb $t4, ($t1)

sb $t3, ($t1)

sb $t4, ($t0)

addi $t0, $t0, 1

addi $t1, $t1, 1

addi $a1, $a1, -1

bnez $a1, Next

jr $ra

# You are required to write a MIPS assembly program to implement a pseudo random generator using Liner Feedback Shift Register (LFSR). An example of an 8-bit LFSR is shown below:

Two important characteristics of an LFSR are the Feedback Polynomial, which determines the flip-flops (FFs) that are XORed to compute the shifted bit, and the seed which determines the initial content of the FFs. Depending on the Feedback polynomial, the LFSR can generate a maximal-length sequence without repetition, or it may not. The seed can be any number other than 0.

The 8-bit LFSR shown above is a maximal-length i.e. it is guaranteed to generate a random sequence in the range from 1 to 255 before it repeats again.

The Feedback polynomial for the above LFSR can be represented as 10001101. Note that 1 indicates that there is feedback connection, while 0 indicates that there is no feedback connection.

## Write a procedure READB to read a binary number and store it in $v0. The procedure should report an error message and ask the user to reenter the number if the decimal value of the entered number is 0. Also, the user does not have to enter the whole 8-bits. If he enters less than 8 bits and hits return the remaining most significant bits should  be assumed 0. Also, if any digit entered is other than a binary digit, an error message should be reported.

## Write a procedure, RAND8,  that implements an 8-bit pseudo random generator. The procedure should be given the Feedback polynomial, and the seed as parameters in $a0 and $a1 registers and it should generate the next random number in $v0.

## Ask the user to enter an 8-bit feedback ploynomial and an 8-bit  seed in binary. Use the procedure READB for this purbose. Then, ask the user to enter a string of characters. Then, encrypt the string using RAND8 as follows. Each character is encrypted by XORing the least significant 4-bits of the ASCII code of the character with the least significant 4 bits and the most significant 4-bits of the generated random number . For example, assume the character to be encrypted is 'A'=0x41 and the random number is 0xA1. Then, the encrypted character will have the ASCII code 0x4A='J'. To decrypt the character, the decrypted character 0x4A='J',  will be XORed with the same corresponding random number used for encryption i.e. 0xA1 and this will generate the original character 0x41='A'. As an example, show the encryption of the string "This is an interesting assignment". Then, rerun your program giving it the encrypted string and it should correctly decrypt it to "This is an interesting assignment". Encrypt  this with the feedback polynomial 10001101 and a seed of 00001111.

################# Data segment #####################

.data

msg1: .asciiz "Enter an 8-bit feedback polynomial: "

msg2: .asciiz "Enter an 8-bit seed:"

msg3: .asciiz "Enter a message to encrypt/decrypt: "

msg4: .asciiz "Encrypted/Decrypted message is: "

buffer: .space 101	# Assuming maximum message length is 100 characters

bnum: .space 9

Errmsg: .asciiz "One of the entered digits is not a binary digit, renter the number again\n"

Errmsg2: .asciiz "Entered number is zero, renter the number again\n"

################# Code segment #####################

.text

.globl main

main:	# main program entry

# Getting an 8-bit feedback polynomial

li $v0, 4

la $a0, msg1

syscall

jal ReadB

move $s0, $v0

# Getting an 8-bit seed

li $v0, 4

la $a0, msg2

syscall

jal ReadB

move $s1, $v0

# Reading the message yo be encrypted/decrypted

li $v0, 4

la $a0, msg3

syscall

li $v0, 8

la $a0, buffer

li $a1, 101

syscall

# Encrypting/Decrypting message

li $v0, 4

la $a0, msg4

syscall

li $s4, 10

li $s5, 100		# Loop counter

la $s2, buffer

NextChar:

lb $s3, ($s2)

beq $s3, $s4, DoneE

# Generating next random number

move $a0, $s0

move $a1, $s1

jal RAND8

move $s1, $v0		# Storing returned number as next seed

move $t2, $v0		# encrypting/decrypting character

srl $t2, $t2, 4

andi $v0, $v0, 15

xor $v0, $v0, $t2

xor $s3, $s3, $v0

sb $s3, ($s2)

addi $s2, $s2, 1

addi $s5, $s5, -1

bnez $s5, NextChar

DoneE:

li $v0, 4

la $a0, buffer

syscall

li $v0, 10	# Exit program

syscall

# Procedure for reading an 8-bit binary number

# The read number will be returned in $v0.

ReadB:

# Reading the number as a string

Again:

xor $v1, $v1, $v1 # to hold binary number

li $v0, 8

la $a0, bnum

move $a2, $a0

li $a1, 9

syscall

li $t0, 8	#loop counter

li $t2, 10

li $t3, '0'

li $t4, '1'

Next:

lb $t1, ($a2)

beq $t1, $t2, Done

sll $v1, $v1, 1

beq $t1, $t3, Bdigit

bne $t1, $t4, Error

Bdigit:

andi $t1, $t1, 1

or $v1, $v1, $t1

addi $a2, $a2, 1

addi $t0, $t0, -1

bnez $t0, Next

bnez $v1, Done

la $a0, Errmsg2

li $v0, 4

syscall

j Again

Error:

la $a0, Errmsg

li $v0, 4

syscall

j Again

Done:

move $v0, $v1

jr $ra

# Procedure for implementing an 8-bit LFSR-based pseudo random

# number generater. The procedure is given the Feedback polynomial,

# and the seed as parameters in $a0 and $a1 registers and it generates

# the next random number in $v0.

RAND8:

move $v0, $a1

and $a1, $a1, $a0 	#Mask the bits that should not be Xored

# Count number of 1's in $a0

li $t0, 8			# Loop counter

xor $t1, $t1, $t1	# Number of ones

Loop:

move $t2, $a1

andi $t2, $t2, 1

add $t1, $t1, $t2

srl $a1, $a1, 1

addi $t0, $t0, -1

bnez $t0, Loop

srl $v0, $v0, 1

andi $t1, $t1, 1	# Check if number of ones is even or odd

beqz $t1, Skip

ori $v0, 0x0080

Skip:

jr $ra

Snapshot of running the program is given below:

Enter an 8-bit feedback polynomial: **** user input : 10001101

Enter an 8-bit seed:**** user input : 00001111

Enter a message to encrypt/decrypt: **** user input : This is an interesting assignment

Encrypted/Decrypted message is: [gnx%cv"`n(e`sf{i}{nmf iubjhnlbr

Enter an 8-bit feedback polynomial: **** user input : 10001101

Enter an 8-bit seed:**** user input : 00001111

Enter a message to encrypt/decrypt: **** user input : [gnx%cv"`n(e`sf{i}{nmf iubjhnlbr

Encrypted/Decrypted message is: This is an interesting assignment