June 10, 2008

COMPUTER ENGINEERING DEPARTMENT

ICS 233

COMPUTER ARCHITECTURE & ASSEMBLY LANGUAGE

Final Exam

Second Semester (072)

Time: 7:30-10:30 AM

Student Name : ______________________________________________

Student ID.     : ______________________________________________

| Question | Max Points | Score |
| --- | --- | --- |
| Q1 | 30 |  |
| Q2 | 15 |  |
| Q3 | 15 |  |
| Q4 | 10 |  |
| Q5 | 18 |  |
| Q6 | 12 |  |
| Total | 100 |  |

Dr. Aiman El-Maleh

# [30 Points]

# (Q1) Consider the single-cycle datapath and control given below along with ALU and Next PC blocks design for the MIPS processor implementing a subset of the instruction set:

## Show the control signals generated for the execution of the following instructions by filling the table given below:

| Op | RegDst | RegWrite | ExtOp | ALUSrc | ALUOp | Beq | Bne | J | MemRead | MemWrite | MemtoReg |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| R-type |  |  |  |  |  |  |  |  |  |  |  |
| addi |  |  |  |  |  |  |  |  |  |  |  |
| xori |  |  |  |  |  |  |  |  |  |  |  |
| lw |  |  |  |  |  |  |  |  |  |  |  |
| bne |  |  |  |  |  |  |  |  |  |  |  |

The format of these instructions is given below for your reference:

| Instruction | Meaning | Format |
| --- | --- | --- |
| sub rd, rs, rt | rd = rs + rt | Op6 = 0 | rs5 | rt5 | rd5 | 0 | 0x22 |
| addi rt, rs, imm16 | rt = rs + imm16 | 0x08 | rs5 | rt5 | imm16 |
| xori rt, rs, imm16 | rt = rs ^ imm16 | 0x0e | rs5 | rt5 | imm16 |
| lw rt, imm16(rs) | rt = MEM[rs+imm16] | 0x23 | rs5 | rt5 | imm16 |
| bne rs, rt, label | branch if (rs != rt) | 0x05 | rs5 | rt5 | imm16 |

## We wish to add the following instructions to the MIPS single-cycle datapath. Add any necessary datapath modifications and control signals needed for the implementation of these instructions. Show only the modified and added components to the datapath.  Show the values of the control signals to control the execution of each instruction.

  - lui

| Instruction | Meaning | Format |
| --- | --- | --- |
| lui rt, imm16 | rt= imm16 << 16 | Op6 = 0xf | 0 | rt5 | imm16 |

  - sltiu

| Instruction | Meaning | Format |
| --- | --- | --- |
| sltiu rt, rs, imm16 | rt=(rs<imm?1:0) | Op6 = 0xb | rs5 | rt5 | imm16 |

  - bgtz

| Instruction | Meaning | Format |
| --- | --- | --- |
| bgtz rs, label | branch if (rs>0) | Op6 = 7 | rs5 | 0 | imm16 |

  - jalr

| Instruction | Meaning | Format |
| --- | --- | --- |
| jalr rd, rs | rd=pc+4, pc=rs | op6 = 0 | rs5 | 0 | rd5 | 0 | 9 |

## Assume that the propagation delays for the major components used in the datapath are as follows:

    - Instruction and data memories: 150 ps

    - ALU and adders: 100 ps

    - Register file access (read or write): 60 ps

    - Main control: 20 ps

    - ALU control: 20 ps

Ignore the delays in the multiplexers, PC access, extension logic, and wires.

- What is the cycle time for the single-cycle datapath given above?

- A friend of yours suggested modifying the MIPS instruction set architecture to remove the ability to specify an offset for memory access instructions. Specifically, all load-store instructions with nonzero offsets would become pseudo instructions and would be implemented using two instructions. For example: the instruction lw $t0, 4($t1) is implemented as:

addi  $at, $t1, 4 			# add the offset to a temporary

lw     $t0, $at		 	# new way of doing lw $t0, 4($t1)

What will be the cycle time if the proposed simplified architecture were to be used? Under what conditions, the proposed architecture will be faster?

# [15 Points]

# (Q2) Consider the pipelined MIPS processor design given below:

## Make all the necessary changes to the given pipelined design to overcome data and control hazards by showing the design of hazard detection, forwarding and stall unit.

## Show the control signals that will be used for forwarding along with their conditions.

## Show the control signals that will be used for stalling the pipeline along with their conditions.

# [15 Points]

# (Q3) Consider the code given below:

add $1, $2, $3

lw $2, 8($1)

sub $2, $2, $1

sw $2, 8($1)

## Identify all the RAW data dependencies in the above code. Which dependencies are data hazards that will be resolved by forwarding? Which dependencies are data hazards that will cause a stall?

## Using a multiple-clock-cycle graphical representation, show the instruction execution across the pipeline including forwarding paths and stalled cycles if any. How many clock cycles will be needed to execute the instructions?

[10 Points]

# (Q4) Consider the MIPS program given below:

.data

Table: .word 2, 4, 3, 5, 6, 1

.text

.globl main

main:

la 	$a0, Table	# address of first element

add	$a1, $a0, 20	# address of last element

max:	move	$v0, $a0	# max pointer = first pointer

lw	$v1, ($v0)	# $v1 = first value

move	$t0, $a0	# $t0 = array pointer

loop:	addi	$t0, $t0, 4	# point to next array element

lw	$t1, 0($t0)	# $t1 = value of A[i]

slt	$at, $v1, $t1	# if (A[i] ( max) then skip

beq	$at, $0, skip

move	$v0, $t0	# found new maximum

move	$v1, $t1

skip:	bne	$t0, $a1, loop	# loop back if more elements

ret:

## Show the outcomes of each of the conditional branch instructions due to the execution of the program (T for taken, N for not taken).

## List the predictions and the accuracies for each of the following dynamic branch predictions schemes:

- 1-bit prediction, initialized to predict not taken.

- 2-bit predictor, initialized to weakly predict not taken.

[18 Points]

# (Q5) Assume that you have a cache with 64 bytes data size (i.e. not including tag and valid bits). Consider the following series of address references given as 16-bit addresses:

0x00c2, 0x00c3, 0x00c4, 0x00c5, 0x0ec2, 0x0ec3, 0x0ec4, 0x0ec5, 0x00c2, 0x00c3, 0x00c4, 0x00c5, 0x00c6, 0x00c7, 0xffc6, 0xffc7.

## Assuming that the cache is organized as direct-mapped with 2-byte block size, determine the number of bits in the offset, index and tag fields. Starting with an empty cache, show the offset, index and tag (in binary) for each address reference in the list and indicate whether it is a hit or a miss. What is the miss ratio for this sequence on this cache?

Offset = 		Index = 		Tag=

| Address | Tag | Index | Offset | Hit/Miss |
| --- | --- | --- | --- | --- |
| 0x00c2 |  |  |  |  |
| 0x00c3 |  |  |  |  |
| 0x00c4 |  |  |  |  |
| 0x00c5 |  |  |  |  |
| 0x0ec2 |  |  |  |  |
| 0x0ec3 |  |  |  |  |
| 0x0ec4 |  |  |  |  |
| 0x0ec5 |  |  |  |  |
| 0x00c2 |  |  |  |  |
| 0x00c3 |  |  |  |  |
| 0x00c4 |  |  |  |  |
| 0x00c5 |  |  |  |  |
| 0x00c6 |  |  |  |  |
| 0x00c7 |  |  |  |  |
| 0xffc6 |  |  |  |  |
| 0xffc7 |  |  |  |  |

## Miss ratio =

## Assuming that the cache is organized as four-way set associative with 2-byte block size, determine the number of bits in the offset, index and tag fields. Starting with an empty cache, show the offset, index and tag (in binary) for each address reference in the list and indicate whether it is a hit or a miss. Assume that a FIFO replacement policy is used. What is the miss ratio for this sequence on this cache?

Offset = 		Index = 		Tag=

| Address | Tag | Index | Offset | Hit/Miss |
| --- | --- | --- | --- | --- |
| 0x00c2 |  |  |  |  |
| 0x00c3 |  |  |  |  |
| 0x00c4 |  |  |  |  |
| 0x00c5 |  |  |  |  |
| 0x0ec2 |  |  |  |  |
| 0x0ec3 |  |  |  |  |
| 0x0ec4 |  |  |  |  |
| 0x0ec5 |  |  |  |  |
| 0x00c2 |  |  |  |  |
| 0x00c3 |  |  |  |  |
| 0x00c4 |  |  |  |  |
| 0x00c5 |  |  |  |  |
| 0x00c6 |  |  |  |  |
| 0x00c7 |  |  |  |  |
| 0xffc6 |  |  |  |  |
| 0xffc7 |  |  |  |  |

## Miss ratio =

[12 Points]

# (Q6) A processor runs at 2 GHz and has a CPI=1.4 for a perfect cache (i.e. without including the stall cycles due to cache misses). Assume that load and store instructions are15% of the instructions. The processor has an I-cache with a 4% miss rate and a D-cache with 6% miss rate. The hit time is 1 clock cycle. Assume that the time required to transfer a block of data from the RAM to the cache, i.e. miss penalty, is 40 ns.

## What is the number of stall cycles per instruction and the overall CPI?

## What is the average memory access time (AMAT) in ns?

## Discuss how you can reduce the AMAT.