July 22, 2007

COMPUTER ENGINEERING DEPARTMENT

ICS 233

COMPUTER ARCHITECTURE & ASSEMBLY LANGUAGE

Major Exam I

Summer Semester (063)

Time: 7:00-9:30 PM

Student Name : ______________________________________________

Student ID.     : ______________________________________________

| Question | Max Points | Score |
| --- | --- | --- |
| Q1 | 40 |  |
| Q2 | 15 |  |
| Q3 | 18 |  |
| Q4 | 12 |  |
| Q5 | 15 |  |
| Total | 100 |  |

Dr. Aiman El-Maleh

# [40 Points]

# (Q1) Indicate whether the following is true or false, and if it is false correct it (correct the answer and not the question):

## (1) (True, False)	The smallest (negative) number that can be represented using 8-bit 2`s complement in hexadecimal is FF and the largest positive number in hexadecimal is 7F.

## (True, False)	Assume that the CPU has just read a 32-bit instruction from the address 0x00400000. Then, the address of the next instruction that this CPU is going to read is 0x00400001.

## (True, False)	Assuming 8-bit representation of numbers, the binary number 10100100 is equal to -36 in sign-magnitude representation, -91 in 1`s complement representation, and -92 in 2`s complement representation.

## (True, False)	The following assembler directive allocates 1 word initialized by 10.

X: .word 1:10

## (True, False)	With a 32-bit address bus and 32-bit data bus, the maximum memory size than can be accessed by a processor is 4MByte and the maximum number of bytes that can be read or written in a single cycle is 8 Bytes.

## (True, False)	Assuming variable Array is defined as shown below:

Array: .word 0x00000010, 0x00000020

The content of register $t0 after executing the following sequence of instructions is 0x00000020.

la $t0, Array

lw $t0, 1($t0)

## (True, False) The instruction set architecture of a processor consists of its control unit, data path, memory, and the instruction set.

## (True, False)	Given a magnetic disk with the following properties:

- Rotation speed = 7200 RPM (rotations per minute)

- Average seek = 8 ms, Sector = 512 bytes, Track = 200 sectors

The average time to access a block of 64 consecutive sectors is 13.5 ms.

## (True, False)	Assuming the following data segment, and assuming that the first variable X is given the address 0x10010000, then the address for variable Y will be  0x10010005.

## .data

## X: 	.byte  10, 11, 12, 13, 14

## Y: 	.word  15

## (True, False) The code given below prints the statement: Exam1

MSG: .ascii  "Exam1"

.asciiz " ICS 233"

li $v0, 4

la $a0, MSG

syscall

## (True, False)	Assume that the instruction j NEXT is at address 0x00400020 in the text segment, and the label NEXT is at address 0x00400010. Then, the address stored in the assembled instruction for the label NEXT is 0x0400010.

## (True, False)	Assume that the instruction beq $t0, $t1, NEXT is at address 0x00400020 in the text segment, and the label NEXT is at address 0x00400010. Then, the address stored in the assembled instruction for the label NEXT is 0xfffb.

## (True, False)	After executing the instruction sll $t0, $t0, 2, the content of register $t0 is equal to 2*$t0, for both signed and unsigned content.

## (True, False)	The code given below implements the conditional statement

## if (($t0 < 1) AND ($t1 > 100)) Then $t2=0.

slti $t3, $t0, 1

bne $t3, $zero,  Zero_index

li $t3, 100

slt $t3, $t3, $t1

beq $t3, $zero, End_if

Zero_index:

xor $t2, $t2, $t2

End_if:

## (True, False) Assuming that $a0 contains an Alphabetic character, the instruction andi $a0, $a0, 0xdf will guarantee that the character in $a0 is an upper case character. Note that the ASCII code of character ‘A’ is 0x41 while that of character ‘a’ is 0x61.

## (True, False) Assume you are in a company that will market a certain IC chip. The cost per wafer is $4000, and each wafer can be diced into 2000 dies. The die yield is 60%. Then the cost per good die is $2.

## (True, False)	Assume that $t0=0xffff8111 and $t1=0xfffff265. Executing the instruction subu $t0, $t0, $t1 produces correct result in $t0 assuming both signed and unsigned number representation.

## (True, False)	The difference between add and addu instructions is that add should be used for addition of signed numbers while addu should be used for addition of unsigned numbers.

## (True, False)	Executing the following sequence of instructions produces the value 0x0000009b in $s2.

## li 	$s1, 5

## sll	$s2, $s1, 5

## subu	$s2, $s2, $s1

## (True, False)	Assuming that $s1=0xabcd1234 and $s2=0xffff0000, executing the instruction nor $s0,$s1,$s2 produces the value 0xffff1234 in $s0.

# [15 Points]

# (Q2) Using only basic MIPS instructions, write the shortest sequence of instructions to implement each of the following pseudo instructions:

## li $t0, 0x12345678  #$t0 is loaded with the immediate value 0x12345678

## not $t0, $t1   #$t0 is loaded with the 1's complement value of $t1

## bge $t0, $t1, Next   # branch to Next if $t0 is greater than or equal $t1

## abs $t0, $t1   #$t0 is loaded with the absolute value of $t1

## rol $t0, $t0, 5   #$t0 is rotated to the left by 5 bits and stored in $t0

[18 Points]

# (Q3) Answer the following questions. Show how you obtained your answer:

## (i)   Given that TABLE is defined as: TABLE: .ascii "Ahmad Ali Anas"

## Determine the content of register $t0 after executing the following code:

xor $t0, $t0, $t0

li $t1, 14

la $t2, TABLE

addi $t2, $t2, -1

Next: 	beq $t1, $zero, ENL

addi $t2, $t2, 1

lbu $t3, ($t2)

ori $t3, $t3, 0x20

li $t4, 'a'

addi $t1, $t1, -1

bne $t3, $t4, Next

addi $t0, $t0, 1

j Next

ENL:

## (ii)   Given that TABLE is defined as shown below:

## TABLE: .space 33

## Determine the output produced after executing the following code:

li $t0, 0xabcde765

li $t1, 32

la $t2, TABLE

AGAIN:          li $t3, '0'

rol $t0, $t0, 1

andi $t4, $t0, 1

add  $t3, $t3, $t4

sb $t3, ($t2)

addi $t2, $t2, 1

addi $t1, $t1, -1

bne $t1, $zero, AGAIN

la $a0, TABLE

li $v0, 4

syscall

## (iii) Given that TABLE is defined as shown below, determine the content of TABLE after executing the following code:

## TABLE:  .word 1, 2, 3, 4, 5, 6, 7, 8

la $t0,  TABLE

addi $t1, $t0, 28

li $s0, 4

Again:

lw $t2, ($t0)

lw $t3, ($t1)

sw $t2, ($t1)

sw $t3, ($t0)

addi $t0, $t0, 4

addi $t1, $t1, -4

addi $s0, $s0, -1

bne $s0, $zero, Again

[12 Points]

# (Q4) Write a MIPS assembly program to do the following using the smallest possible number of instructions. Ask the user to enter two integers and then display their sum according to the format given below.

Sample Execution:

Enter an integer: -2

Enter another integer: 20

The sum of -2 and 20 = 18

[15 Points]

# (Q5) Write a MIPS assembly program to sort an array of integers (i.e. 32-bit signed numbers) in an ascending order using BubbleSort algorithm.  Minimize the number of instructions used.

The pseudocode for the BublleSort algorithm is given below:

BubbleSort (ArrayPointer, ArraySize)

Status = Unsorted

#comprisons = ArraySize-1

while (#comparisons<>0 AND status = Unsorted)

Status = Sorted

for (i= 0 to #comparisons)

if (Array[i] > Array[i+1])

swap ith and (i+1)th elements of the array

Status = Unsorted

end if

end for

#comparisons = #comparisons – 1

end while

end BubbleSort

# Clearly indicate the registers used for each variable. Store the array to be sorted in variable Array as defined below.

Array: .word 10, 2, 0, 15, 25, 30, 7, 22