Nov. 13, 2008

COMPUTER ENGINEERING DEPARTMENT

ICS 233

COMPUTER ARCHITECTURE & ASSEMBLY LANGUAGE

Major Exam I

First Semester (081)

Time: 1:00-3:00 PM

Student Name : ______________________________________________

Student ID.     : ______________________________________________

| Question | Max Points | Score |
| --- | --- | --- |
| Q1 | 35 |  |
| Q2 | 20 |  |
| Q3 | 15 |  |
| Q4 | 30 |  |
| Total | 100 |  |

Dr. Aiman El-Maleh

# [35 Points]

# (Q1) Fill in the blank in each of the following questions:

## (1)	The smallest (negative) number that can be represented using 16-bit 2`s complement in hexadecimal is ________ and the largest positive number in hexadecimal is ________.

## Assuming 8-bit representation of numbers, the hexadecimal number 8E is equal to __________ as unsigned number and __________ in 2`s complement representation.

## Assuming variable Array is defined as shown below:

Array: .word 0x000000A0, 0x000000B0

The content of register $t0 after executing the following sequence of instructions is _________________________________.

la $t0, Array

lw $t0, 4($t0)

## With a 32-bit address bus and 32-bit data bus, the maximum memory size than can be accessed by a processor is ________ Byte and the maximum number of bytes that can be read or written in a single cycle is ________ Bytes.

## Given a magnetic disk with the following properties:

- Rotation speed = 8000 RPM (rotations per minute)

- Average seek = 7 ms, Sector = 1024 bytes, Track = 250 sectors

The average time to access a block of 200 consecutive sectors is _______________________________________________ ms.

## Assuming the following data segment, and assuming that the first variable X is given the address 0x10010000, then the addresses for variable Y and Z will be  _____________ and _____________.

## .data

## X: 	.byte  1, 2, 3, 4, 5

## Y:	.half   6, 7

## Z: 	.word 8

## Assume that the CPU has just read a 32-bit instruction from the address 0x00400000. Then, the address of the next instruction that this CPU is going to read is ___________________________.

## Assume that the instruction j NEXT is at address 0x00400030 in the text segment, and the label NEXT is at address 0x004000a8. Then, the address stored in the assembled instruction for the label NEXT  is ___________________________.

## Assume that the instruction bne $t0, $t1, NEXT is at address 0x00400030 in the text segment, and the label NEXT is at address 0x004000a8. Then, the address stored in the assembled instruction for the label NEXT is __________________.

## Assuming that $a0 contains an Alphabetic character, the instruction ____________________ will guarantee that the character in $a0 is always a lower case character. Note that the ASCII code of character ‘A’ is 0x41 while that of character ‘a’ is 0x61.

## Assume you are in a company that will market a certain IC chip. The cost per wafer is $2000, and each wafer can be diced into 200 dies. The die yield is 80%. Then the cost per good die is __________________.

## ________________ language produces more compact and more efficient code than ___________________   language.

## ________________ memory is faster than random access memory but  it  is slower  than ___________________ .

## The instruction set architecture of a processor consists of ___________________________, ________________________________ and ___________________________.

## The difference between slt and sltu instructions is that _________________________________________________________________.

# [20 Points]

# (Q2) Using only basic MIPS instructions, write the shortest sequence of instructions to implement each of the following pseudo instructions:

## andi $t0, 0x12345678  #$t0 is anded with the 32-bit value  0x12345678

## bge $t0, $t1, Next   # branch to Next if $t0 is greater than or equal to $t1

## bgt $t0, 100, Next   # branch to Next if $t0 is greater than 100

## neg $t0, $t1   #$t0 is loaded with the negative value of $t1

## rol $t0, $t0, 12   #$t0 is rotated to the left by 12 bits and stored in $t0

[15 Points]

# (Q3) Answer the following questions. Show how you obtained your answer:

## (i)   Determine the content of register $s1 after executing the following code:

ori $s1, $zero, 4

sll $t0, $s1, 4

sub $t0, $t0, $s1

sra $t1, $s1, 2

add $s1, $t0, $t1

## Determine the content of register $t2 after executing the following code:

li $s1, 0x1b

and $t2, $zero, $t2

Next:

andi $t1, $s1, 1

add $t2, $t2, $t1

srl  $s1, $s1, 1

bne $s1, $0, Next

## (iii) Given that TABLE is defined as: TABLE: .word 1, 10, -4, 5, 20, 3

## Determine the content of registers $t2 after executing the following code:

la         $t0, TABLE

li	$t1, 6

lw	$t2, ($t0)

loop:	addi	$t0, $t0, 4

lw	$t3, ($t0)

ble	$t3, $t2, skip

move	$t2, $t3

skip:	addi	$t1, $t1, -1

bne	$t1, $0, loop

[30 Points]

# (Q4) Merge sort is a technique to combine two sorted arrays. Merge sort takes two sorted input arrays X and Y, say of size m and n, and produces a sorted array Z of size m+n that contains all elements of the two input arrays. The pseudo code of merge sort is as follows:

MergeSort (X, Y, Z, m, n)

i:=0 	{index variables for arrays X, Y, and Z}

j:=0

k:=0

while (i<m)AND (j<n)

if (X[i] ( Y[j]) then

Z[k]:=X[i]

k:=k+1

i:=i+1

else

Z[k]:=Y[j]

k:=k+1

j:=j+1

end if

end while

if (i<m) then

while (i<m)

Z[k]:=X[i]

k:=k+1

i:=i+1

end while

else

while (j<n)

Z[k]:=Y[j]

k:=k+1

j:=j+1

end while

end if

end MergeSort

# Write a MIPS assembly program to implement MergeSort to merge sort two arrays of integers (i.e. 32-bit signed numbers) in an ascending order. Assume that the address of X array, Y array and Z array are stored in registers $s0, $s1 and $s2, respectively. Also, assume that m, the size of array X, is stored in register $s3 and n, the size of array Y, is stored in register $s4. Your code should not change the content of registers $s0-$s4 after execution.