May 17, 2008

COMPUTER ENGINEERING DEPARTMENT

ICS 233

COMPUTER ARCHITECTURE & ASSEMBLY LANGUAGE

Major Exam II

Second Semester (072)

Time: 8:00-10:00 PM

Student Name : ______________________________________________

Student ID.     : ______________________________________________

| Question | Max Points | Score |
| --- | --- | --- |
| Q1 | 20 |  |
| Q2 | 15 |  |
| Q3 | 16 |  |
| Q4 | 10 |  |
| Q5 | 14 |  |
| Q6 | 10 |  |
| Q7 | 15 |  |
| Total | 100 |  |

Dr. Aiman El-Maleh

# [20 Points]

# (Q1) You are required to write a procedure that receives two parameters N and K in registers $a0 and $a1 and computes the result of multiplying NxN-1xN-2x…xK and stores the result in $v0.  The procedure is described in a recursive way as follows:

# RangeMul(N,K){ If N=K return N else return N*RangeMul(N-1,K) }

Implement the given recursive procedure, RangeMul, in MIPS assembly programming with the minimal number of instructions. Then, write a program to ask the user to enter two integers N and K and print RangeMul(N,K).

A sample execution of the program is:

Enter first integer N: 5

Enter second integer K: 3

Result is: 60

A summary of syscall services you can use is given below:

| Service | $v0 | Arguments / Result |
| --- | --- | --- |
| Print Integer | 1 | $a0 = integer value to print |
| Print String | 4 | $a0 = address of null-terminated string |
| Read Integer | 5 | $v0 = integer read |

# [15 Points]

# (Q2) You are required to design a circuit that can be used to perform either signed or unsigned multiplication of two N-bit operands A and B depending on an input signal OP. When OP=0, the circuit will perform unsigned multiplication. Otherwise, it will perform signed multiplication. Show the algorithm that will be used with the circuit in performing the multiplication operations.

# [16 Points]

# (Q3) Given that Dividend=1001 and Divisor=0100.

## Using the refined unsigned division hardware, show the unsigned division of Dividend by Divisor. The result of division should be stored in the Remainder and Quotient registers. Show the steps of your work.

## Using the refined unsigned division hardware, show the signed division of Dividend by Divisor. The result of division should be stored in the Remainder and Quotient registers. Show the steps of your work.

# [10 Points]

# (Q4) Consider a simplified 8-bit floating point representation following the general guidelines of the IEEE format in representing normalized, denormalized, Nan, infinity and 0. Suppose that the number of bits used for the exponent is 3 and for the fraction is 4 bits.

## Determine the smallest and largest positive values of normalized numbers.

## Determine the smallest and largest positive values of denormalized numbers.

## Determine the representation used for +0 and +(.

## What is the largest and smallest error in this representation?

[14 Points]

# (Q5) Given the following two floating-point numbers in single-precision format:

X=0100 0011 1000 0000 0000 0000 0000 0000

Y=1011 1000 0000 1100 0000 0000 0000 0000

## Determine the decimal value of the two numbers X and Y.

## Perform the floating-point operation X+Y rounding the result to the nearest even, using guard, round and sticky bits. Represent the result in single-precision format.

[10 Points]

# (Q6) You are going to enhance a computer, and there are two possible improvements: either make multiply instructions run four times faster than before, or make memory access instructions run two times faster than before. You repeatedly run a program that takes 100 seconds to execute. Of this time, 20% is used for multiplication, 50% for memory access instructions, and 30% for other tasks. What will the speedup be if you improve only multiplication? What will the speedup be if you improve only memory access? What will the speedup be if both improvements are made?

[15 Points]

(Q7) You are the lead designer of a new processor. The processor design and compiler are complete, and now you must decide whether to produce the current design as it stands or spend additional time to improve it. You discuss this problem with your hardware engineering team and arrive at the following options:

## Leave the design as it stands. Call this base computer Mbase. It has a clock rate of 500 MHz, and the following measurements have been made using a simulator:

| Instruction Class | CPI | Frequency |
| --- | --- | --- |
| A | 2 | 40% |
| B | 3 | 25% |
| C | 3 | 25% |
| D | 5 | 10% |

## Optimize the hardware. The hardware team claims that it can improve the processor design to give it a clock rate of 600 MHz. Call this computer Mopt. The following measurements were made using a simulator for Mopt:

| Instruction Class | CPI | Frequency |
| --- | --- | --- |
| A | 2 | 40% |
| B | 2 | 25% |
| C | 3 | 25% |
| D | 4 | 10% |

## What is the average CPI for each computer?

## What are the MIPS ratings for Mbase and Mopt?

## How much faster is Mopt  more than Mbase ?