January 8, 2009

COMPUTER ENGINEERING DEPARTMENT

ICS 233

COMPUTER ARCHITECTURE & ASSEMBLY LANGUAGE

Major Exam II

First Semester (081)

Time: 1:00-3:30 PM

Student Name : ______________________________________________

Student ID.     : ______________________________________________

| Question | Max Points | Score |
| --- | --- | --- |
| Q1 | 20 |  |
| Q2 | 16 |  |
| Q3 | 16 |  |
| Q4 | 16 |  |
| Q5 | 8 |  |
| Q6 | 8 |  |
| Q7 | 16 |  |
| Total | 100 |  |

Dr. Aiman El-Maleh

# [20 Points]

# (Q1) Given below a summary of syscall services:

| Service | $v0 | Arguments / Result |
| --- | --- | --- |
| Print Integer | 1 | $a0 = integer value to print |
| Read Integer | 5 | $v0 = integer read |
| Exit Program | 10 |  |

## Determine the output produced by the following program given that the program inputs are 7 and 4.

.text

.globl main

main:

li $v0, 5

syscall

move $t0, $v0

li $v0, 5

syscall

move $a1, $v0

move $a0, $t0

jal Proc1

move $a0, $v0

li $v0, 1

syscall

li $v0, 10

syscall

Proc1:

bne $a0, $a1, Skip

move $v0, $a0

jr $ra

Skip:

addi $sp, $sp, -8

sw $a0, ($sp)

sw $ra, 4($sp)

addi $a0, $a0, -1

jal Proc1

lw $t0, ($sp)

lw $ra, 4($sp)

addi $sp, $sp, 8

mul $v0, $v0, $t0

jr $ra

## Determine the output produced by the following program given that the program input is 987.

.text

.globl main

main:

li $v0, 5

syscall

move $a0, $v0

jal Proc2

move $a0, $v0

li $v0, 1

syscall

li $v0, 10

syscall

Proc2:

li $t0, 10

move $t1, $a0

Next:

xor $t3, $t3, $t3

Again:

divu $t1, $t0

mflo $t1

mfhi $t2

addu $t3, $t3, $t2

bnez $t1, Again

move $t1, $t3

bge $t1, $t0, Next

move $v0, $t1

jr $ra

# [16 Points]

# (Q2) Given that Multiplicand=1010 and Multiplier=1111.

## Using the refined unsigned multiplication hardware, show the unsigned multiplication of Multiplicand by Multiplier. The result of the multiplication should be an 8 bit unsigned number in HI and LO registers. Show the steps of your work.

## Using the refined signed multiplication hardware, show the signed multiplication of Multiplicand by Multiplier. The result of the multiplication should be an 8 bit signed number in HI and LO registers. Show the steps of your work.

# [16 Points]

# (Q3) Given that Dividend=1001 and Divisor=0101.

## Using the refined unsigned division hardware, show the unsigned division of Dividend by Divisor. The result of division should be stored in the Remainder and Quotient registers. Show the steps of your work.

## Using the refined unsigned division hardware, show the signed division of Dividend by Divisor. The result of division should be stored in the Remainder and Quotient registers. Show the steps of your work.

[16 Points]

# (Q4)

## What is the decimal value of the following single-precision floating-point number?

## 0100 0011 0110 1001 1000 0100 0000 0000.

# Show the single-precision floating-point binary representation for: 555.9375.

# Perform the following floating-point operation rounding the result to the nearest even. Perform the operation using guard, round and sticky bits.

## 1100 1110 0000 0000 0000 0000 0100 0000

## +	0101 0010 0000 0000 1000 0000 0000 0000

[8 Points]

# (Q5)

## Fill the following table by placing a check mark (() indicating the impact of each listed factor on the Instruction Count (I-Count), CPI and Cycle time.

|  | I-Count | CPI | Cycle |
| --- | --- | --- | --- |
| Compiler |  |  |  |
| Instruction Set Architecture (ISA) |  |  |  |
| Organization |  |  |  |
| Technology |  |  |  |

## List three problems in using MIPS as a performance metric.

[8 Points]

# (Q6) Suppose that a program runs in 150 seconds on a machine, with ALU operations responsible for 40 seconds of this time, multiply operations responsible for 50 seconds of this time and divide operations responsible for 40 seconds of this time. The remaining time is taken by the remaining operations. Suppose that a new implementation of the machine has improved the execution time of the ALU by a factor of 2, the multiplier by a factor of 1.5 and the divider by a factor of 1.6. Determine the new execution time and the speedup of the program based on the new implementation.

[16 Points]

# (Q7) Given the following instruction mix of a program on a RISC processor:

| Class | CPI | Frequency |
| --- | --- | --- |
| ALU | 2 | 40% |
| Branch | 2 | 25% |
| Jump | 1 | 15% |
| Load | 4 | 10% |
| Store | 3 | 10% |

## What is the average CPI?

## Assuming that the processor has a clock rate of 2 GHz, determine MIPS.

## What is the percent of time used by each instruction class?

## How much faster would the program run if load time is reduced to 3 cycles, and two ALU instructions could be executed at once, assuming that the cycle time has increased by 5% and the instruction count has increased by 10%?