Nov. 22, 2014

ICS DEPARTMENT

ICS 233

COMPUTER ARCHITECTURE & ASSEMBLY LANGUAGE

Midterm Exam

First Semester (141)

Time: 1:00-3:30 PM

Student Name : ______________________________________________

Student ID.     : ______________________________________________

| Question | Max Points | Score |
| --- | --- | --- |
| Q1 | 35 |  |
| Q2 | 7 |  |
| Q3 | 20 |  |
| Q4 | 18 |  |
| Q5 | 10 |  |
| Q6 | 10 |  |
| Total | 100 |  |

# Dr. Aiman El-Maleh

Dr. Samer Arafat

# [35 Points]

# (Q1) Fill in the blank in each of the following questions:

- Each memory cell of DRAM holds 1 bit of information and consists of _______ transistor(s) and __________ capacitor(s). 				(1 Point)

- Typically, the SRAM technology is used for the ________ memory. 	(1 Point)

- Given a magnetic disk with rotation speed = 15000 rotations per minute and average seek time 10 milliseconds, then the time needed for one rotation is ______________ milliseconds. 						(1 Point)

- A processor with 2.0 GHz speed has a _____________ picoseconds clock cycle duration. 									(1 Point)

- A certain chip manufacturing process produces 25 bad dies, on average. Given that the total number of dies on any given wafer is 300, then, this process has a yield equal to ____ %. 							(1 Point)

- Cache memory is faster than _____________ memory and slower than _______________. 							(1 Point)

- One main advantage for programming in high-level language is _________________________________________________________________.

(1 Point)

- One main advantage for programming in assembly language is _________________________________________________________________.

(1 Point)

## Assuming variable Array is defined as shown below:

Array: .byte 1, -1, 2, -2, 3, -3, 4, -4

After executing the following sequence of instructions, the content of the three registers is $t1=_______________, $t2=_______________, and $t3=_______________.

(3 Points)

la $t0, Array

lbu $t1, 4($t0)

lh $t2, 4($t0)

lw $t3, 4($t0)

## Assume that the instruction j NEXT is at address 0x0040002c in the text segment, and the label NEXT is at address 0x00400018. Then, the address stored in the assembled instruction for the label NEXT is ___________________________. 					    (2 Point)

## Assume that the instruction bne $t0, $t1, NEXT is at address 0x0040002c in the text segment, and the label NEXT is at address 0x00400018. Then, the address stored in the assembled instruction for the label NEXT is __________________.										(2 Points)

## Given that the instruction jal MyProc is at address 0x0040002c in the text segment, and that MyProc is at address 0x00400018. Then, the address stored in $ra register after executing this instruction is __________________.

## (1 Point)

## To allocate 10 words, each initialized by 0, we use the following assembler directive __________________________________________________________.

## (1 Point)

## The pseudo instruction bge $s2, $s1, Next is implemented by the following minimum MIPS instructions:

____________________________________________________________________________________________________________________________________________________________

## (2 Points)

## The code given below prints the following:

## ___________________________________________________________________________________________________________________________________.

## Note that the ASCII code for the line feed character is 10 and the ASCII code for the carriage return character is 13. 					(2 Points)

MSG: .ascii  "Midterm Exam "

.byte 10

.ascii "ICS 233 "

.asciiz "is easy !! "

li $v0, 4

la $a0, MSG

syscall

## Using minimum native MIPS instructions, the assembly code to Jump to label L1 if bits 0, 2, and 5 in $t0 are all set (i.e. =1) is:

________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

## (3 points)

## To multiply the signed content of register $t0 by 63.75 without using multiplications and division instructions, we use the following instructions:

__________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

## (3 points)

## Assuming that all registers contain signed numbers, the MIPS assembly code (with minimum execution time) to implement the equation $v0=(5-16*$a0)/($a1) is:__________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

## (3 points)

## Suppose that we would like to translate 8-bit numbers into characters according to a given translation table. Part of the translation table is shown below. The MIPS assembly code to translate a number in register $t0 according to the translation table below and store the resulting character in the same register is (e.g. if $t0=3 the program should store ‘G’ in $t0):

| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | … |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| ‘a’ | ‘C’ | ‘x’ | ‘G’ | ‘y’ | ‘!’ | ‘h’ | ‘?’ | ‘-’ | … |

__________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

## (2 points)

## Consider a simplified 5-bit floating-point representation following the general guidelines of the IEEE standard format. Suppose that the number of bits used for the exponent is 2 bits and for the fraction is 2 bits. Then, the smallest and largest positive values of normalized numbers that can be represented using this representation are ____________________ and __________________, and the largest error in this representation is ______________________. 	(3 points)

[7 Points]

(Q2)

## Assuming that one byte is typed into each small block (one word per row) in the table below, fill out the table for the following data segment. Assume a Little Endian ordering, which is the same as the Mars 4.4 simulator default. Start from the top and work out the rest of the memory segment. Assume that the address of the first byte is 0x10010000. Remember that hex numbers start with 0x. Note that you do not need to show the ASCII code of characters. (5 Points)

.data

var1:  .BYTE   3,'1', -7

.ALIGN  0

var2:  .WORD   10

str1:  .ASCIIZ "ICS"

.ALIGN  2

var3:  .WORD   0xabcdef22

.ALIGN  3

Var4:  .HALF   -1

MSB                                        LSB           Address

|  |  |  |  | 0x10010000 |
| --- | --- | --- | --- | --- |
|  |  |  |  | 0x10010004 |
|  |  |  |  | 0x10010008 |
|  |  |  |  | 0x1001000c |
|  |  |  |  | 0x10010010 |
|  |  |  |  | 0x10010014 |

## Fill out the symbol table, below, that corresponds to the data segment in Part (i), above. (2 Points)

[20 Points]

# (Q3) Answer the following questions. Show how you obtained your answer:

## Determine what will be displayed after executing the following code: (5 Points)

li $a0, 23

li $a1, 5

div $a0, $a1

mflo $a0

li $v0, 1

syscall

li $a0, '.'

li $v0, 11

syscall

li $t0, 10

mfhi $t1

mul $t1, $t1, $t0

div $t1, $a1

mflo $a0

li $v0, 1

syscall

## Given the following definition in the data segment:

Array: .word    0,   1,   2,   3,    4

.word    5,   6,   7,   8,    9

.word  10, 11, 12, 13,  14

## Determine the content of Array after executing the following code: (5 Points)

la $t0, Array

li $t1, 5

li $t2, 20

addu $t2, $t2, $t0

li $t3, 40

addu $t3, $t3, $t0

Next:     lw $t4, 0($t2)

lw $t5, 0($t3)

sw $t4, 0($t3)

sw $t5, 0($t2)

addi $t2, $t2, 4

addi $t3, $t3, 4

addi $t1, $t1, -1

bnez $t1 Next

## Determine what will be displayed after executing the following code: (5 Points)

li $t0, 0x1d76

andi $a0, $t0, 0x1f

li $v0, 1

syscall

li $a0, '-'

li $v0, 11

syscall

srl $t0, $t0, 5

andi $a0, $t0, 0xf

li $v0, 1

syscall

li $a0, '-'

li $v0, 11

syscall

srl $t0, $t0, 4

andi $a0, $t0, 0x3ff

addu $a0, $a0, 2000

li $v0, 1

syscall

## Given the following definition in the data segment: (5 Points)

TABLE: .asciiz  "Emad Ali Anas"

Determine the content of TABLE after executing the following code:

li $t0, 'a'

li $a0, '*'

la $t1, TABLE

addi $t1, $t1, -1

Next: 	addi $t1, $t1, 1

lbu $t2, 0($t1)

beq $t2, $0, ENL

ori $t2, $t2, 0x20

bne $t2, $t0, Next

sb $a0, 0($t1)

j Next

ENL:

[18 Points]

# (Q4) Write separate MIPS assembly code fragments with minimum instructions to implement each of the given requirements.

## Given the following high level language code structure, write down the corresponding MIPS assembly language instructions: (6 Points)

i = 1;

size = 10;

while (i < size || A[i] !=0){

A[i] = A[i] + A[i – 1] ;

i = i + 1;

}

Assume that the assembler has assigned i to register $s0, size to register $s1, and has stored the address of array A in register $s2.

## Assuming that functions F and G receive two arguments in $a0 and $a1 and return their results in $v0, implement the function F given below saving needed registers on the stack. Save changed registers according to the assumed programming convention. (6 Points)

int F(int a, int b) {

return  a+G(b, G(a, b));

}

## Write a procedure that counts the number of even and odd integers that are input via a keyboard. The user will continue to enter nonnegative integers until he enters -1 to terminate the input. The procedure is called countevenodd and returns the total count of odd integers in register $v1 and the total count of even integers in register $v0. Assume that a main program prompts the user asking for input and that the main program will print the output counts with proper messages. You do not need to write the main program code. (6 Points)

[10 Points]

(Q5)

## Assume that we have a Multiplicand = 1100 and a Multiplier = 0011.

# Using the revised unsigned multiplication hardware, show the unsigned multiplication product for the given numbers, above. The result of the multiplication should be an 8 bit unsigned number in the HI and LO registers. Show all the steps of your work.

# (4 Points)

| Iteration | Multiplicand | Carry | Product = HI,LO |
| --- | --- | --- | --- |
| 0 | Initialize |  |  |  |
| 1 |  |  |  |  |
| 2 |  |  |  |  |
| 3 |  |  |  |  |
| 4 |  |  |  |  |

## Show the hardware diagram that corresponds to the revised integer (signed) multiplication. Carefully label all parts and connections in your diagram.

# (6 Points)

[10 Points]

# (Q6)

## What is the decimal value of the following single-precision floating-point number?

## 1100 0010 1110 1101 1000 0000 0000 0000. 		(2 Points)

# Show the single-precision floating-point binary representation for: 120.125.

## (2 Points)

# Perform the following floating-point operation rounding the result to the nearest even. Perform the operation using guard, round and sticky bits.

## 1100 0001 1000 0000 0000 0000 0000 0100

## +	0100 0011 1000 1000 0000 0000 0000 0000

## (6 Points)

Syscall Services:

MIPS Instructions: