Name:									Id#

ICS 233, Term 063

Computer Architecture & Assembly Language

Quiz# 1

Date: Saturday, July 14, 2007

# Q1. Fill the blanks in the following questions:

## Assuming 6-bit 2`s complement representation, the smallest (negative) number is _________________ in binary and ____________ in decimal and the largest (positive) number is _________________ in binary and _________________ in decimal.

## Consider an 8-bit register that has the binary number 10110100. The decimal value of this number as a signed number in sign-magnitude representation is __________________ while in 1’s complement representation it is __________________ and in 2’s complement representation it is __________________.

## Assuming 8-bit 2`s complement representation, the number F0 represents the decimal number _________________.

## The binary number 01100100 represents character _____________, and uses an ___________ parity bit. Note that the ASCII code of character A is 41H and that of character a is 61H.

## The ______________________ register is the register in the CPU that holds the address of the next instruction to be fetched from memory.

## The ______________________ register is the register in the CPU that stores the machine language instructions, temporarily, after the instructions are fetched from memory.

## Given that a wafer can be diced into 2000 dies, out of which 800 dies are defective. Then, the yield is _____________.

## Given a magnetic disk with Rotation speed = 7200 RPM (rotations per minute). Then, the average rotation latency, i.e. time to locate needed sector is _______________________________________________________________________.

## ______________________________ is a specific interface that the hardware provides the low-level software which includes the instruction set, programmer accessible registers and memory.

## ________________ is a small fast memory that acts as a buffer for the main memory.

## _____________________ is a program that manages the resources of a computer for the benefit of the programs that run on that machine.

## ______________________ is a program that converts symbolic versions of instructions into their binary formats.

## ______________________ is component of the processor that performs arithmetic operations.

## Given and address bus of 32 bits and data bus of 32 bits, the maximum memory size that can be interfaced with the CPU is __________________ bytes and the maximum number of bytes that can be read in a single read/write cycle is __________ bytes.

# Q2. Perform the following arithmetic operations assuming that numbers are represented using 8-bit 2’s complement representation. Indicate in your answer when an overflow occurs.

## i.  FC + AF

## ii. 81 – 7D