Name: KEY									Id#

ICS 233, Term 063

Computer Architecture & Assembly Language

Quiz# 1

Date: Saturday, July 14, 2007

# Q1. Fill the blanks in the following questions:

## Assuming 6-bit 2`s complement representation, the smallest (negative) number is 100000 in binary and -32 in decimal and the largest (positive) number is 011111 in binary and +31 in decimal.

## Consider an 8-bit register that has the binary number 10110100. The decimal value of this number as a signed number in sign-magnitude representation is -52 while in 1’s complement representation it is -75 and in 2’s complement representation it is -76.

## Assuming 8-bit 2`s complement representation, the number F0 represents the decimal number -16.

## The binary number 01100100 represents character d, and uses an odd parity bit. Note that the ASCII code of character A is 41H and that of character a is 61H.

## The Program Counter register is the register in the CPU that holds the address of the next instruction to be fetched from memory.

## The Instruction register is the register in the CPU that stores the machine language instructions, temporarily, after the instructions are fetched from memory.

## Given that a wafer can be diced into 2000 dies, out of which 800 dies are defective. Then, the yield is (2000-800)/2000=1200/2000=60%.

## Given a magnetic disk with Rotation speed = 7200 RPM (rotations per minute). Then, the average rotation latency, i.e. time to locate needed sector is 0.5*1000*60/7200=4.17 ms.

## The Instruction Set Architecture is a specific interface that the hardware provides the low-level software which includes the instruction set, programmer accessible registers and memory.

## Cache is a small fast memory that acts as a buffer for the main memory.

## Operating System is a program that manages the resources of a computer for the benefit of the programs that run on that machine.

## Assembler is a program that converts symbolic versions of instructions into their binary formats.

## Datapath  is component of the processor that performs arithmetic operations.

## Given and address bus of 32 bits and data bus of 32 bits, the maximum memory size that can be interfaced with the CPU is 232=4G bytes and the maximum number of bytes that can be read in a single read/write cycle is 32/8=4 bytes.

# Q2. Perform the following arithmetic operations assuming that numbers are represented using 8-bit 2’s complement representation. Indicate in your answer when an overflow occurs.

## i.  FC + AF

= AB

There is no overflow as adding two negative numbers produced a negative number.

## ii. 81 – 7D

= 81 + 83 = 04

There is overflow as adding two negative numbers produced a positive number.