Name: KEY									Id#

ICS 233, Term 072

Computer Architecture & Assembly Language

Quiz# 1

Date: Wednesday, Feb. 27, 2008

# Q1. Fill the blanks in the following questions:

## There is a one-to-one correspondence between assembly language and machine language.

## Advantages of programming in high-level language are: program development is faster, program maintenance is easier and programs are portable.

## Advantages of programming in assembly language are: accessibility to system hardware and space and time efficiency.

## The processor consists of two main units: data path unit and control unit.

## Given an address bus of 20 bits and data bus of 16 bits, the maximum memory size that can be interfaced with the CPU is 220=1 M bytes and the maximum number of bytes that can be read in a single read/write cycle is 16/8=2 bytes.

## Dynamic RAM is slower than static RAM but is denser and cheaper.

## Given a magnetic disk with Rotation speed = 8000 RPM (rotations per minute). Then, the average rotation latency, i.e. average time to locate a needed sector is:

## Rotations per second= 8000/60=133.33. Time for one rotation in ms= 1000/133.3=7.5 ms. Average rotation latency = 0.5 * 7.5 ms = 3.75 ms.

## The need for a memory hierarchy is due to widening speed gap between CPU and main memory.

## Cache memory is faster than random access memory (RAM) but slower than registers.

## Instruction Pointer (IP) or Program Counter (PC) is a register that holds the address of the next instruction to be fetched from memory.

## Given that a wafer can be diced into 1000 dies, out of which 200 dies are defective. Then, the yield is 800/1000=80%.

## The instruction set architecture is considered as an interface between software and hardware and consists of instruction set, programmer accessible registers and main memory.

## Operating system is a program that manages the resources of a computer for the benefit of the programs that run on that machine.

## Compiler is program that translates from high-level languages to assembly language.

## Very Large Scale Integration (VLSI) is a technology in which a single chip contains hundreds of thousands to millions of transistors.