Name: KEY									Id#

ICS 233, Term 141

Computer Architecture & Assembly Language

Quiz# 1

Date: Tuesday, Sep. 14, 2014

# Q1. Fill the blanks in the following questions:

## There is a one-to-one correspondence between assembly language and machine language.

## Two main advantages of programming in high-level language are: program development is faster and programs are portable,

## Two main advantages of programming in assembly language are: space and time efficiency and accessibility to system hardware.

## Given an address bus of 32 bits and a data bus of 64 bits, the maximum memory size that can be interfaced with the CPU is 232=4 Gbytes and the maximum number of bytes that can be read in a single read/write cycle is 64/8=8 bytes.

## Dynamic RAM is slower than static RAM but is denser and cheaper.

## The need for a memory hierarchy is due to widening speed gap between CPU and main memory and also due to performance/cost tradeoff.

## The instruction Pointer (IP) is a register that holds the address of the next instruction to be fetched from memory.

## The instruction set architecture (ISA) is considered as an interface between software and hardware and consists of the instruction set, programmer accessible registers and memory.

## Compiler is program that translates high-level languages to assembly language.

## Given a magnetic disk with the following properties:

- Rotation speed = 8000 RPM (rotations per minute)

- Average seek = 7 ms, Sector = 1024 bytes, Track = 250 sectors

The average time to access a block of 200 consecutive sectors is 16.75 ms.

Average access time =  Seek Time + Rotation Latency + Transfer Time

Rotations per second = 8000/60 =133.33 RPS

Rotation time in milliseconds = 1000/133.33 = 7.5 ms

Rotation Latency = 7.5/2 = 3.75 ms

Time to transfer 200 sectors = (200/250)* 7.5 = 6 ms

Average access time = 7 + 3.75 + 6 = 16.75 ms.

## Assuming 8-bit 2`s complement representation, the smallest (negative) number is 10000000 in binary and -128 in decimal and the largest (positive) number is 01111111 in binary and +127 in decimal.

## Assuming 8-bit 2`s complement representation, the binary number 11011100 represents the decimal number -36.

2’s complement of 11011100 = 00100100 = +36

## Assuming 8-bit 2`s complement representation, the number F0 represents the decimal number -16.

2’s complement of F0= 10 = +16

## The binary number 11100101 represents character e, and uses an odd parity bit. Note that the ASCII code of character A is 41H and that of character a is 61H.

## Character is 110 0101 = 65H = ‘e’