Name:									Id#

ICS 233, Term 141

Computer Architecture & Assembly Language

Quiz# 2

Date: Sunday, Oct. 26, 2014

# Q1. Fill in the blank in each of the following questions:

## Assuming variable Array is defined as shown below:

Array: .byte 1, 2, 3, 4, 5, 6, 7, 8, 9, 10

The content of register $t0 after executing the following sequence of instructions is ______________.

la $t0, Array

lw $t0, 4($t0)

## Assume that the instruction j NEXT is at address 0x00400030 in the text segment, and the label NEXT is at address 0x004000a8. Then, the address stored in the assembled instruction for the label NEXT is ________________________________.

## Assume that the instruction bne $t0, $t1, NEXT is at address 0x00400030 in the text segment, and the label NEXT is at address 0x004000a8. Then, the address stored in the assembled instruction for the label NEXT is ____________________________________________________________________.

## Assuming that $a0 contains an Alphabetic character, the instruction __________________________ will guarantee that the character in $a0 is always an upper case character. Note that the ASCII code of character ‘A’ is 0x41 while that of character ‘a’ is 0x61.

# Q2. Using only basic MIPS instructions, write the shortest sequence of instructions to implement each of the following pseudo instructions:

## xori $t0, 0x12345678  #$t0 is xored with the 32-bit value  0x12345678

## ble $t0, $t1, Next   # branch to Next if $t0 is less than or equal to $t1

## bgt $t0, 100, Next   # branch to Next if $t0 is greater than 100

## neg $t0, $t1   #$t0 is loaded with the negative value of $t1

## rol $t0, $t0, 12   #$t0 is rotated to the left by 12 bits and stored in $t0

# Q3. Answer the following questions. Show how you obtained your answer:

## Determine the content of register $s1 after executing the following code:

ori $s1, $zero, 12

sll $t0, $s1, 3

sub $t0, $t0, $s1

sra $t1, $s1, 2

add $s1, $t0, $t1

## Determine the content of register $t2 after executing the following code:

li $s1, 0x5A

and $t2, $zero, $t2

Next:

andi $t1, $s1, 1

add $t2, $t2, $t1

srl  $s1, $s1, 1

bne $s1, $0, Next

## Given that TABLE is defined as: TABLE: .word 7, 10, -4, 5, 20, 13

## Determine the content of registers $t2 after executing the following code:

la         $t0, TABLE

li	$t1, 6

lw	$t2, ($t0)

loop:	addi	$t0, $t0, 4

lw	$t3, ($t0)

bge	$t3, $t2, skip

move	$t2, $t3

skip:	addi	$t1, $t1, -1

bne	$t1, $0, loop