Name:									Id#

COE 301/ICS 233, Term 151

Computer Architecture & Assembly Language

Quiz# 2

Date: Tuesday, Oct. 6, 2015

# Q1. Fill the blanks in the following questions:

## Assume that the instruction j NEXT is at address 0x00400010 in the text segment, and the label NEXT is at address 0x00400fec. Then, the address stored in the assembled instruction for the label NEXT  is ___________________________.

## Assume that the instruction bne $t0, $t1, NEXT is at address 0x00400010 in the text segment, and the label NEXT is at address 0x00400fec. Then, the address stored in the assembled instruction for the label NEXT is __________________.

## The pseudo instruction ori $t0, 0x12345678 is implemented by the following minimum MIPS instructions:

## After executing the instruction addu $t0, $s1, $s2, the following MIPS instruction can be used to store the carry out of addition in register $t1:

## To multiply the signed content of register $t0 by 62.5 without using multiplications and division instructions, we use the following MIPS instructions:

## The content of register $s1 after executing the following code is __________.

li $s0, 0x5a

li $s1, 0

Next:

andi $t0, $s0, 1

add $s1, $s1, $t0

srl  $s0, $s0, 1

bne $s0, $0, Next

## The code given below implements the conditional statement:

________________________________________________________________________________

slti $t3, $t0, 1

bne $t3, $zero,  Zero_index

li $t3, 100

slt $t3, $t3, $t1

beq $t3, $zero, End_if

Zero_index:

xor $t2, $t2, $t2

End_if: