Name: KEY									Id#

ICS 233, Term 072

Computer Architecture & Assembly Language

Quiz# 2

Date: Wednesday, March 5, 2008

# Q1. Consider an 8-bit register that has the binary number 10010110. Determine the decimal value of the number if it represents:

## An unsigned number.

128+16+4+2=150

## A signed number in sign-magnitude representation.

=-(16+4+2)=-22

## A signed number in 1’s complement representation.

1's complement of 10010110 = 01101001=(64+32+8+1)=+105

Thus, 10010110 represents -105

## A signed number in 2’s complement representation.

2's complement of 10010110 = 01101010=(64+32+8+2)=+106

Thus, 10010110 represents -106

# Q2. Perform the following arithmetic operations assuming that numbers are represented using 8-bit 2’s complement representation. Indicate in your answer when an overflow occurs.

## FF + FF

= FE

There is no overflow as we are adding two negative numbers and we got a negative number.

## FE – 80

# = FE + 2's comp. of 80 = FE + 80 = 7E

# There is overflow as we are adding two negative numbers and we got a positive.

# Q3. Fill the blanks in the following questions:

## Assuming unsigned number representation, (F1)16 represents the decimal number = 15x16+1=241.

## The decimal number 1020 is represented in binary as 1111111100.

## The binary number 01100011 represents character c, and uses an even parity bit. Note that the ASCII code of character A is 41H and that of character a is 61H.

## Assuming 4-bit 2`s complement representation, the smallest (negative) number is 1000 in binary and -8 in decimal and the largest (positive) number is 0111 in binary and +7 in decimal.