Name:									Id#

ICS 233, Term 063

Computer Architecture & Assembly Language

Quiz# 3

Date: Monday, August 6, 2007

# Using the refined signed multiplication hardware, show the signed multiplication of: Multiplicand=1101 by Multiplier=1101. The result of the multiplication should be an 8 bit signed number in HI and LO registers. Show the steps of your work by filling the table given below.

| Iteration | Multiplicand | Sign | Product = HI, LO |
| --- | --- | --- | --- |
| 0 |  |  |  |  |
| 1 |  |  |  |  |
| 2 |  |  |  |  |
| 3 |  |  |  |  |
| 4 |  |  |  |  |

# Using the refined unsigned division hardware, show the unsigned division of: Dividend=1111 by Divider=0110. The result of division should be stored in the Remainder and Quotient registers. Show the steps of your work by filling the table given below.

| Iteration | Remainder | Quotient | Divisor | Difference |
| --- | --- | --- | --- | --- |
| 0 |  |  |  |  |  |
| 1 |  |  |  |  |  |
| 2 |  |  |  |  |  |
| 3 |  |  |  |  |  |
| 4 |  |  |  |  |  |

# Show the IEEE 754 binary representation for: -13.53125 in single precision.

# Perform the following floating-point operation rounding the result to the nearest even, using guard, round and sticky bits.

## 0100 0010 0000 0000 0000 0000 0000 0000

## -  0011 1111 1000 0000 0000 0000 0001 0001