Name:									Id#

ICS 233, Term 141

Computer Architecture & Assembly Language

Quiz# 3

Date: Sunday, Nov. 2, 2014

# Q1. Fill in the blank in each of the following questions:

## Assuming variable Array is defined as shown below:

Array: .byte 1, -1, 2, -2, 3, -3, 4, -4

The content of register $t0 after executing the following sequence of instructions is ______________.

la $t0, Array

lh $t0, 2($t0)

## Assume that the instruction j NEXT is at address 0x00400094 in the text segment, and the label NEXT is at address 0x0040008C. Then, the address stored in the assembled instruction for the label NEXT is ________________________________.

## Assume that the instruction bne $t0, $t1, NEXT is at address 0x00400094 in the text segment, and the label NEXT is at address 0x0040008C. Then, the address stored in the assembled instruction for the label NEXT is ____________________________________________________________________.

## Assuming that $a0 contains an Alphabetic character, the single instruction __________________________ will convert an upper case character in $a0 to a lower case, and a lower case to an upper case. Note that the ASCII code of character ‘A’ is 0x41 while that of character ‘a’ is 0x61.

# Q2. Write separate MIPS assembly code fragments to do the following minimizing the number of executed instructions (Pseudo instructions can be used):

## Count the number of 0’s in register $a0 and store the result in $v0. Assume that the number of 0’s is larger than the number of 1’s in register $a0. Assume that the content of register $a0 needs to be preserved.

## Implement the following high-level statement assuming that the registers contain signed numbers:

## if ( ($sl > 10  ||  $s1<=100) && $s1 > $s2) {$s3 = 1;}