Name:									Id#

ICS 233, Term 142

Computer Architecture & Assembly Language

Quiz# 3

Date: Tuesday, March 17, 2015

## Q1. Assuming that functions F and G receive two arguments in $a0 and $a1 and return their results in $v0, implement the function F given below saving needed registers on the stack. Save changed registers according to the assumed programming convention.

int F(int a, int b) {

return  a+G(b, G(a, b));

}

# .

# Q2. Given that Multiplicand=1010 and Multiplier=0111, using the refined signed multiplication hardware, show the signed multiplication of Multiplicand by Multiplier. The result of the multiplication should be an 8 bit signed number in HI and LO registers. Show the steps of your work.

| Iteration | Multiplicand | Sign | Product = HI,LO |
| --- | --- | --- | --- |
| 0 |  |  |  |  |
| 1 |  |  |  |  |
| 2 |  |  |  |  |
| 3 |  |  |  |  |
| 4 |  |  |  |  |

Q3. Given that Dividend=1011 and Divisor=0011, Using the refined unsigned division hardware, show the unsigned division of Dividend by Divisor. The result of division should be stored in the Remainder and Quotient registers. Show the steps of your work.

| Iteration | Remainder (HI) | Quotient (LO) | Divisor | Difference |
| --- | --- | --- | --- | --- |
| 0 |  |  |  |  |  |
| 1 |  |  |  |  |  |
| 2 |  |  |  |  |  |
| 3 |  |  |  |  |  |
| 4 |  |  |  |  |  |