Name: KEY									Id#

ICS 233, Term 063

Computer Architecture & Assembly Language

Quiz# 3

Date: Monday, August 6, 2007

# Using the refined signed multiplication hardware, show the signed multiplication of: Multiplicand=1101 by Multiplier=1101. The result of the multiplication should be an 8 bit signed number in HI and LO registers. Show the steps of your work by filling the table given below.

| Iteration | Multiplicand | Sign | Product = HI, LO |
| --- | --- | --- | --- |
| 0 | Initialize (LO = Multiplier) | 1101 |  | 0000 1101 |
| 1 | LO[0] = 1 => ADD |  | 1 | 1101 1101 |
|  | Shift Product = (HI, LO) right 1 bit | 1101 |  | 1110 1110 |
| 2 | LO[0] = 0 => Do Nothing |  | 1 | 1110 1110 |
|  | Shift Product = (HI, LO) right 1 bit | 1101 |  | 1111 0111 |
| 3 | LO[0] = 1 => ADD |  | 1 | 1100 0111 |
|  | Shift Product = (HI, LO) right 1 bit | 1101 |  | 1110 0011 |
| 4 | LO[0] = 1 => SUB (ADD 2's comp.) | 0011 | 0 | 0001 0011 |
|  | Shift Product = (HI, LO) right 1 bit |  |  | 0000 1001 |

# Using the refined unsigned division hardware, show the unsigned division of: Dividend=1111 by Divider=0110. The result of division should be stored in the Remainder and Quotient registers. Show the steps of your work by filling the table given below.

| Iteration | Remainder | Quotient | Divisor | Difference |
| --- | --- | --- | --- | --- |
| 0 | Initialize | 0000 | 1111 | 0110 |  |
| 1 | 1: SLL, Difference | 0001 | 1110 | 0110 | 1011 |
|  | 2: Diff < 0 => Do Nothing |  |  |  |  |
| 2 | 1: SLL, Difference | 0011 | 1100 | 0110 | 1101 |
|  | 2: Diff < 0 => Do Nothing |  |  |  |  |
| 3 | 1: SLL, Difference | 0111 | 1000 | 0110 | 0001 |
|  | 2: Rem = Diff, set lsb Quotient | 0001 | 1001 |  |  |
| 4 | 1: SLL, Difference | 0011 | 0010 | 0110 | 1101 |
|  | 2: Diff < 0 => Do Nothing |  |  |  |  |

# Show the IEEE 754 binary representation for: -13.53125 in single precision.

13.53215 =( 1101.10001)2 = 1.10110001 x 23

Exponent= 3+127=130

Thus, the representation of the number in single precision is:

1100 0001 0101 1000 1000 0000 0000 0000

# Perform the following floating-point operation rounding the result to the nearest even., using guard, round and sticky bits.

## 0100 0010 0000 0000 0000 0000 0000 0000

## -  0011 1111 1000 0000 0000 0000 0001 0001

1.000 0000 0000 0000 0000 0000 000		x 25

-	1.000 0000 0000 0000 0001 0001 000		x 20

=	1.000 0000 0000 0000 0000 0000 000		x 25

-	0.000 0100 0000 0000 0000 0000 101  	x 25

=   01.000 0000 0000 0000 0000 0000 000		x 25

+   11.111 1011 1111 1111 1111 1111 011  	x 25

## =       00.111 1011 1111 1111 1111 1111 011	 	x 25

## =       +0.111 1011 1111 1111 1111 1111 011	 	x 25

## =       +1.111 0111 1111 1111 1111 1110 111 		x 24

## Then, we round to the nearest even and we add a 1. Thus, the result will be:

+1.111 0111 1111 1111 1111 1111 	 	x 24