Name: KEY									Id#

ICS 233, Term 072

Computer Architecture & Assembly Language

Quiz# 3

Date: Saturday, March 15, 2008

# Fill the blanks in the following questions:

## The MIPS processor is a Reduced Instruction Set (RISC) computer.

## The MIPS processor has 32 general purpose registers.

## The MIPS instructions are 32 bit wide, and there are 3 instructions formats called: Register (R-Format), Immediate (I-Format), Jump (J-Format).

## The difference between add and addu instructions is that overflow causes an arithmetic exception for add instruction but not for addu instruction.

## The difference between sll and sllv instructions is the shift amount is constant for sll instruction but variable and stored in a register for sllv.

# Write the minimum required MIPS instructions to implement each of the following pseudo instructions:

## li $s1, 0x12345678

## lui $s1, 0x1234

## ori $s1, $s1, 0x5678

## move $s1, $s2

## or $s1, $zero, $s2

## bgt $s1, $s2, Next

## slt $at, $s2, $s1

## bne $at, $zero, Next

## bge $s1, $s2, Next

## slt $at, $s1, $s2

## beq $at, $zero, Next

## rol $s1, $s1, 4

## Note that this instruction should rotate the content of register $s1 by 4 bits to the left. For example, if $s1=0x12345678, after executing the instruction the content of $s1 becomes $s1=0x23456781.

## srl $at, $s1, 28

## sll $s1, $s1, 4

## or $s1, $s1, $at

# Write the minimum required MIPS instructions to implement each of the following. Pseudo instruction can be used.

## Multiply the content of register $s1 by 30 without using multiplication instructions.

## sll $t1, $s1, 5		# $t1=32*$s1

## sll $s1, $s1, 1		# $s1=2*$s1

subu $s1, $t1, $s1		# $s1=2*$s1

## if (   ($s1 > 0) && ( ($s2 < 100) || ($s2 > $s3) )    )  {$s4++;}

## ble $s1, $zero, EndIf

## li $t1, 100

## blt $s2, $t1, Skip

## ble $s2, $s3, Endif

## Skip:	      addiu $s4, $s4, 1

EndIf: