Name: KEY									Id#

ICS 233, Term 081

Computer Architecture & Assembly Language

Quiz# 3

Date: Wednesday, Nov. 26, 2008

# Consider the definitions given in the data segment below. Determine what is printed by each of the following sequence of MIPS instructions:

.data

Msg1: .ascii "Welcome to "

Msg2: .ascii "ICS "

X:       .byte 0x32, 0x33, 0x33, 0

## la $a0, Msg1

## li $v0, 4

## syscall

Welcome to ICS 233

## la $a0, X

## lb $a0, ($a0)

## li $v0, 1

## syscall

50

## la $a0, X+1

## lb $a0, ($a0)

## li $v0, 11

## syscall

3

# Determine the output produced by the following program. What functionality is the code implementing?

## 1.	 li 	 $a0, 21

## 2. 	 li	 $a1, 14

## 3. 	jal	 myfunction

## 4. 	addu 	 $a0, $v0, $zero

## 5. 	li 	 $v0, 1

## 6. 	syscall

## 7. 	j end

## myfunction:

## 8.	bnez      $a1, else

## 9.	addu     $v0, $zero, $a0

## 10.	jr	 $ra

## else:

## 11.	addiu	 $sp, $sp, -4

## 12.	sw	 $ra, ($sp)

## 13.	addu     $t0, $zero, $a0

## 14.	addu     $a0, $zero, $a1

## 15.	remu     $a1, $t0, $a1	    # $a1= $t0 % $a1 (i.e. remainder)

## 16.	jal	myfunction

## 17.	lw	$ra, ($sp)

## 18.	addi	$sp, $sp, 4

## 19.	jr	$ra

## end:

## The program will display 7, which is the greatest common divisor of the two numbers passed to the procedure.