Name: KEY									Id#

ICS 233, Term 142

Computer Architecture & Assembly Language

Quiz# 3

Date: Tuesday, March 17, 2015

## Q1. Assuming that functions F and G receive two arguments in $a0 and $a1 and return their results in $v0, implement the function F given below saving needed registers on the stack. Save changed registers according to the assumed programming convention.

int F(int a, int b) {

return  a+G(b, G(a, b));

}

F:	addiu	$sp, $sp, -12	# frame = 12 bytes

sw	$ra, 0($sp)	# save $ra

sw	$a0, 4($sp)	# save argument a

sw	$a1, 8($sp)	# save argument b

jal	G		# call g(a,b)

lw	$a0, 8($sp)	# $a0 = b

move	$a1, $v0	# $a1 = g(a,b)

jal	G		# call g(b, g(a,b))

lw	$a0, 4($sp)	# $a0 = a

addu	$v0, $a0, $v0	# $v0 = a+G(b, G(a, b))

lw	$ra, 0($sp)	# restore $ra

addiu	$sp, $sp, 12	# free stack frame

jr	$ra		# return to caller

# Q2. Given that Multiplicand=1010 and Multiplier=0111, using the refined signed multiplication hardware, show the signed multiplication of Multiplicand by Multiplier. The result of the multiplication should be an 8 bit signed number in HI and LO registers. Show the steps of your work.

| Iteration | Multiplicand | Sign | Product = HI,LO |
| --- | --- | --- | --- |
| 0 | Initialize (LO = Multiplier) | 1010 |  | 0000 0111 |
| 1 | LO[0] = 1 => ADD |  | 1 | 1010 0111 |
|  | Shift Product = (HI, LO) right 1 bit | 1010 |  | 1101 0011 |
| 2 | LO[0] = 1 => ADD |  | 1 | 0111 0011 |
|  | Shift Product = (HI, LO) right 1 bit | 1010 |  | 1011 1001 |
| 3 | LO[0] = 1 => ADD |  | 1 | 0101 1001 |
|  | Shift Product = (HI, LO) right 1 bit | 1010 |  | 1010 1100 |
| 4 | LO[0] = 0 => Do nothing |  | 1 | 1010 1100 |
|  | Shift Product = (HI, LO) right 1 bit |  |  | 1101 0110 |

Q3. Given that Dividend=1011 and Divisor=0011, Using the refined unsigned division hardware, show the unsigned division of Dividend by Divisor. The result of division should be stored in the Remainder and Quotient registers. Show the steps of your work.

| Iteration | Remainder (HI) | Quotient (LO) | Divisor | Difference |
| --- | --- | --- | --- | --- |
| 0 | Initialize | 0000 | 1011 | 0011 |  |
| 1 | 1: SLL, Difference | 0001 | 0110 | 0011 | 1110 |
|  | 2: Diff < 0 => Do Nothing |  |  |  |  |
| 2 | 1: SLL, Difference | 0010 | 1100 | 0011 | 1111 |
|  | 2: Diff < 0 => Do Nothing |  |  |  |  |
| 3 | 1: SLL, Difference | 0101 | 1000 | 0011 | 0010 |
|  | 2: Rem = Diff, set lsb Quotient | 0010 | 1001 |  |  |
| 4 | 1: SLL, Difference | 0101 | 0010 | 0011 | 0010 |
|  | 2: Rem = Diff, set lsb Quotient | 0010 | 0011 |  |  |