Name: KEY									Id#

ICS 233, Term 141

Computer Architecture & Assembly Language

Quiz# 4

Date: Tuesday, Nov. 18, 2014

# Q1. Determine the content of register $v0 after executing the following code:

li $a0, 0x12340000

jal MyProc

MyProc:

or $v0, $0 ,$0

ori $t0, $0, 8

loop:

rol $a0, $a0, 4

andi $t1, $a0, 0xf

add $v0, $v0, $t1

addiu $t0, $t0, -1

bne $t0, $0, loop

jr $ra

# The procedure adds the number of hexadecimal digits and stores the result in register $v0. Thus $v0=1+2+3+4=0xA.

# Q2. Assuming that functions F and G receive two integer arguments in $a0 and $a1 and return their results in $v0, implement the function F given below saving needed registers on the stack. Save changed registers according to the assumed programming convention:

int F(int a, int b) {

return  G(2a,b)+G(a,2b);

}

F:	addiu	$sp, $sp, -16	# frame = 16 bytes

sw	$ra, 0($sp)	# save $ra

sw	$a0, 4($sp)	# save argument a

sw	$a1, 8($sp)	# save argument b

shl	$a0, 1		# $a0 = 2*$a0

jal	G		# call G(2a,b)

sw	$v0, 12($sp)	# save result of  call G(2a,b)

lw	$a0, 4($sp)	# $a0 = a

lw	$a1, 8($sp)	# $a0 = b

shl 	$a1, 1		#$a1 = 2*$a1

jal	G		# call G(a,2b)

lw	$v1, 12($sp)	# restore result of  call G(2a,b)

addu	$v0, $v0, $v1	# $v0 = G(2a,b)+G(a,2b)

lw	$ra, 0($sp)	# restore $ra

addiu	$sp, $sp, 16	# free stack frame

jr	$ra