Name:									Id#

ICS 233, Term 072

Computer Architecture & Assembly Language

Quiz# 5

Date: Monday, April 21, 2008

# Given that Multiplicand=1110 and Multiplier=1011. Using the refined signed multiplication hardware, show the signed multiplication of Multiplicand by Multiplier. The result of the multiplication should be an 8 bit signed number in HI and LO registers. Show the steps of your work by filling the given table.

# Given that Dividend=1110 and Divisor=0110. Using the refined unsigned division hardware, show the unsigned division of Dividend by Divisor. The result of division should be stored in the Remainder and Quotient registers. Show the steps of your work by filling the given table.