Name:									Id#

ICS 233, Term 141

Computer Architecture & Assembly Language

Quiz# 6

Date: Monday, Dec. 22, 2014

# Q1. Consider the single-cycle datapath and control given below along with ALU and Next PC blocks design for the MIPS processor implementing a subset of the instruction set:

## Show the control signals generated for the execution of the following instructions by filling the table given below:

| Op | RegDst | RegWrite | ExtOp | ALUSrc | ALUOp | Beq | Bne | J | MemRead | MemWrite | MemtoReg |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| R-type |  |  |  |  |  |  |  |  |  |  |  |
| xori |  |  |  |  |  |  |  |  |  |  |  |
| lw |  |  |  |  |  |  |  |  |  |  |  |
| bne |  |  |  |  |  |  |  |  |  |  |  |

The format of these instructions is given below for your reference:

| Instruction | Meaning | Format |
| --- | --- | --- |
| sub rd, rs, rt | rd = rs - rt | Op6 = 0 | rs5 | rt5 | rd5 | 0 | 0x22 |
| xori rt, rs, imm16 | rt = rs ^ imm16 | 0x0e | rs5 | rt5 | imm16 |
| lw rt, imm16(rs) | rt = MEM[rs+imm16] | 0x23 | rs5 | rt5 | imm16 |
| bne rs, rt, label | branch if (rs != rt) | 0x05 | rs5 | rt5 | imm16 |

## We wish to add the following instructions to the MIPS single-cycle datapath. Add any necessary datapath modifications and control signals needed for the implementation of these instructions. Show only the modified and added components to the datapath.  Show the values of the control signals to control the execution of each instruction.

  - lui

| Instruction | Meaning | Format |
| --- | --- | --- |
| lui rt, imm16 | rt= imm16 << 16 | Op6 = 0xf | 0 | rt5 | imm16 |

  - sltiu

| Instruction | Meaning | Format |
| --- | --- | --- |
| sltiu rt, rs, imm16 | rt=(rs<imm?1:0) | Op6 = 0xb | rs5 | rt5 | imm16 |

  - bgtz

| Instruction | Meaning | Format |
| --- | --- | --- |
| bgtz rs, label | branch if (rs>0) | Op6 = 7 | rs5 | 0 | imm16 |

## Assume that the propagation delays for the major components used in the datapath are as follows:

    - Instruction and data memories: 150 ps

    - ALU and adders: 100 ps

    - Register file access (read or write): 60 ps

    - Main control: 20 ps

    - ALU control: 20 ps

Ignore the delays in the multiplexers, PC access, extension logic, and wires. What is the cycle time for the single-cycle datapath given above?