Name: KEY									Id#

ICS 233, Term 072

Computer Architecture & Assembly Language

Quiz# 7

Date: Saturday, May 10, 2008

# Consider two different implementations, M1 and M2, of the same instruction set. There are three classes of instructions (A, B, and C) in the instruction set. M1 has a clock rate of 6 GHz and M2 has a clock rate of 3 GHz. The CPI for each instruction class on M1 and M2 is given in the following table:

| Class | CPI on M1 | CPI on M2 | C1 Usage | C2 Usage |
| --- | --- | --- | --- | --- |
| A | 2 | 1 | 40% | 60% |
| B | 3 | 2 | 40% | 15% |
| C | 5 | 2 | 20% | 25% |

The above table also contains a summary of the usage of instruction classes generated by two different compilers: C1 and C2. Assume that each compiler generates the same number of instructions for a given program. Which computer and compiler combination give the best performance?

Execution time based on M1 and C1=ICx(0.8+1.2+1.0)x1/6x109=ICx3x1/6x109=ICx0.5ns.

Execution time based on M2 and C1=ICx(0.4+0.8+0.4)x1/3x109=ICx1.6x1/3x109=ICx0.53ns.

Execution time based on M1 and C2=ICx(1.2+0.45+1.25)x1/6x109=ICx2.9x1/6x109=ICx0.48ns.

Execution time based on M2 and C2=ICx(0.6+0.3+0.5)x1/3x109=ICx1.4x1/3x109=ICx0.47ns.

The best performance is achieved using compiler C2 and machine M2.

# A benchmark program runs for 100 seconds. We want to improve the speedup of the benchmark by a factor of 3. We enhance the floating-point hardware to make floating point instructions run 6 times faster. How much of the initial execution time would floating-point instructions have to account for to show an overall speedup of 3 on this benchmark?

Speedup = 1 / (f/s + (1-f))=> 3 = 1 / (f/6+(1-f)) => f/6 + 1-f = 1/3 => f + 6 – 6f = 6/3 =>

5f = 4 => f =4/5=0.8

Thus, floating-point instructions must account for 80% of the initial execution time, i.e. 80 seconds, to show an overall speedup of 3 on this benchmark.