COE 405, Term 162

Design & Modeling of Digital Systems

Assignment# 2 Solution

Due date: Saturday, March 11

# Consider the given FSM that has 6 states, two inputs X and Y, and one output Z, represented by the following state table:

| Present State | Next State | Output |
| --- | --- | --- |
|  | XY=00 | XY=01 | XY=10 | XY=11 | Z |
| S0 | S1 | S3 | S0 | S4 | 0 |
| S1 | S0 | S4 | S1 | S5 | 0 |
| S2 | S2 | S5 | S0 | S5 | 0 |
| S3 | S1 | S3 | S0 | S4 | 1 |
| S4 | S0 | S4 | S2 | S5 | 1 |
| S5 | S1 | S3 | S1 | S3 | 1 |

## Determine the equivalent states.

| S1 | (3,4), (4,5) |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| S2 | (1,2), (3,5), (4,5) | (0,2), (4,5), (0,1) |  |  |  |
| S3 |  |  |  |  |  |
| S4 |  |  |  | (0,1), (0,2), (4,5) |  |
| S5 |  |  |  | (0,1), (3,4) | (0,1), (3,4), (1,2), (3,5) |
|  | S0 | S1 | S2 | S3 | S4 |

## Equivalent states are: (S0, S1, S2), (S3, S4, S5).

## Thus, the machine can be reduced to two states: S0'=(S0, S1, S2), S1'=(S3, S4, S5).

## Reduce the state table into the minimum number of states and show the reduced state table.

## The reduced state table is:

| Present State | Next State | Output |
| --- | --- | --- |
|  | XY=00 | XY=01 | XY=10 | XY=11 | Z |
| S0' | S0' | S1' | S0' | S1' | 0 |
| S1' | S0' | S1' | S0' | S1' | 1 |

# Consider the given FSM that has 4 states, one input (X) and one output (Z), represented by the following state table:

| Present State | Next State, Z |
| --- | --- |
|  | X=0 | X=1 |
| S0 | S0, 1 | S2, 0 |
| S1 | S0, 0 | S2, 0 |
| S2 | S1, 0 | S3, 0 |
| S3 | S1, 0 | S3, 1 |

## Implement the FSM using the following state assignment: S0=00, S1=10, S2=01, S3=11.

## Implement the FSM using the following state assignment: S0=10, S1=01, S2=11, S3=00.

## Compare the area of the two resulting circuits.

The number of literals using the first state assignment is 6 while it is 14 using the second state assignment. We could also say that the first assignment uses an equivalent of 5 2-input primitive gates while the second state assignment uses 10 2-input primitive gates. Therefore, the first assignment produces a significantly lower area than the second assignment.

# It is required to design a sequential circuit using Mealy model that computes the equation Z=3*X-3, where X is an unsigned number that will be fed serially.  Assume that the circuit has an asynchronous Reset input that resets the machine to the reset state.

## Draw the state diagram for your sequential circuit. Make sure that your state machine is minimal and that it does not have any redundant state.

| Present State | Next State, Y |
| --- | --- |
|  | X=0 | X=1 |
| S0 (B=3) | S1, 1 | S3, 0 |
| S1 (B=2) | S2, 0 | S3, 1 |
| S2 (B=1) | S2, 1 | S4, 0 |
| S3 (B=0) | S3, 0 | S4, 1 |
| S4 (C=1) | S3, 1 | S5, 0 |
| S5 (C=2) | S4, 0 | S5, 1 |

## Derive minimized equations for the output Z and next state variables.

## Since we have 6 states, we need 3 FFs: F2, F1, and F0. We will use the following encoding: S0=000, S1=001, S2=010, S3=011, S4=100, and S5=101.

## Transition Table:

| Present State F2F1F0 | Next State, Y F2+F1+F0+ |
| --- | --- |
|  | X=0 | X=1 |
| 000 | 001, 1 | 011, 0 |
| 001 | 010, 0 | 011, 1 |
| 010 | 010, 1 | 100, 0 |
| 011 | 011, 0 | 100, 1 |
| 100 | 011, 1 | 101, 0 |
| 101 | 100, 0 | 101, 1 |

Y = (F0 ( X)'

F0+ = F1' F0' + F1' X + F1 F0 X' = F1' (F0' + X) + F1 F0 X' = F1 ( (F0' + X)

F1+ = F1 X' + F2' F1' F0 + F2' F1' X + F2 F0' X'

F2+ = F2 X + F2 F0 + F1 X

## Write a Verilog model for modeling your sequential circuit.

module Y3XM3 (output reg Z, input X, Reset, CLK);

parameter S0 = 3'b000;//B=3

parameter S1 = 3'b001;//B=2

parameter S2 = 3'b010;//B=1

parameter S3 = 3'b011;//B=0 & C=0

parameter S4 = 3'b100;//C=1

parameter S5 = 3'b101;//C=2

reg [2:0] CS, NS;

always @ (posedge CLK, posedge Reset)

begin

if (Reset)

CS <= S0;

else

CS <= NS;

end

always @ (X or CS)

begin

Z = 0;

case (CS)

S0:  if (X)  NS=S3;   else begin Z=1; NS=S1; end

S1: if (X) begin Z=1; NS=S3; end  else NS=S2;

S2:  if (X) NS=S4;  else begin Z=1; NS=S2; end

S3:  if (X) begin Z=1; NS=S4; end else NS=S3;

S4:  if (X) NS=S5;  else begin Z=1; NS=S3; end

S5:  if (X) begin Z=1; NS=S5; end else NS=S4;

default: begin Z='bx; NS='bx; end

endcase

end

endmodule

## Write a Verilog test bench to test the correctness of your design for the following input values: {X=1}, {X=3}, {X=5} and {X=4}.

module Y3XM3_TB() ;

reg CLK, Reset, X ;

wire Z ;

Y3XM3 M1 (Z, X, Reset, CLK);

initial begin

CLK = 0 ; forever #10 CLK = ~ CLK ;

end

initial begin

//Applying X=1

@(negedge CLK) Reset=1;

@(negedge CLK) Reset=0; X=1;

@(negedge CLK) X=0;

@(negedge CLK) X=0;

@(negedge CLK) X=0;

//Applying X=3

@(negedge CLK) Reset=1;

@(negedge CLK) Reset=0; X=1;

@(negedge CLK) X=1;

@(negedge CLK) X=0;

@(negedge CLK) X=0;

//Applying X=5

@(negedge CLK) Reset=1;

@(negedge CLK) Reset=0; X=1;

@(negedge CLK) X=0;

@(negedge CLK) X=1;

@(negedge CLK) X=0;

//Applying X=4

@(negedge CLK) Reset=1;

@(negedge CLK) Reset=0; X=0;

@(negedge CLK) X=0;

@(negedge CLK) X=1;

@(negedge CLK) X=0;

end

endmodule

The simulation waveform below demonstrates the correct functionality of the designed sequential circuit: