COE 405, Term 181

Design & Modeling of Digital Systems

Assignment# 3

Due date: Thursday, Oct. 25, 2018

# Consider the state table given below for a Mealy sequential circuit that computes the equation Z=3*X-4, where X is an unsigned number that will be fed serially.  Assume that the circuit has an asynchronous Reset input that resets the machine to the reset state.

| Present State | Next State | Output (Z) |
| --- | --- | --- |
|  | X=0 | X=1 | X=0 | X=1 |
| S0 | S1 | S2 | 0 | 1 |
| S1 | S2 | S3 | 0 | 1 |
| S2 | S2 | S4 | 1 | 0 |
| S3 | S3 | S4 | 0 | 1 |
| S4 | S3 | S5 | 1 | 0 |
| S5 | S4 | S5 | 0 | 1 |

## Write a behavioral Verilog model for modeling your sequential circuit.

## Write a Verilog test bench to test the correctness of your design for the following input values: {X=0}, {X=1}, {X=2} {X=3} and {X=4}.

## Implement the sequential circuit on FPGA and demonstrate its correct functionality for the following input values: {X=0} and {X=3}. Include a link for a video demonstrating correct functionality.

# It is required to model a seconds counter that counts from 0 to 59. Assume that the counter has a synchronous Reset input that resets the counter to zero.

## Write a Verilog model for generating a 1 HZ clock.

## Write a behavioral Verilog model for modeling an up/down module 60 counter that counts either up or down depending on a DIR input. When DIR=0, the counter will count up, otherwise it will count down.  The counter will reset to 0 synchronously if a Reset input is pressed.

## Implement the modulo-60 up/down counter on FPGA and demonstrate its correct functionality. Include a link for a video demonstrating correct functionality.