COE 405, Term 162

Design & Modeling of Digital Systems

Assignment# 5

Due date: Saturday, May 13

# Consider the following function:

## X=AC+BC+AD+BD+A’B’C’+A’B’D’+AEF+BEF+AE’F’+BE’F’+A’B’EF’+A’B’E’F

## Compute all double-cube divisors of X along with their bases and their weights. Show only double-cube divisors that have non-empty bases.

## Apply the fast extraction algorithm based on extracting double-cube divisors along with complements or single-cube divisors with two-literals. Show all steps of the algorithm. Determine the number of literals saved. Compare your solution with the result obtained by running the sis commands fx.

# Consider the logic network defined by the following expressions:

# e=a  b d

# f =c  d

# g = e + f

# h = a d

# i =a’ b’ d’

# j = h + i

# k= b d

# l =j + k

# x =g + l

# Inputs are {a, b, c, d} and output is {x}.  Assume that the delay of a gate is related to the number of its inputs. Also, assume that the input data-ready times are zero except for input d, which is equal to 2.

## Draw the logic network graph and compute the data ready times and slacks for all vertices in the network.

## Determine the maximum propagation delay and the topological critical path.

## Suggest an implementation of the function x to reduce the delay of the circuit. What is the maximum propagation delay after the modified implementation?

# It is required to design a circuit to compute the equation Y=A+2*B+3*C, where A, B, and C are N-bit inputs representing signed numbers in 2's complement representation. Assume that inputs are available only during the first cycle when a START input is asserted.  Assume that a DONE signal will be set when the result is ready and the result will remain held until the next Start operation.

## Show a schedule of the operations with minimum latency (i.e., clock cycles) assuming that the clock cycle is limited by the time for performing one addition operation. Store the output Y in a register.

## Show the Data Path design of your circuit indicating all the control signals and the used adder sizes.

## Show the ASMD diagram of your control unit.

## Write the necessary Verilog modules to module the data path unit, control unit and the overall circuit.

## Write a test bench to test the correct operation of your circuit. Include simulation snapshots.

## Implement your circuit on FPGA assuming N=2 bits. Include a link for a video snapshot to demonstrate correct functionality of your circuit.

This assignment can be solved based on a group of two students. The solution should be well organized. Submit a soft copy of your solution in a zip file including your Verilog models. Your solution should be submitted in a word file that contains the following items:

#### Your name and ID

#### Assignment number

#### Problem statement

#### Your solution

#### Include snapshots of simulation output to illustrate the correctness of your models.