April 4, 2013

COMPUTER ENGINEERING DEPARTMENT

COE 405

DESIGN & MODELING OF DIGITAL SYSTEMS

Midterm Exam

Second Semester  (122)

Time: 1:00-3:30 PM

OPEN BOOK EXAM

Student Name : __KEY_________________________________________

Student ID.     : ______________________________________________

| Question | Max Points | Score |
| --- | --- | --- |
| Q1 | 20 |  |
| Q2 | 15 |  |
| Q3 | 30 |  |
| Q4 | 25 |  |
| Q5 | 10 |  |
| Total | 100 |  |

Dr. Aiman El-Maleh

[20 Points]

# (Q1) It is required to design an iterative combinational circuit that receives an n-bit number X and computes the result Y=3*X. The design should be based on a one-bit cell (i.e. processing one bit Xi) that can be copied n times to construct the n-bit design. (Hint: 3*X = X+X+X. Note that the maximum carry from one cell to the next is 2.)

# Determine the inputs and outputs for a one-bit cell.

# Derive the truth table for a one-bit cell.

# Derive minimized sum-of-product equations for a one-bit cell.

# Show the block diagram for a 4-bit design.

[15 Points]

# (Q2) It is required to design a synchronous  sequential circuit that receives a serial input X and produces a serial output Z. The output Z will be 1 if the input has been alternating for at least 3 clock periods.  Assume the existence of an asynchrnous reset input to reset the machine to a reset state. Draw the state diagram of the circuit assuming a Mealy model. You are not required to derive the equations and the circuit. The following is an example of some input and output streams:

Example:

| Input | X | 1 0 1 0 1 0 1 1 0 1 0 1 0 0 1 0 |
| --- | --- | --- |
| Output | Z | 0 0 0 1 1 1 1 0 0 0 1 1 1 0 0 0 |

[30 Points]

# (Q3) The ASMD chart given below describes a state machine that counts 1’s in a word and terminates activity as soon as possible. The machine remains in its reset state, S_idle, until an external agent asserts start. This action asserts the output, load_temp, which will cause data to be loaded into register temp when the state makes a transition to S_counting at the next active edge of clk. The machine remains in S_counting while temp contains a 1. Two actions occur concurrently at each subsequent clock: (1) temp is shifted towards its LSB and (2) temp[0] is added to bit_count. When temp finally has a 1 in only the LSB, the machine’s state moves to S_waiting, where done is asserted. The state remains in S_waiting until start is reasserted. Assume that when the synchrnous reset input is asserted the machine is reset to the state  S_idle and bit_count and temp are initialized to 0.

## Show the design of the data-path unit.

## Show the design of the control unit using the following state assignment: S_idle=00, S_counting =01, and S_waiting=10.

- DataPath Unit:

- Control Unit:

| C.S. | Input | N.S. | Output |
| --- | --- | --- | --- |
|  | start | temp_gt_1 |  | done | busy | load_temp | shift_add | clear |
| S_idle | 0 | x | S_idle | 0 | 0 | 0 | 0 | 0 |
| S_idle | 1 | x | S_counting | 0 | 0 | 1 | 0 | 0 |
| S_counting | x | 1 | S_counting | 0 | 1 | 0 | 1 | 0 |
| S_counting | x | 0 | S_waiting | 0 | 1 | 0 | 1 | 0 |
| S_waiting | 1 | x | S_counting | 1 | 0 | 1 | 0 | 1 |
| S_waiting | 0 | x | S_waiting | 1 | 0 | 0 | 0 | 0 |

## Assuming the two flip flops F1 and F2 for storing the machine state and the state assignment: S_idle=00, S_counting =01, and S_waiting=10, the contrl signals will be as follows:

done  = F1 F0’

busy = F1’ F0

shift_add = F1’ F0

load_temp = F0’ start

clear  = F1 F0’ start

[25 Points]

(Q4)  A JK flip-flop with the following interface is given below:

- Write a JKFF module with behavioral model for a rising-edge triggered JK flip-flop.

module JKFF (output reg Q, output QB, input J, K, CLK);

assign QB = ~Q;

always @( posedge CLK)

case ({J,K})

2'b00: Q <= Q;

2'b01: Q <= 0;

2'b10: Q <= 1;

2'b11: Q <= ~Q;

endcase

endmodule

- Using the JK flip-flop modeled in (i) model the 1-bit modular binary counter given below.

module OneBitCount (output  Q, Cout, input Reset, Enable, CLK);

and (J, ~Reset, Enable);

or (K, Reset, Enable);

and (Cout, Enable, Q);

JKFF F (Q, , J, K, CLK);

endmodule

- Based on the 1-bit  modular binary counter modeled in (ii), build a 3-bit binary up counter as shown below. The counter does not count when the count enable is 0. Otherwise, it counts on the rising-edge of the clock.

module ThreeBitCount (output  Q2, Q1, Q0, Cout, input Reset, Enable, CLK);

OneBitCount F0 (Q0, Cout0, Reset, Enable, CLK);

OneBitCount F1 (Q1, Cout1, Reset, Cout0, CLK);

OneBitCount F2 (Q2, Cout, Reset, Cout1, CLK);

endmodule

- Write a test bench to test the 3-bit counter using the data given below. You need to generate the clock signal inside the test bench with a period of 10 and 50% duty cycle. The test bench should simulate the circuit for 300 delay units.

| Time | Action |
| --- | --- |
| 20 | Reset=1 |
| 35 | Reset=0 |
| 50 | Enable=1 |
| 90 | Enable=0 |
| 120 | Enable=1 |

module t_ThreeBitCount ();

wire Q2, Q1, Q0, Cout;

reg CLK, Reset, Enable;

ThreeBitCount C0 (Q2, Q1, Q0, Cout, Reset, Enable, CLK);

initial #300 $finish;

initial begin

CLK = 0;

forever #5 CLK = ~CLK;

end

initial fork

#20 Reset = 1;

#35 Reset = 0;

#50 Enable = 1;

#90 Enable = 0;

#120 Enable = 1;

join

endmodule

[10 Points]

(Q5)  It is required to model a generic n-bit Ripple Carry Adder (RCA).  A 4-bit RCA is shown below:

Model a behavioral  n-bit RCA using repetitive constructs.

module RCA #(parameter n=4)

(output reg [n-1:0] Sum, output Cout, input [n-1:0] A, B, input Cin);

reg [n-1:0] Carry;

integer i;

assign Cout = Carry[n-1];

always @(A, B, Cin) begin

Sum[0] = A[0] ^ B[0] ^ Cin;

Carry[0] = A[0] & B[0] | Cin & (A[0] ^ B[0]);

for (i=1; i < n ; i=i+1) begin

Sum[i] = A[i] ^ B[i] ^ Carry[i-1];

Carry[i] = A[i] & B[i] | Carry[i-1] & (A[i] ^ B[i]);

end

end

endmodule