COE 405, Term 152

Design & Modeling of Digital Systems

HW# 1

Due date: Thursday, Feb. 11

# Consider the two functions f=a ( b ( c and g=a b + a c + b c.

## Implement the function g using only 2x1 MUXs.

## Compute the function f(g based on orthonormal basis expansion.

# It is required to design a combinational circuit that computes the equation Y=3*X-1, where X is an n-bit signed 2's complement number.

## Design the circuit as a modular circuit where each module receives a single bit of the input, Xi.

## Derive the truth table of your 1-bit module in (i).

## Derive minimized two-level sum-of-product equations for your 1-bit module circuit.

## Verify the correctness of your design by modeling and simulating a circuit to compute the required equation assuming X is a 4-bit number using logicworks.

This assignment can be solved based on a group of two students. The solution should be well organized. Submit a soft copy of your solution in a zip file including your logicworks files. Your solution should be submitted in a word file that contains the following items:

#### Your name and ID

#### Assignment number

#### Problem statement

#### Your solution

#### Include snapshots of simulation output to illustrate the correctness of your solution.