COE 405, Term 152

Design & Modeling of Digital Systems

HW# 3

Due date: Tuesday, March 1

# It is required to design a circuit that receives an array of n unsigned 4-bit numbers along with a 4-bit target value and counts the number of data elements that are greater or equal to the target value. Assume that once the user presses Start he will also supply the number of elements in the array n (n≤15) through input1 and the target value through input2 in the same cycle. Assume that input2 will hold the target value until the circuit finishes its operation. In the next n consecutive cycles, the user will provide the n data elements through input1. Once the circuit finishes computation, it will assert a Done signal and will generate a 4-bit output indicating the count of the number of elements in the array ≥ target value. The Done signal and the result will remain valid unless the user resets the machine or asserts the Start signal.

## Develop an ASMD chart for the circuit.

## Show a block diagram for the datapath and control unit interface.

## Show the design of the data-path and control unit of the circuit.

## Implement the circuit using logicworks and verify its correct functionality by simulation.