COE 405, Term 131

Design & Modeling of Digital Systems

HW# 5

Due date: Sunday, Dec. 8

# Consider the logic network below with inputs {a, b, c, d, e, f, g, h} and output {X}:

# Assume that the delay of a gate is related to the number of its inputs i.e. the delay of a 2-input AND gate is 2.  Also, assume that the input data-ready times are zero for all inputs.

## Compute the data ready times and slacks for all vertices in the network.

## Determine the topological critical path(s).

## Suggest an implementation of the function X to reduce the delay of the circuit to the minimum possible and determine the maximum propagation delay in the optimized circuit. Has the area been affected?

# It is required to design a circuit to compute the equation Y=A+B+C+D+E+F using only two adders. Assume that the inputs will hold their values until the end of the operation. Also, assume that the inputs will be ready when a Start input is asserted and a Done signal will be set when the result is ready.

## Show a schedule with minimum latency (i.e., clock cycles) satisfying the area constraints.

## Show the DataPath design of your circuit.

## Show the ASMD diagram of your control unit.

## Model the DataPath and Control units in Verilog and verify the correctness of your model.