Name:									Id#

COE 405, Term 031

Design & Modeling of Digital Systems

Quiz# 1

Date: Sunday, October 12, 2003

Q.1. It is required to model a 4-bit comparator that compares two 4-bit numbers A=A3A2A1A0 and B=B3B2B1B0, and produces two outputs GT and LT. If A>B, then the output signal GT is set to 1 and LT is set to 0. If A<B, then the output signal LT is set to 1, and GT is set to 0. Otherwise both signals will be set to 0, which indicates that the two numbers are equal (i.e. A=B). The 4-bit comparator circuit can be designed in a modular way as shown below:

The equations for the 1-bit magnitude comparator can be found to be:

## Describe an Entity COMP for a 1-bit magnitude comparator.

## Model an Architecture Conc for this 1-bit COMP using concurrent statements.

## Describe an Entity COMP4 for a 4-bit magnitude comparator.

## Model Architecture Struct for the 4-bit magnitude comparator (COMP4) using instantiations of the Entity COMP.

# Text boxes

LT0

GT0

LT1

GT1

LT

GT

B0

A0

LT1

GT1

LT2

GT2

LT2

GT2

LT3

GT3

LT3

GT3

LT4

GT4

0

0

B1

A1

B2

A2

B3

A3