Name:									Id#

COE 405, Term 181

Design & Modeling of Digital Systems

Quiz# 1 Solution

Date: Thursday, Sep. 20, 2018

# Area and testability are two important design criteria that are targeted during design. Explain the importance of minimizing area and having a design testable.

Optimizing area results in lowering the manufacturing cost, increases the manufacturing yields and reduces the packaging cost.

It is important to have a design testable so that manufacturing defects can be detected as early as possible before putting a chip in a system that is sent to the customer. The cost increases by a factor of 10x if a defective part goes from one level to the next without being detected.

# Performance and power are two important design criteria that are targeted during design. Explain how performance and power of a design are optimized.

Performance is optimized by reducing the critical path in combinational circuits and hence reducing the cycle time.

Power is optimized by reducing the switching activity in a design. It can be also reduced by using a lower voltage and lower clock frequency.

# Give two examples of semicustom design approaches.

Examples of semicustom design approaches include

  - Gate Arrays

    - Mask Programmable (MPGAs)

    - Field Programmable (FPGAs))

  - Standard Cells

  - Silicon Compilers & Parametrizable Modules (adder, multiplier, memories)

# Consider the function and the set of implementations given below. Assume that the area and delay of a gate are directly related to the number of its inputs. Using only 2-input and 3-input AND gates:

# Design a circuit to implement the function F with the minimum area. Report the area and delay of your suggested circuit.

Area=6, Delay=6

# Design a circuit to implement the function F with the minimum delay. Report the area and delay of your suggested circuit.

Area=7, Delay=5

# Consider the function:

# Compute the expansion of using the Orthonormal Basis {(1=, (2=, (3=, (4=}.

F = A'B' [0] + A'B [C(D] + AB' [C(D] + AB[0]

# Compute the functionutilizing the orthonormal based expansion of the function.

F' = A'B' [1] + A'B [C(D]' + AB' [C(D]' + AB[1]

= (A(B)' + (C(D)'(A(B)= (A(B)' + (C(D)'

# Implement the function F using minimal number of  2x1 MUXs and inverters.

F = A' [ B' [0] + B [C(D] ] + A [B' [C(D] + B[0] ]

# Suppose that the function F is part of a circuit whose output is Y as shown below. Simplify the equation of F to minimum area.

We simply the function using A B as a don't care condition.

F = B C' D + B C D' + A C' D + A C D' = (A+B)(C(D)